3GPP TSG-RAN WG3 Meeting #107-e	R3-201127

E-meeting, 24 February – 6 March, 2020

Agenda item:	10.2.1.3

Source:	ZTE

Title:	Summary for SN_change_failure

Document for:	Discussion

# Introduction

In TS 37.816，SN change failure in case of EN-DC and MR-DC is identified and need to be solved in NR_SON_MDT WI stage.

TR 37.816 RAN3 has studied the mobility optimization function and has converged to the solution principles and description outlined above. RAN3 has concluded its study on mobility optimization and determined that the mobility optimization feature can be moved to normative phase. The details of the solution parts involving UE behaviour remain pending to RAN2 analysis. The SN change failure optimization in case of EN-DC and MR-DC is concluded to be specified in the normative phase of this function.

In order to solve the issue ,an offline discussion list below is reserved for this object.

CB: # 23_Email023-SN_change_failure

-  Introduce a new RLF indication like message, HO report like message, EN-DC forwarded HO report message? (Nok), (ZTE)

- 1 vs. 2 procedures? (ZTE), (SS)

- UE records failure info and sends to the network (liaise RAN2?), then MN receives and forwards to SN who makes final analysis? (CATT)

- St2 needed? (ZTE)

- split work

- revise/merge if needed; check details

(ZTE)

Summary of offline disc

The email discussion would be organized as two phases:

Phase 1: Collecting company views on related questions, before Feb. 26, midnight CET

Phase 2: Work split and provide draft CR for Rel-16 , Feb.28, 6pm CET

# Discussion

The email discussion aiming to collect views from companies in following four issues:

Issue 1 : Approach selection

Based on input from contributions,three approaches are identified as approach 1,2,3.

Approach 1[1][2][4][6]: MN performs provides MRO root cause and forwards measurements to SN in similar “HO REPORT” message

As shown in section 5.1, take figure 2 in Annex of [1] as example to show general signalling procedure of Approach 1.

MN is coordinating the SN changes, stays connected with the UE in SN Change failure situations and is receiving the SCG Failure Information message which includes available measurements up to the point in time the SCG failure was detected by the UE. This may enable the MN to perform MRO root cause analysis after SN change failures on behalf of the SN node that initiated the SN change. The MN informs the SN about the MRO root cause  using e.g. the message Handover Report. The message also contains the measurement results received from the UE that may also be useful for optimizing the parameters for SN change at the SN.[1]

Support companies: Nokia, Samsung, ZTE

Approach 2[1][2][4][6]: SN performs MRO root cause (Measurements from MN)

As shown in section 5.2, take figure 5 in Annex of [1] as example to show general signalling procedure of Approach 2.

The MN sends a failure indication message to the SN containing the measurements received with the SCG Failure Information message. The SN performs root cause analysis and if it recognizes that a source SN was the originator of the problem then the SN sends a Handover Report message hinting to the analysed root cause and including the received measurements. The S-SN performs root cause analysis and may optimize the parameters.[1]

Supported companies: Nokia, CATT

Approach 3[1]：Approach 1+ Approach 2

Supported companies: Nokia

Comparison table of three approaches :

|  | Approach 1 | Approach 2 | Approach 3 |
| --- | --- | --- | --- |
| Signalling impact[1][2][4][6] | XnAP/X2AP SN_FAILURE_Report(MN->SN) | XnAP/ X2AP 1: SN change failure indication (MN->SN) 2: HANDOVER report(SN- SN) 3: Forward Handover report (MN->SN, SN->MN) | 1+2 |
| Signalling overhead[4] | No | Compare to approach 1 | 1+2 |
| no Xn interface between source SN and target SN[4] | No issue | Need reroute | 1+2 |
| Who trigger SN change[4] | No issue | Need more information | 1+2 |
| More memory and processing for MN recording UE-related information[2][4] | Impact MN node | No issue | 1+2 |
| Need RAN2 impact | NA | Wait for RAN2’s decision ,e.g enhance on SCGfailureReport | 1+2 |

All three approaches can solve the SN change failure issue, identify the root cause of the failure and modify the mobile setting parameters of the SN where the error occurred.But considering that RAN3 107e is the last meeting of NR_SON_MDT in Rel-16, and this meeting is arranged as an electronic meeting which introduce inconvenient for coordinate among different Working groups. Cooperate with RAN2 needs interact multiple times and impact the specification of TS 38.331, which bring challenge as urgent in time. Therefore, it is recommended to select a simple solution first.From the current analysis, approach 1 is the in favor in aspect of signalling design and has less impact on the protocol. It is recommended that approach 1 be used as a baseline for SN change failure in Rel-16.

The following questions is aiming to achieve conclusion on this topic based on companies response.

Question 1: Do you think approach 1 is selected as baseline for Rel-16 SN change failure?

| Company | Yes/No | Remark |
| --- | --- | --- |
| ZTE | YES |  |
| Ericsson | NO | One observation is that the SCG Failure Information is already signalled as part of the CG-ConfigInfo from MN to SN, see TS38.331§11.2.2. Hence there is no need for any special message to convey the SCGConfigInfo IE to the SN. Secondly, in an SN triggered SN change, the only node that can perform a meaningful root cause analysis is the SN, as it was the SN that applied policies for SN selection and triggered the SN change. Finally, RAN2 has postponed the discussion on MRO applied to SN change failure to the next meeting. It is suggested that RAN3 also postpones discussions on MRO for SN change failure cases to the next meeting, as we will be anyhow be pending from RAN2’s agreements. |
| CATT |  | Also prefer to postpone and discuss based the agreement made in RAN2 |
| Samsung | Yes | For handover case, we have agreed to support legacy UEs. The same principle can be used for handover and SN change. For legacy UE, the detection mechanism should depend on the UE context in the network side if availble. The MN may have the overall information. Therefore, the MN can make proper detection. |
| HW | YES | Different from MRO scheme for HO case, for DC, the connection between UE and MN is always available. The MN knows the whole SN change mobility and can decide the final target SN. Thus, the MN can give the root cause analysis based on the stored timer and the received SCGfailureinformation. |
| Qualcomm | No | Agree with Ericsson. Let’s wait for RAN2 progress. |

Conclusion:

Issue 2 : Based on the context in the network side or based on enhanced SCGInformationIndiation message from the UE

Based on analysis in issue 1, MN node perform SN change failure root cause based on

A: save the context of old SN node (which is an new implementation request for MN)[4]

Or either

B: by enhanced SCGInformationIndiation [2][3][4]

After the MN node receives SCGFailureInformation message, it could further forward it to SN node and let SN make the final analysis. The parameters introduced in the UE report could be defined as below: previousPSCellId: the source PSCell of the last SN change; failedPSCellId: the PSCell in which RLF is detected or the target PSCell of the failed SN change; timeConnFailure :the time elapsed since the last SN change initialization until connection failure; connectionFailureType: radio link failure or SN change failure.

While RAN2 seems to discussion this part at same time, then it is better to wait for RAN2’s input.

Question 2: Do you think behavior of MN when conduct SN Change failure root cause analysis based on UE context saving or enhanced SCGInformationIndiation is basing RAN2 ‘s progress?

| Company | Yes/No | Remark |
| --- | --- | --- |
| ZTE | Yes |  |
| Samsung | Not exactly | MN can perform root cause analyse based on the saved UE context. This has no relation with RAN2. If RAN2 agreed to enhance SCGFailureIndication, the MN don’t need to save the old SN information after successful SN change. Approach 2 for Issue 1 is rely on the enhanced UE report. |
| HW | A | The MN can know the cell info of the S-SN, T-SN and final-SN based on the stored UE context. These information is not needed to be provided from UE. Besides, the timeConnFailure in RLF report can be used to identify whether the RLF is caused by too early HO or too late HO. For DC case, it is not needed, because it is always too early SN change. |

Conclusion:

Issue 3: Ruse or new message for similar “HO REPORT” from MN to SN

There are two on the table:

A:reuse HO report message

Support company : ZTE, Samsung

B: new message

Support company : Samsung

Conclusion:

Issue 4: Mobility Information in S-NODE ADDITION REQUEST ACKNOWLEDGE message and Handover Report like message[4]

Supported company : ZTE, Samsung

Not supported company:

Conclusion:

# Conclusions

Before the end of phase 1 discussion, we receive 6 companies response including Ericsson , CATT,Samsung ,Huawei and Qualcomm.

From the contributions and email feedback, at least the consensus is that there are three options to choose from.

Option 1: The MN perform root cause analysis of SN change failure and sends the the result to SN

Option 2: SN perform root cause analysis

Option 3: The MN first perform root cause analysis and provides the result to the SN as assistant information, while providing other assistant information such as SCGFailurereport, and the SN performs the final optimization.

For option 1, the MN may not obtain the pscell information of the old SN through the UE history information, and the MN may obtain such information by retaining the UE context. The storage capacity of this MN may need to be enhanced.That is the main weakness of this option.

The option 1 is apply for legacy UE(R16)

For option 2, the main weakness is not just to wait for the conclusion of RAN2, but to consider how to pass the failure report to the old SN when there is no interface between the SNs. Obviously, this has a greater impact on the protocol. And the solution is sub-optimal in case MN triggers the SN change.

The option 2 is not apply for legacy UE(R16)

For option 3, it has same performance efficient as option 1 and is more effective to solve the SN change failure triggered by SN. But this option also need RAN2 ‘s progress on enhancement of SCGFailurereport .

The option 3 is apply for legacy UE(R16)

During the email discussion, three companies express confirmation on select option 1 for Rel-16 (ZTE,Samsung, Huawei). While three companies (Ericsson, CATT, Qualcomm) propose to postpone the discussion and wait for RAN2’ progress.

After check ongoing RAN2 email discussion, in minutes of SON open issues of RAN2 and in [R2-2002025] , enhancement of SCGFailureReport with RLF is postponed to Rel-17.

Based on above discussions, we made following conclusion:

Conclusion :

Agreeable proposal 1: For MRO of SN change failure , three options were identified includes:

Option 1: The MN perform root cause analysis of SN change failure and sends the the result to SN

Option 2:  The SN perform root cause analysis

Option 3: The MN first perform root cause analysis and provides the result to the SN as assistant information, while providing other assistant information such as SCGFailurereport, and the SN performs the final optimization.

Agreeable proposal 2: The normative of MRO of SN change failure postpone to Rel-17.

# References

- R3-200074 Further discussion on MRO for SN change failure Nokia, Nokia Shanghai Bell

- R3-200441 Consideration on support of MRO for SN change in case of MR-DC CATT

- R3-200442 [draft]LS to RAN2 on MRO for SN change CATT

- R3-200572 (TP for SON BL CR for TS 38.423) Solution for SN change failure Samsung

- R3-200573 (TP for SON BL CR for TS 38.423) New procedure for SN change failure report  Samsung

- R3-200612  Detection solution for SN change failure ZTE

- R3-200613  (TP for [NR_SON_MDT] BL CR for TS 38.300) Detection solution for SN change failure ZTE

- R3-200614  (TP for [NR_SON_MDT] BL CR for TS 38.423) Detection solution for SN change failure ZTE

# Annex

## 5.1 Procedure example of Approach 1

Take figure 2 in Annex of [1] as example to show general signalling procedure of Approach 1.

In Approach 1, MN node performs SN change failure root cause analysis and provides report to SN which need to improve mobility parameter. In the report, SN failure report information may carried in the message.

Figure 2: MRO handling for the SN Change failure while a SN initiated SN change is ongoing in case root cause analysis is performed by the MN.

## 5.2 Procedure example of Approach 2

Take figure 5 in Annex of [1] as example to show general signalling procedure of Approach 2.

Figure 5: MRO handling for the SN Change failures due to too early SN change triggering or due to SN change triggering to a wrong cell in case root cause analysis is performed by the SN.