3GPP TSG-RAN WG3 Meeting #107-e	R3-20xxxx

Online, 24th February - 6th March 2020

Agenda Item:	10.2.3.1

Source: 	CMCC, Huawei

Title: 	TP to SON BLCR 38.300 on support of RACH optimization

Document for:	Approval

# Introduction

This paper provides a TP to 38.300 to support of RACH optimization function as per the agreement in CB # 30_Email030-Config_conflicts_RACHopt.

# Text proposal for TR 38.300

15.X.3 Support for RACH Optimization

Editor’s note: This section captures the stage 2 descriptions for RACH Optimization

RACH optimization is supported by UE reported information made available at the NG RAN node and by PRACH parameters exchange between NG RAN nodes.

The contents of the RACH information report comprise of the following:

- Contention detection indication per RACH attempt

- Indexes of the SSBs and number of RACH preambles sent on each tried SSB listed in chronological order of attempts.

- Indication whether the selected SSB is above or below the rsrp-ThresholdSSB threshold per RACH attempt.