3GPP TSG-RAN WG3 meeting #107-e	R3-201377

E-meeting, 24 February– 6 March, 2020

Title	[Draft] LS on inter donor DU re-routing and source IP configuration

Reply to:

Release:	Release 16

Work Item:	NR_IAB-Core

Source:	Huawei [to be RAN3]

To:	RAN2

Cc:	-

Contact person:

- Name:		Yuanping Zhu

- E-mail Address:	zhuyuanping [at] huawei [dot] com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:	None

1. Overall description

RAN3 has discussed the inter donor DU re-routing and the source IP configuration, considering that the Source IP filtering may deployed in the wireline intra donor F1 network, and the IP address allocated to IAB DU is anchored at the IAB donor DU, the following agreements are achieved:

Inter-donor DU re-routing is not support, the UL BAP address is donor DU specific.

CU includes the mapping between the IPv4 address(es)/IPv6 prefix assigned to the IAB node, and the related donor-DU’s BAP address, in the RRC message when assign the IP address to the IAB node.

2. Actions

To RAN2 group:

ACTION: 	RAN3 kindly ask RAN2 to take above RAN3 agreements into account and design the RRC signaling to support the source IP configuration.

3. Dates of next TSG RAN WG3 meetings

TSG RAN WG3 Meeting #107bis	20-24 April 2020		Sapporo, Japan

TSG RAN WG3 Meeting #108		25-29 May 2020		Athens, Greece