3GPP TSG-RAN WG3#107-e                                             	                     R3-201150

E-Meeting, 24th February – 6th March 2020

Agenda item:	14.2

Source:	Nokia, Nokia Shanghai Bell

Title: 	Summary of offline discussion on MT-EDT Finalization (CB60bis)

Document for:	Approval

# 1   Introduction

The following email discussion was started on Monday 24th February.

14.2:

CB: # 60bis_Email036-MTC_NB-IoT_MT-EDT_finalization - finalization of MDT details? - if agreeable, merge/revise as needed; go for agreement? (Nok) Summary of offline disc R3-201150

# 2   Description

Question 1: can we remove the editor’s note and confirm the use of the Pending Data Indication IE in the UE Context Resume Response message.

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes |  |
| Qualcomm | Yes | Subject of course to agreement on the related points below. |
| LG | Yes |  |
| Ericsson | Yes |  |
| Huawei | Yes |  |
| ZTE | Yes |  |

Proposal 2: can we update the procedural text in baseline CR as per TP R3-200233 to not mandate the support of the Pending Data Indication IE.

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes |  |
| Qualcomm | Yes | We are fine with having a “shall, if supported” linked to any new text because anyway MT-EDT handling and any related functionality is new. |
| LG | Yes |  |
| Ericsson | Yes |  |
| Huawei | Yes |  |
| ZTE | Yes |  |

Question 3: should the existing Pending Data Indication IE be extended with a second codepoint.

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes | there are cases where the MME is sure that further data is to be expected (RAI received with UL data or pending DL data), cases where MME is sure that no further data is to be expected (RAI received w/o UL data and no pending data), cases in the middle (e.g. RAI not used) |
| Qualcomm | No | As discussed in our paper, we see that the new codepoint may cause complication and is not strictly necessary. The complication is due to the existing use of this IE in other procedures (irrespective of codepoints), which can lead to wrong behaviour when the new codepoint is used. On the other hand, the added functionality is specific to MT-EDT, where the MME itself controls the possible start of the flow towards the RAN, and also receives an EDT indication in the INITIAL UE MESSAGE. Hence the MME already knows that it is able (via Pending Data) to provide an update to the eNB in case anything has changed. Since both MME and eNB are aware this is an MT-EDT flow, if the MME does not send the Pending Data indication, it is implicitly informing the eNB that it is not aware of further data or need for uplink data (note this is a new flow in EPS). This is something that can be made explicit in stage 2. To have two codepoints plus the “abstain” option – case in the middle – seems over complicated, and ultimately the eNB still has to make a decision. |
| LG | No | For the case in the middle (e.g., RAI not used), it seems that the MME does not send the Pending data indication to the eNB. When the Pending data indication is not included in the Context Resume Response message, the eNB just considers that MME is not aware of the further data with or without the RAI. Therefore, the eNB itself determines whether to release the RRC connection. |
| Ericsson | - | We consider that an indication is needed for MT-UP EDT so that the eNB can know that no further DL data is pending. Currently, there is no such indication that plays that role. For CP MT EDT case, the eNB can receive both the Pending Data Indication IE (to signal whether more data is expected) and the End Indication IE (that can inform the eNB that no further NAS PDU is expected for that UE) in the DL NAS TRANSPORT message. However, this End Indication is used only for CP specific signalling and cannot be used for UP case. Thus, there is an unbalance between the two solutions for MT-EDT, and an equivalent to “end indication” IE is needed for UP. With respect to the SA2 LS in R3-196428, that mentions “For UP optimized solution, SA2 will further work with RAN2/3 regarding the fallback mechanism.” A solution is needed for optimize the UP to be on par with the CP. Either, we can use the new codepoint False for the pending data indication or introduce a new IE in the S1 context resume response message. Since this is the end of the release and due to lack of time, we prefer the first option that was agreed in last meeting. Companies can also think whether the DL data size can also be used as an implicit indicator that no further data is expected in the S1 UT context resume. |
| Huawei | No | The “false” could be understood by the absence of the IE. |
| ZTE | No | Although “false” can be used to indicate that there is no data pending, the absence of the IE is used to indicate that MME cannot decide whether there is data pending, eNB will usually deal these with the same way, the new “false” codepoint is not necessary. |

Question 4: Do we need to send a short LS to RAN2 confirming that RAN3 made a working assumption for the addition of further UE category information in the radio paging information.

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | No | Seems not needed as RAN2 already working on this. |
| Qualcomm | - | This would only be needed in case RAN2 is not clear of the use case, it is ok to monitor the RAN2 situation and only react if needed. |
| LG | No | Seems to be RAN2 issue |
| Ericsson | No | RAN2 is aware of this |
| Huawei | No | Do not see the need. |
| ZTE | No | RAN2 is already discussing this issue now. |

# 3   Conclusion and proposal

Proposal:

# 3  References

- RP-172109, Revised Work Item on New Radio (NR) Access Technology, NTT DOCOMO, Inc.

- 3GPP TS 23.501, Architecture for Next Generation System, SA2