3GPP TSG-RAN WG3#107-e                                             	                     R3-201175

E-Meeting, 24th February – 6th March 2020

Agenda item:	16.2.8

Source:	Nokia, Nokia Shanghai Bell, Orange

Title: 	Summary of offline discussion on NPN Dual connectivity (CB81)

Document for:	Approval

# 1   Introduction

The following email discussion was started on Monday 24th February.

16.2.8:

CB: # 81_Email081-NPN_DC - DC is supported in both SNPN and PNI-NPN. No additional stage 3 is needed because the mobility TP for stage 3 procedural, tabular and asn1 can be reused; clarify st2 (2 options, “detailed” vs. “minimalistic” approach)? (Nok), (E///) - need for 37.340 changes? (HW) - “minimalistic” approach feasible? - if agreeable, revise/merge as needed (Nok) Summary of offline disc R3-201175

# 2   Description

Question 1: do we agree that NPN is supported in DC in release 16?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes |  |
| Huawei | Yes |  |
| ZTE | Yes |  |
| Qualcomm | Yes |  |
| Ericsson | Yes |  |

Question 2: if yes, do you agree that NPN support in DC does not require any additional stage 3 as said in R3-200202 and R3-200421?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes | Handling of the mobility restriction list and stage 3 of handover can be reused for DC. |
| Huawei | Yes |  |
| ZTE | No | Taking the manual CAG ID selection into account, the serving CAG ID needs to be included in the UE associated signaling during DC operation. |
| Qualcomm | Yes | Nothing is required beyond what should be available via current Xn changes. |
| Ericsson | Yes | Contained in already available BL content |

Question 3: if yes, do you prefer to cover the support in 38.300 only (answer 1), in 37.340 only (answer 2), or in both specifications (answer 3)?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | 1 | A short text in TS 38.300 is enough. No additional text needed for 37.340. |
| Huawei | 3 | The details of multi-connectivity for NPN should be captured in TS 37.340, which follows the basic Rel-15 principles. And TS 38.300 can add the very general descriptions of MR-DC for NPN as well. |
| ZTE | 3 | Brief description in TS 38.300 is enough, and details need to be updated in TS 37.340. |
| Qualcomm | 1 | Not a strong opinion but it seems enough to have a general statement in TS 38.300. |
| Ericsson | 1 | Not the biggest challenge for us, but we propose 38.300 |

Question 4: if yes, do you prefer to cover the support in 38.300 with the long version named option 1 in tdoc R3-200202 (answer 1) or the short version named option 2 in R3-200202 (answer 2)?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | 2 | The short version of R3-200202 (one sentence for SNPN, one sentence for PNI-NPN) is good enough. |
| Huawei | 2 | As mentioned in our answer to Q3, TS 38.300 can capture very general descriptions, while leave the details to TS 37.340. |
| ZTE | 2 | Brief description in TS 38.300 is enough. |
| Qualcomm | 2 |  |
| Ericsson | 2 |  |

# 3   Conclusion and proposal

For DC support with NPN, there is unanimity so this can be agreed.

For stage 3 impacts, all companies agree that there is no impact if you set apart the manual CAG ID selection issue. However, given that the latter point cannot be agreed as per outcome of CB74 and CB76, no stage 3 input can be agreed at this stage.

For the stage 2 there is consensus to have the short version in TS 38.300. In addition, two companies are proposing to have as well on top a CR against TS 37.340 however 3 companies do not agree.

Proposal: .

To make progress at this meeting, we propose to put the short version in TP R3-200202 for agreement at this stage and continue the discussion on the need of the TS 37.340 at next meeting.

# 3  References

- RP-172109, Revised Work Item on New Radio (NR) Access Technology, NTT DOCOMO, Inc.