3GPP TSG-RAN WG3#107-e                                             	                     R3-201175

E-Meeting, 24th February – 6th March 2020

Agenda item:	16.2.8

Source:	Nokia, Nokia Shanghai Bell, Orange

Title: 	Summary of offline discussion on NPN Dual connectivity (CB81)

Document for:	Approval

# 1   Introduction

The following email discussion was started on Monday 24th February.

16.2.8:

CB: # 81_Email081-NPN_DC - DC is supported in both SNPN and PNI-NPN. No additional stage 3 is needed because the mobility TP for stage 3 procedural, tabular and asn1 can be reused; clarify st2 (2 options, “detailed” vs. “minimalistic” approach)? (Nok), (E///) - need for 37.340 changes? (HW) - “minimalistic” approach feasible? - if agreeable, revise/merge as needed (Nok) Summary of offline disc R3-201175

# 2   Description

Question 1: do we agree that NPN is supported in DC in release 16?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes |  |
| Huawei | Yes |  |

Question 2: if yes, do you agree that NPN support in DC does not require any additional stage 3 as said in R3-200202 and R3-200421?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | Yes | Handling of the mobility restriction list and stage 3 of handover can be reused for DC. |
| Huawei | Yes |  |

Question 3: if yes, do you prefer to cover the support in 38.300 only (answer 1), in 37.340 only (answer 2), or in both specifications (answer 3)?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | 1 | A short text in TS 38.300 is enough. No additional text needed for 37.340. |
| Huawei | 3 | The details of multi-connectivity for NPN should be captured in TS 37.340, which follows the basic Rel-15 principles. And TS 38.300 can add the very general descriptions of MR-DC for NPN as well. |

Question 4: if yes, do you prefer to cover the support in 38.300 with the long version named option 1 in tdoc R3-200202 (answer 1) or the short version named option 2 in R3-200202 (answer 2)?

| Company | answer | Detailed answer |
| --- | --- | --- |
| Nokia | 2 | The short version of R3-200202 (one sentence for SNPN, one sentence for PNI-NPN) is good enough. |
| Huawei | 2 | As mentioned in our answer to Q3, TS 38.300 can capture very general descriptions, while leave the details to TS 37.340. |

# 3   Conclusion and proposal

Proposal: .

# 3  References

- RP-172109, Revised Work Item on New Radio (NR) Access Technology, NTT DOCOMO, Inc.