3GPP TSG-RAN WG3 Meeting #107-e	R3-201420

24 February-6 March 2020

Online

Title:	[Draft] LS on IP address management in IAB network

Response to:

Release:	Rel-16

Work Item:	IAB_NR

Source:	RAN3

To:	RAN2

Cc:

Contact Person:

Name:	Weiwei Wang

Tel. Number:	+86 10 8443 9777

E-mail Address:	ww1016.wang@samsung.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:  R3-201363; R3-201419

1. Overall Description:

RAN3 has discussed IP management in IAB network, and has reached the following agreements with RAN2 impact:

- For the F1AP signalling design, the maximum number of IPv4 addresses allocated by IAB donor DU in one F1AP message is 16 and the length of allocated IPv6 prefix is fixed to 64

- For IPv4 allocation, the IAB donor CU requests multiple IPv4 addresses by providing the number of the requested IPv4 address, and IAB donor DU provides a list of IPv4 addresses

- For IPv6 prefix allocation, IAB donor-CU sends IPv6 address request, and the IAB donor DU provides one IPv6 prefix, under the assumption of one IPv6 prefix per Donor DU.

- The IP version information is explicitly included when IAB Donor-CU request the IP address from IAB-Donor DU.

- IP address add/removal list is introduced in RRC signalling

- The configuration of security layer, discovery of CU-CP and SeGWs, and other IP-based services can be done via the existing solutions (e.g., OAM configuration).

- WA: address update list is introduced in RRC signalling, in which each item includes the new IP address and the corresponding old IP address.

RAN3 further achieved agreements on IP address assignment during intra-CU topology adaptation and BH RLF recovery procedure, during which the new TNL address(es) is signalled to the IAB-MT via RRC signalling. The further details are provided in attached documents (R3-201419 and R3-201363).

Meanwhile, RAN3 will continue the discussion on the above WA, the outcome of which may have implications on RRC signalling.

2. Actions:

To RAN2 group:

ACTION: 	RAN3 kindly ask RAN2 to take RAN3 agreements into account when introducing IAB-specific modifications of RRC messages.

3. Dates of Next TSG-RAN WG3 Meetings:

3GPP RAN3#107-ebis	20 – 24 April 2020			Online

3GPP RAN3#108	25 – 29 May 2020			Athens, Greece

# Comments

Don’t forget to delete on Friday.