3GPP TSG-RAN WG3 Meeting #107bis-e	R3-202461

Online, 20th - 30th April 2020

Agenda Item:	10.1

Source:	CMCC

Title:	Summary of offline discussion on SON and MDT BLCRs

Document for:	Approval

# Introduction

CB: # 1000_Email_SON-MDT_BLs

-  endorse work plan

-  Endorse all BL CRs

-  check details, revise if needed

- expect discussions only to ensure correctness of BL CRs, no new proposals (in this discussion)

(CMCC - moderator)

Summary of offline discussion R3-202461

# For the Chairman’s Notes

Propose the following:

Propose to capture the following:

# Discussion

The papers in agenda item 10.1 can be divided into the following 2 groups:

- BL CRs that have been reviewed via the reflector before the E-meeting

- LS received from SA5 on the status update of SON/MDT WI

## BLCRs

The following BL CRs captured the agreed TPs from RAN3 #107-e meeting, which are rebased on the latest Rel-16 specs and  reviewed through the reflector, so it is assumed these BL CRs are easy agreeable.

| R3-201528 | Addition of SON feature (Huawei) | draftCRr, TS 36.300 v16.1.0, Rel-16, Cat. B |
| --- | --- | --- |
| R3-201555 | BLCR to 38.420: Addition of MDT feature (CMCC) | CR0018r1, TS 38.420 v15.2.0, Rel-16, Cat. B |
| R3-201556 | BLCR to 38.420: Addition of SON feature (CMCC) | CR0019r1, TS 38.420 v15.2.0, Rel-16, Cat. B |
| R3-201557 | BLCR to 38.470: Addition of SON feature (CMCC) | CR0064r1, TS 38.470 v16.1.0, Rel-16, Cat. B |
| R3-201558 | BLCR to 38.460: Addition of SON feature (CMCC) | CR0031r1, TS 38.460 v16.0.0, Rel-16, Cat. B |
| R3-201566 | MDT support for EN-DC (Huawei) | CR1747r2, TS 36.413 v16.1.0, Rel-16, Cat. B |
| R3-201569 | Addition of RACH Optimization Feature (CMCC, Huawei) | CR0116r2, TS 38.401 v16.1.0, Rel-16, Cat. B |
| R3-201574 | MDT support for EN-DC (Huawei, SAMSUNG) | CR1440r3, TS 36.423 v16.1.0, Rel-16, Cat. B |
| R3-201608 | Addition of SON features (Huawei) | CR1710r8, TS 36.413 v16.1.0, Rel-16, Cat. B |
| R3-201609 | Addition of SON feature (CATT) | CR1373r9, TS 36.423 v16.1.0, Rel-16, Cat. B |
| R3-201610 | Addition of SON features (CMCC, Huawei) | draftCRr, TS 38.300 v16.1.0, Rel-16, Cat. B |
| R3-201611 | Addition of MDT features (Samsung) | CR0099r4, TS 38.401 v16.1.0, Rel-16, Cat. B |
| R3-201612 | Addition of SON features (Huawei) | CR0237r7, TS 38.413 v16.1.0, Rel-16, Cat. B |
| R3-201613 | Addition of MDT feature (Huawei) | CR0280r5, TS 38.413 v16.1.0, Rel-16, Cat. B |
| R3-201614 | Addition of SON features (Samsung) | CR0221r9, TS 38.423 v16.1.0, Rel-16, Cat. B |
| R3-201615 | MDT Configuration support for XnAP (Ericsson) | CR0291r7, TS 38.423 v16.1.0, Rel-16, Cat. B |
| R3-201616 | Addition of SON features (Ericsson) | CR0142r9, TS 38.463 v16.1.0, Rel-16, Cat. B |
| R3-201617 | Addition of MDT features (ZTE) | CR0477r3, TS 38.463 v16.1.0, Rel-16, Cat. B |
| R3-201618 | Addition of SON features (Huawei) | CR0441r9, TS 38.473 v16.1.0, Rel-16, Cat. B |
| R3-201619 | Addition of MDT features (Samsung) | CR0492r4, TS 38.473 v16.1.0, Rel-16, Cat. B |

Proposal 1: Endorse the above BLCRs

In case you still have some comments, please indicate it in the table. Further discussion if needed on the email reflector is preferred.

| Company | Comment |
| --- | --- |

## LS from SA5

We received a LS from SA5 on the status update of SON support for NR. Note that there is no paper of for the reply submitted to RAN3 #107bis-e meeting, we have the following two options to handle this,

- Defer the reply LS to next meeting

- Work out a reply LS as output of the email discussion

Considering the reply LS is not complex, it can be worked out during the email discussion. A draft LS is provided in the inbox.

| R3-201520 | LS on the status update of the SON support for NR works (3GPP SA5, Intel) | LS in Move to 10.1 |
| --- | --- | --- |

Proposal 2: Approval of the reply LS to SA5

Any comments on the reply LS, please indicate in the table.

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations