3GPP TSG-RAN WG3 #107bis-e	R3-202464

Online, 20-30 April 2020

Agenda item:		10.2.1.4

Source:	LG Electronics

Title:	Summary of offline discussion on SON-MDT CU-DU MRO

Document for:		Discussion

# 1. Introduction

This is the summary for the following email discussion:

CB: # 1003_Email_SON-MDT_CUDUMRO

-  Start the discussion from high level principles as raised in 1791, 2121, 2122, 2317, and 2394

-  Remember the agreements from the previous meeting

- Discuss what information has to be provided from gNB-CU to gNB-DU and from gNB-DU to gNB-CU – list these as issues in the email discussion summary and solicit comments from companies

- Attempt to agree the principles as mentioned above, once there is an agreement or at least clear majority view – proceed to discuss the TPs

- Attempt to come up with agreeable TP at least for 38.473 based on 2124, 2125, 2318, and 2395

- Furthermore, you may also attempt to come up with agreeable TPs for 38.470 and 38.401 (second priority, stage-3 comes first), based on 2123 and 2126

- This email discussion is expected to produce agreements (to be captured in the meeting minutes) on the high level principles, stage-3 TP, and possibly stage-2 TP – in that order

- Note – this email discussion may benefit from some “online” time, preferably after the “first phase” of collecting companies’ views on the high-level principles

(LG - moderator)

Summary of offline discussion R3-202464

# 2. Discussion

Considering above chairman note for this email discussion, this document consists of two phases. In Phase 1, we attempt to agree the high level principles for open issues for CU-DU aspects in MRO. According to a result of Phase 1, in Phase 2, we first attempt to come up with agreeable TP for 38.473 and, if possible, agreeable TPs for 38.470 and 38.401.

## 2.1 Phase 1

In the last RAN3 meeting, the following for CU-DU MRO was agreed:

gNB-CU should forward the UE RLF report to the gNB-DU using a dedicated procedure at least in case of the RLF caused by random access problem

Based on the submitted documents [1~5], there are three open issues that we can focus the discussion on, as below.

Question 1: Does the UE RLF report need to be provided to the gNB-DU in case of beam failure recovery (BFR) failure?

| Company | Answer | Comment |
| --- | --- | --- |
| LG | Yes | The BFR failure may be caused by random access problem. Also, because the UE RLF report includes the beam information related to BFR failure, if the gNB-DU which is in charge of beam management can receive it, optimizing the beam configuration to avoid or reduce the BFR failure is possible. |
| ZTE | Yes | Based on RAN2 progress, RLF cause includes several cases. One case is Random access in which case RAN3 has been agreed for CU send RLF to DU. For another case is beamfailurerecovery, in this case RLF information is valuable for DU to analysis beam failure root cause |
| HW | Yes | This seems beneficial |
| Ericsson | Yes | In general the RLF Report shouldbe always forwarded to the gNB-DU when received it because it contains important beam and RACH related information that could help the DU optimizing its configurations |
| Qualcomm | Yes | We agree as well that UE RLF Report should be forwarded from CU to DU so that DU (which handles beam management functions) can optimize beam configurations for improving chances of beam failure recovery and other RLF causes in general. |
| CMCC | Yes | Share the same view as above that providing RLF report to gNB-DU helps improve the possibility of successful beam failure recovery. |

Question 2: In order for the gNB-CU to send the UE RLF report to the gNB-DU, should new procedure be defined or the existing procedure be used?

| Company | Answer | Comment |
| --- | --- | --- |
| LG | New procedure | In case the gNB-CU receives the UE RLF report from either its gNB-DU or neighbor gNB-CU, it can forward them to the gNB-DU using UE-associated or non UE-associated procedure respectively. In order for one procedure to support these cases, new procedure should be defined. |
| ZTE |  | It is noting RLF report from other node does not achieve agreement. During UE setup RRC connection to the RAN node, RAN node aware UE RLF report from indication in MSG5. Without RLF assistant information from DU, CU is able to retrieve UE RLF Report via RRC “UE information ” procedure. Since UE in RRC_CONNECTED state, the retrieved RLF report come from UE has UE context in DU, it is straightforward to reuse UE associating signalling fro gNB-CU to forward UE RLF report to gNB-DU. |
| HW | New procedure | Using new procedure seems beneficial. |
| Ericsson | New procedure | A procedure for both UE associated and non Ue associated RLF Report signaling should be defined |
| Qualcomm | New procedure | We also prefer a new procedure for forwarding UE RLF Report from CU to DU. Also considering that forwarding of RACH Report over F1 is also discussed in CB#1007, we propose to use a generic message for CU to collect reports from DU which can include RLF Report, RACH Report and other reports in the future. |
| CMCC | New procedure | Share the same view as LG. |

Question 3: Does the new procedure need to be defined to provide information about the detection of RLF events and the root cause of such events from the gNB-DU to the gNB-CU?

| Company | Answer | Comment |
| --- | --- | --- |
| LG | No | Since the configuration which causes RLF is changed depending on statistics for occurrence of RLF, we wonder whether it is needed to allow the gNB-DU to provide the gNB-CU immediately with some information (e.g., detection of RLF events, root cause). Also, even if this signaling is agreeable, these information can be provided via the existing procedure (e.g., UE Context Release procedure). |
| ZTE | No | Based on UE behavior (which defined in TS38.331) in case of sending MSG 5 to RAN node, it observed that RAN node able to aware RLF report in UE during setup RRC connection. Therefore it is not necessary for DU send RLF event trigger to CU. |
| HW | No | Information is available from UE Context Release procedure. The information is not time sensitive – MRO is a statistical process. CU can wait for UE Context Release |
| Ericsson | Yes | We think that notification from DU to CU of a detected RLF at the DU is useful toallow the CU to Understand the reasons for the RLF. For example, the cause “Maximum number of DL RLC retransmissions” cannot be deduced by the CU Anticipate possible actions that follow an RLF, for example prepare for a possible re-establishment from the UE, prepare for an upload of the RLF Report |
| Qualcomm | No | Considering that UE already indicates the presence of RLF Report using rlf-InfoAvailable IE for most RLF causes and in other cases such as “maximum number of DL RLC retransmissions”, DU can indicate CU to release UE resources using UE Context Release procedures, we don’t see the strong need to introduce a new procedure indicating the RLF cause for optimization purposes. |
| CMCC | No | In our opinion, using UE Context Release procedure is enough, and the Cause value ‘RL Failure-RLC’ has been defined. |

## 2.2 Phase 2

TBD

# Conclusion

TBD

# References

- R3-201791, “Remaining issues in CU-DU MRO”, Qualcomm Incorporated

- R3-202121, “Signalling of RLF information from gNB-CU to gNB-DU”, Ericsson

- R3-202122, “Signalling of RLF information from gNB-CU to gNB-DU”, Ericsson

- R3-202317, “Open issues for CU-DU MRO”, LG Electronics

- R3-202394, “Left issue for CU-DU MRO”, ZTE