# 3GPP TSG-RAN WG3 Meeting #107bis-e 					       R3-20xxxx

# 20 - 30 April 2020, E-Meeting

Agenda item:	13.2.4

Source:	Nokia, Nokia Shanghai Bell

Title:	(TP for NR-IAB BL CR for TS 36.423) TP to clarify the F1-C traffic over LTE leg

Document for:	Discussion and Decision

# 1	Introduction

This is the Stage-3 TP per CB: # 10_Email_IAB_DC_operation ([1])

# References

# R3-202482, Summary of offline discussion on CB: # 10_Email_IAB_DC_operation

# Proposed TP to TS36.423 BL CR:

-------------------------------------------Start of Change -------------------------------------------

>>>	Unaffected parts skipped    <<<

### 8.7.x	F1-C Traffic Transfer

#### 8.7.x.1	General

The purpose of the F1-C Traffic Transfer procedure is to deliver F1-C traffic to the MeNB so that it is then forwarded to the IAB-node, or deliver F1-C traffic to the en-gNB, if it was received from the IAB-node.

The procedure uses UE-associated signalling.

#### 8.7.x.2	Successful Operation

Figure 8.7.x.2-1: F1-C Traffic Transfer procedure, successful operation.

Either the MeNB initiates the procedure by sending the F1-C TRAFFIC TRANSFER message including the received F1-C traffic to the en-gNB, or the en-gNB initiates the procedure by sending the F1-C TRAFFIC TRANSFER message to the MeNB.

Upon reception of the F1-C TRAFFIC TRANSFER message, the MeNB shall deliver the contained F1-C traffic to the IAB-node as specified in TS36.331 [9].

Upon reception of the F1-C TRAFFIC TRANSFER message, the en-gNB shall handle the received F1-C traffic as specified in TS38.473 [x] and TS38.472 [y].

#### 8.7.x.3	Abnormal Conditions

Not applicable.

#### 8.7.x.4	Abnormal Condition

Not Applicable.

------------------------------------------Next Change -------------------------------------------

#### 9.1.4.x	F1-C TRAFFIC TRANSFER

This message is sent by the MeNB to the en-gNB or by the en-gNB to the MeNB to transfer the F1-C traffic.

Direction: MeNB ( en-gNB or en-gNB ( MeNB.

| IE/Group Name | Presence | Range | IE type and reference | Semantics description | Criticality | Assigned Criticality |
| --- | --- | --- | --- | --- | --- | --- |
| Message Type | M |  | 9.2.13 |  | YES | reject |
| MeNB UE X2AP ID | M |  | eNB UE X2AP ID 9.2.24 | Allocated at the MeNB. | YES | reject |
| SgNB UE X2AP ID | M |  | en-gNB UE X2AP ID 9.2.100 | Allocated at the en-gNB. | YES | reject |
| F1-C Traffic Container | M |  | OCTET STRING | Contains an F1-C IP packet including a F1AP message or a SCTP CHUNK, as well as the SCTP/IP header. This IE corresponds to the DedicatedInfoF1AP-r16 defined in TS 36.331 [9]. | YES | reject |

------------------------------------------End of Change -------------------------------------------

# Comments

The below description text use "shall deliver".