3GPP TSG-RAN WG3 #107bis-e	R3-202511

20-30 April 2020

Online

Agenda Item:	16.3.2

Source:	Nokia, Nokia Shanghai Bell

Title:	Summary of Offline Discussion of NPN Mobility Restriction List

Document for:	Approval

# Introduction

CB: # 30bis_Email_PRN_MobRestrList

- SNPN ID contained in NPN Mobility Information IE? (Nok)

- Add MRL to the UE CONTEXT MODIFICATION REQUEST message? (E///)

- Add a note on the application of mobility restriction for NPN in the NGAP BL CR, and update the note in the XnAP BL CR; add the procedural texts on NPN mobility information in NGAP BLCR and XnAP BLCR? (HW)

- st2 aspects? (CT,HW)

- revise as needed; check details

(Nok - moderator)

Summary of offline disc R3-202511

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on the gNB-CU. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Stage 3: Modification Request

Question 1: do we need to add MRL in the UE Context modification Request (tdoc 2129):

| Company | Comment |
| --- | --- |
| Nokia | No. This is already included in DL NAS Transport therefore redundant. Adding in Modification Request would force NG-RAN node to implement both. Sending it in DL NAS Transport allows automatic synchronization between NG-RAN and UE. |
| Huawei | Same understanding as Nokia. Sending the MRL together with the NAS-PDU in DL NAS transport can allow the UE and RAN synchronized. |
| ZTE | No. Mobility Restriction List is already provided in the DL NAS Transoport Message. |

## Stage 3: Coding of Mobility Information

Question 2: is it ok to change NID into SNPN ID in the mobility information IE to have it self-contained (tdocs 1814, 1815)?

| Company | Comment |
| --- | --- |
| Nokia | Yes. This allows a complete definition of the mobility area of the UE for NPN in one IE (= self-contained). This also makes this Mobility Information IE reusable. |
| Huawei | Seems not necessary. This will create redundancy with the serving PLMN ID IE in MRL. Note that we have a similar discussion on initial UE message (CB#30) to change 9.3.3.Y5 in the BL CR to only contain the NID, not the SNPN ID. It seems the same logic can be applied here: no redundancy is introduced. |
| ZTE | Yes. It makes the NPN mobility information of UE clear. |

## Stage 3: Update of NGAP CR

Question 3: is it ok to add the note in the NGAP similar as XnAP and some NPN procedural text (tdoc 2338)

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Huawei | Yes |
| ZTE | Yes. |

## Stage 3: Update of XnAP CR

Question 4: is it ok to modify the note in the XnAP and some NPN procedural text (tdoc 2339)?

| Company | Comment |
| --- | --- |
| Nokia | Partly ok. Modification of the note is ok but no need for the additional procedural text. |
| Huawei | Ok about the note. Also the following descriptions “or for above aspects for NPN” seems necessary in 9.2.3.53 Mobility Restriction List We are open to the NPN related procedural texts. |
| ZTE | Seems OK. |

## Stage 2: 38.300

Question 5: is it ok to add received MRL at incoming handover in addition to context creation (tdoc 2177)?

| Company | Comment |
| --- | --- |
| Nokia | No. This change is not correct. The words “context creation” was carefully thought to cover all possible scenarios including when UE context is created at incoming handover. |
| Huawei | Yes. The original descriptions is that: “The NG-RAN node has received…… from the AMF at the time of UE context creation”, it may be understood in a way that this context creation only applies to initial access. |
| ZTE | No. |

## Stage 2: 37.340

Question 6: do we need specific text for NPN in section 11.1 of TS37.340 (tdoc 2340)?

| Company | Comment |
| --- | --- |
| Nokia | No. The section 11.1 is supposed to be generic enough and doesn’t need to be refined per added feature. |
| Huawei | Yes. The section 11.1 now only covers the roaming and access restriction information for PLMN access/mobility. It is a reasonable way to extend to support NPN access as well. |
| ZTE | Yes. |

# Conclusion, Recommendations [if needed]

If needed

# References