3GPP TSG-RAN WG3 #107bis-e	R3-202518

20-30 April 2020

Online

Agenda Item:	16.9

Source:	Nokia, Nokia Shanghai Bell

Title:	Summary of Offline Discussion of NPN slicing

Document for:	Approval

# Introduction

CB: # 37_Email_PRN_slicing

Nok,E///,CT: Served Cell Information IE shall ensure that NID and TAI have a 1:1 relationship over F1

NEC: select among:

Opt1: introduce the list of NIDs at the PLMN ID level

Opt2: introduce a single NID at the PLMN ID level

Opt3: introduce SNPN specific slice information

E///:

Change the Supported TA List IE (in the NG SETUP REQUEST message and the RAN CONFIGURATION UPDATE message) and the PLMN Support List IE (in the NG SETUP RESPONSE message and the AMF CONFIGURATION UPDATE message) so that a one-to-one relation between a network and a network slice is maintained

Separate the current NPN Support IE into a NG-RAN NPN Support IE and a 5GC NPN Support IE.

The same kind of review has to be performed for the other NG-RAN interfaces. See TPs in [R3-202139 ff]. Due to the different nature of the E1, F1 and Xn interfaces, the discussions are led on top of the respective TPs.

CT: The NPN Information in the Served Cell Information for F1AP specification should be defined both at the same level as existing PLMN Identity IE and at the same level as 5GS-TAC

HW:

No need to add the CAG list into the TAI Support List for all related interfaces.

Add the NID support list (including one or multiple NIDs) in TAI Support List for XnAP.

Update the NPN Support Information to include NID lists for E1AP.

Add the NPN support in the network slicing section for TS 38.300.

The current spec does not need additional changes on slices aspects over NG and F1 interfaces.

- remove ed note: “The exact location of the introduced IE ‘NPN Support Information’ needs to be further discussed”? (NEC)

(Nok - moderator)

Summary of offline disc R3-202518

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on the gNB-CU. May be possible to address with a pure st2 change. To be continued…

# Discussion

## one NID or multiple NIDs associated with the slice support list (NG, Xn, E1, F1 interface)

There are two options possible:

- option 1: have only one NID in NPN Support IE (e.g. tdocs 1820, 2138, 2139, 2141) or

- option 2: to have a list of NIDs in NPN Support IE (e.g. 2355, 2356)

Question 1: which option do you prefer among option 1 or option 2?

| Company | Comment |
| --- | --- |
| Nokia | Option 1. This allows easy differentiation of distinct list of slices per SNPN. |
| Huawei | Both options could work. Slightly prefer option 2. According to SA2 TS 23. 501, “a Network Slice is defined within a PLMN or SNPN”. This means, the slice concept is within the PLMN or SNPN. For multiple SNPNs sharing the same TAI, they can hold their respective slices, either the same or different. Option 2 can allow multiple SNPNs sharing the same TAI have their respective but same slices in a single loop. While option 1 needs multiple loops, though with slice and SNPN with 1-to-1 mapping. |

## Specific NG: Split of NPN Support IE

Question 2: do you find useful to split the NPN Support IE in two parts: 5GC part from CN to RAN and RAN part from RAN to 5GC (e.g. tdoc 2138)

| Company | Comment |
| --- | --- |
| Nokia | No. Don’t see the need. |
| Huawei | No, seems not necessary to have same format but with different IE name. |

## Stage 2

Question 3: do we need text in 38.300 for slicing in NPN (e.g. tdoc 2357)?

| Company | Comment |
| --- | --- |
| Nokia | No. This is already described in 23.501. |
| Huawei | Yes. The general RAN support of network slicing is described In TS 38.300, so the NPN support of network slicing should be described well, following the same logic e.g. QoS parameters. |

# Conclusion, Recommendations [if needed]

If needed

# References