3GPP TSG-RAN WG3 #107bis-e	R3-202479

E-Meeting, 20th-30th April 2020

Agenda item:	13.2.1.2

Source:	Huawei

Title:	Summary of offline discussion on CB: # 7_Email_IAB_F1AP _cleanups

Document for:	Discussion & Decision

# Introduction

This contribution is to summarize the offline discussion for the following CB:

CB: # 7_Email_IAB_F1AP_cleanups

- go for minimum set of agreeable changes

- merge and revise as agreeable; check details

(HW - moderator)

Summary of offline disc R3-202479

As assigned by Chairman, the offline discussion will cover the following contributions in this meeting:

[1] R3-202309 (TP for NR-IAB BL CR for TS 38.473): Cleanups (Ericsson)

[2] R3-202085 (TP for NR_IAB BL CR for TS38.473):  BH mapping configuration for control PDU (Huawei)

[3] R3-202086 (TP for NR-IAB BL CR for TS 38.473): Remaining issues for BH RLC channel management (Huawei)

[4] R3-202064 (TP for NR-IAB BL CR for 38.473) Remaining issues except bearer mapping configuration (Samsung)

Since the above papers discussed some common issues but without convergence, it would be better to have some discussions before developing TP.

# For the Chairman’s Notes

[to be added]

# Discussions

## Issue 1. Some values of parameter in BL CR of TS 38.473

- Issue 1-1: Range of BH RLC channel and detailed design for the BH RLC channel ID

RAN2 has determined to extend the LCID for support multiple BH RLC channels in IAB network, according to the latest published MAC spec [38.321], the LCID is extended for BH RLC channel, the value for extended LCID to identify the logical channel corresponds to the BH RLC channel is from 320 to (216 + 191), then the maximum LCID can be used for BH RLC channel is 216-128(reserved) +32 (legacy)=65440. In last RAN3 107-e meeting, the maximum number of BH RLC channel number is set to 16384, so there is misalignment for the max value of BH RLC channel from RAN2 and RAN3.

There are three papers, i.e., [1], [3] and [4] discussed this misalignment issue, and all three papers have same view that the value defined by RAN2 and RAN3 should be aligned. But the three papers propose different solutions for the aligned value, thus we have the following three options:

- Option 1[1]: RAN3 confirm maximum value of BH RLC channel is still 16384, RAN2 should align with RAN3.

- Option 2[3]: RAN3 align with RAN2, the maximum number of BH RLC channel is 65440.

- Option3 [4]: RAN3 align with RAN2, the maximum number of BH RLC channel is 65536.

About the BH RLC channel ID，there are also two options based on the contributions. As shown in the following text box, [1] suggest the BH RLC channel ID use the same format as the LCID, which should be a CHOICE value from the LCID and extended LCID.

But it is worth noting that in the procedure of BH RLC channel establishment, it is the parent DU is responsible for allocating the LCID if a BH RLC channel is requested to be setup or modified. So the IAB donor CU is not able to know the LCID in advance when sending UE CONTEXT SETUP/MODIFICATION REQUEST message to the DU. In fact, the BH RLC channel ID is just used to identify the BH RLC channel and allocated by the IAB donor CU, [3] propose to use a 16bits length bit string to indicate the BH RLC channel ID.

- Issue 1-2: maxnoofChildIABNodes and maxnoofServedCellsIAB

[1] further propose the following  values for the following two parameters:

- maxnoofChildIABNodes, i.e. the maximum number of children IAB-nodes served by an IAB-DU or IAB-donor-DU is 6.

- maxnoofServedCellsIAB, i.e. the maximum number of cells served by an IAB-DU or IAB-donor-DU is 3.

Q1: values/formats of the following parameters:

  - maxnoofBHRLCChannels: Option 1:16384,  Option 2:65440? or Option 3:65536?.

  - BH RLC CH ID: BIT STRING(16) vs. similar format as LCID.

  - noofChildIABNodes=6

  - maxnoofServedCellsIAB=3

| Company | Comments |
| --- | --- |
| Huawei | maxnoofBHRLCChannels: Option 2:65440 BH RLC CH ID: BIT STRING(16). noofChildIABNodes: no strong view on this value. Since we have 10bits for the BAP address length, thus we can support at most 1024 IAB nodes in an IAB donor, if we support at most x child IAB nodes for a given parent DU, and if we still assume at most we support H hops for R16 IAB, x should be constrained by the following inequality: x+x2+…+xH≤1024. So, if H=3, x=9 is the largest integer value, if H=4, x=5 is the largest integer value. maxnoofServedCellsIAB: This value is suggested to refer the maximum cells can be supported by the gNB-DU, which is 512 as shown in the following table from the TS38.473. Range bound Explanation maxCellingNBDU Maximum numbers of cells that can be served by a gNB-DU. Value is 512. |
| Samsung | maxnoofBHRLCChannels: option 2 or option 3 BH RLC CH ID: BIT STRING(16) noofChildIABNodes: we prefer to a future-proof way, i.e., 1024. Also, the maximum number of IAB nodes is limited by length of BAP address, i.e., 1024 maxnoofServedCellsIAB: 512 |
| QCOM | maxnoofBHRLCChannels: option 2 or 3. A few months back, we had long discussions if the Flow Label of 20bits would be large enough to cover all bearers on the BH. Now we are down to 16bits. I think we should not shrink it further. BH RLC CH ID: BIT STRING(16) noofChildIABNodes: We need to allow for deployments where the donor-DU connects many child nodes with only one hop. The present BAP address space supports 10bits. Therefore, the noofChildIABNodes should too. We agree with Samsung: 1024. maxnoofServedCellsIAB: 512 |
| Nokia | For maxnoofBHRLCChannels, slightly prefer Option 3. Agree with QCOM/Samsung for other aspects. |
| KDDI | Agree with Nokia for 4 aspects. |

## Issue 2: Modification for Uplink UP Traffic Mapping

At the RAN3#106 meeting, RAN3 agreed the F1AP UL BH information IE that configures per GTP-U tunnel: BAP Routing ID, Next-hop BAP Address and BH RLC CH ID, where all these 3 parameters are mandatory. [1] shows view that UL UP packets with the same BAP Routing ID will always be mapped to the same Next-hop BAP Address and BH RLC CH ID , and suggest to change the presence of the Next-hop BAP Address and BH RLC CH ID in the UL BH information IE to be optional, such optimization mainly aims at reducing some redundant configuration for the BH bearer mapping if multiple F1-U tunnels are assigned with same BAP routing ID.

Q2: Do we agree to change the Next-hop BAP address and BH RLC CH ID in the UL BH information IE to be optional as suggested by [1]?

| Company | Comments |
| --- | --- |
| Huawei | RAN3 has agreed that the UL mapping to egress BH RLC channel relies on the GTP-U tunnel information for F1-U traffic at the access IAB node, even if packets belongs to different F1-U tunnels are assigned with same BAP routing ID, they still can be mapped to different BH RLC channels. Therefore, we suggest to keep thetwo IEs’ presence field as it is. |
| Samsung | We prefer to keeping the current presence. |
| QC | This is only about optionality of the entries in the UL BH info IE. We are fine with the optimization proposed by [1]. |
| Nokia | Current presence is fine. This proposal may bring a small saving. |
| KDDI | Agree with Nokia |

## Issue 3: Configuration for BH mapping of BAP control PDU

In RAN2 109-e meeting, has made the following agreement on bearer mapping of BAP control PDU in [1].

- The CU may assign a BH RLC channel for BAP control PDU transmission via F1AP. If not assigned by the CU, the IAB-node selects the BH RLC channel for BAP control PDU by implementation.

RAN2 has defined multiple kinds of BAP control PDUs, some are for upstream, e. g. the flow control feedback, while others are for downstream, e.g. the  BH RLF notification, the flow control poll etc. So RAN3 should enable the configuration of the BH mapping for selecting the egress BH RLC channel for BAP control PDU.

In [2],  it propose to extend the existing Uplink BH Non-UP Traffic Mapping IE which is used to configure the BH mapping for non F1-U traffic, since the BAP control PDU is also a non-F1 traffic. [2] suggest to change the name of this IE to be BH Non-UP Traffic Mapping IE since the BAP control PDU may also be DL, and change the BAP routing ID to be optional since the routing information is not needed for BAP control PDU, and add an extra code point to include the BAP control PDU in the Non-UP Traffic Type IE, which just includes the UE-associated F1AP, non-UE-associated F1AP, and non-F1 traffic in current BL CR.  At the same time, considering that only 3 codepoints are defined in Control Plane Traffic Type IE for identifying different priorities. [2] also suggest to introduce an additional codepoint for priority level of BH RLC channel to support BAP control PDU.

Another way proposed by [4]: When configuring the BH RLC CH, an indication for BAP control PDU transmission may be included in F1AP message to configure its serving IAB-DU/IAB donor DU, and included in RRC messages to configure its serving IAB-MT.

Q3: Which solution should be used for providing BH mapping configuration for BAP control PDU?

Option 1. Use same way as what we used for configuring the BH mapping for F1-C and non-F1 traffic, only relies on F1AP message, some existing IEs shall be enhanced, e.g. change the BAP routing ID to be optional, add extra code point to the BH Non-UP Traffic Mapping IE BH Non-UP Traffic Mapping IE, and extend the value field of priority level for BH RLC CH to carry non-UP traffic, etc.

Option 2. Include usage indication (e.g.  for BAP control PDU transmission) in F1AP message to parent DU when configuring BH RLC channel, and also includes similar indication in RRC message to child IAB-MT.

| Company | Comments |
| --- | --- |
| Huawei | Option 1. Only impact the F1AP, same as what we have agreed for configuring mapping of F1-C and non-F1. This solution enables a unified solution for mapping configuration for all kinds of non-F1-U traffics. |
| Samsung | Option 2 The proposal in [2] is misleading, which indicates that the BAP control PDU needs the whole mapping information, which includes BAP routing ID, next-hop BAP address, and BH RLC CH ID. That’s not the intention since BAP control PDU is a one-hop packet. |
| QC | Samsung is right in that only Next-hop BAP address + BH RLC channel need to be configured. However, we still prefer using F1AP based on RAN2’s agreement to use as common signaling protocol. We propose the following: Use F1AP and the present UL BH Info IE with optional BAP Routing ID field. Including [1]’s proposal above, all entries of the UL BH info become optional. |
| Nokia | Option 1 |
| KDDI | Agree with QC |

## Issue 4: Configuration for BH RLC channel

Issue 4-1. DL/UL indication for BH RLC CH Configuration

In the real case, an BH RLC CH may be used for DL or UL traffic only. [4] propose the IAB donor CU should indicate the direction of BH RLC CH when configuring it, to facilitate the RLC configuration (e.g., um-Uni-Directional-UL IE for UL only, or um-Uni-Directional-DL IE for DL only).

Q4-1: Do we need to add BHRLCCHDirection IE to indicate the traffic direction over the configured BH RLC channel, as suggested by [4] the following enhancement about the configuration for BH RLC channel?

| Company | Comments |
| --- | --- |
| Huawei | Not necessary. Even for DRB configuration, there is no such indication in F1 interface, the RLC configuration (includes the direction) can be determined by the DU according to the QoS parameters, so we don’t need this directional information for BH RLC channel either. |
| Samsung | We need such indication. In F1, we have QoS Flow Mapping Indication IE, which indicates the direction of QoS flow, i.e., DL or UL. This information can help DU to generate the configuration for corresponding DRB. BH RLC CH has the similarity to DRB. |
| QC | The node should know the direction of the BH RLC channel. I am not certain we want to imply that QoS for BH RLC channels is used in the same manner as for access RLC channels (see Issue 4-2 for instance). It would be better to add this indication explicitly. |
| Nokia | Agree the indication is needed. But we are not sure that the direction can be modified, it may add more complexity. |
| KDDI | We are fine to add the indication. |

Issue 4-2. QoS parameter for BH RLC CH Configuration

RAN3 has agreed that the DRB/flow level QoS parameters IE defined in TS 38.473 can be reused for the BH RLC channels. According to the discussion in last RAN3 107-e meeting, almost all companies agrees that the QoS parameters configured by the IAB-donor-CU for each BH RLC channel is per hop QoS.

Based on further check, the packet delay budget (PDB) defined in E-UTRAN QoS is “The Packet Delay Budget (PDB) defines an upper bound for the time that a packet may be delayed between the UE and the PCEF.” according to the definition shown in TS23.203, and for 5G QoS, it is “The Packet Delay Budget (PDB) defines an upper bound for the time that a packet may be delayed between the UE and the UPF that terminates the N6 interface.”[TS23.501]. Apparently, the current definition of PDB is not directly applicable for the BH RLC channel which just require per hop QoS. Thus [3] suggest to provide clarification as:

For a BH RLC channel, the Packet Delay Budget included in QCI defines the upper bound for the time that a packet may be delayed between the gNB-DU and its child IAB-MT.

Q4-2: Do we need the clarification about the PDB if configured for BH RLC channel?

| Company | Comments |
| --- | --- |
| Huawei | Yes. The clarification is necessary to support reusing the DRB/QoS flow level QoS parameters for BH RLC channel. |
| Samsung | Yes . The clarification is beneficial. |
| QC | Yes, |
| Nokia | Yes. There is a duplication for “upper bound”. |
| KDDI | Yes |

## Issue 5: DL GTP-U tunnel setting in case of topology redundancy

This issue is for the following scenario: An IAB node is dual-connected via two different donor DUs in case of topology redundancy, and two IP addresses, i.e., IP1 and IP2, are allocated to the IAB node. The IP1 and IP2 are, respectively, used by IAB node for the data transmission over the first path and the second path.

For establishing F1-U tunnels, IAB-DU needs make a selection between IP1 and IP2 in step 2 when determining the IP address in DL GTP-U tunnel. Apparently, the selected IP address for DL GTP-U tunnel determines the routing path of the DL packet, e.g., first-path or second-path. The remaining issue for such scenario is that how can the dual connecting IAB-DU select the IP address for the DL TEID information of an F1-U tunnel. To solve this issue, the following options are provided by [4]:

- Opt 1: IAB node determines the IP address by itself and the IAB donor CU determines the routing path based on the selected IP address

- Opt 2: IAB node determines the IP address according to the BAP address of the destination IAB donor DU contained in the UL BH information IE, which is configured by the IAB-donor-CU in the UE CONTEXT SETUP/MODIFICATION REQUEST message.

- Opt 3: IAB donor CU includes the BAP address of donor DU for the selected routing path when sending UE Context Setup/Modification Request message.

Option 1has no specification impact, the IAB node determines which IP address is used for DL by itself, in other words, the IAB node will determines which donor DU the DL F1-U packets should pass.

For option 2, the DL and UL traffic should be transmitted via the same donor DU, and some clarifications is needed since the current UL mapping information IE is not aiming at indicating the DL routing path.

For option 3, the DL traffic can be transmitted via a different routing path from the UL traffic. IAB-donor-CU need to provide the selected BAP address of the IAB donor DU for IAB node to determine the DL IP address when providing the UL mapping information.

Q5: Which option is preferred?

| Company | Preference and Comments |
| --- | --- |
| Huawei | Option1 or Option 2. No additional specification impacts are needed. And there is no problem if both DL and UL packets of same F1-U traffic be transmitted via same IAB donor DU. |
| Samsung | Option 3 is our first preference since it provides the largest flexibility. In our understanding, one intention of topology redundancy is load balancing. Allowing DL and UL different routing paths is a possible way. Moreover, in the real case, DL traffic may be heavier than UL traffic. Then, DL and UL can be transmitted via separate routing path. We can accept Option 2 with some clarifications since it has less specification impact. The clarifications can be, e.g., 1) the BAP address in current UL mapping information can be used to indicate the donor DU via which the DL traffic is transmitted; and 2) in case of topology redundancy, the DL and UL traffic should be transmitted via the same donor DU. Option 1 is not acceptable since from very beginning, we agree that the IAB donor CU determines the routing path. While option 1 indicates that the routing path of DL traffic is determined by IAB node in case of topology redundancy. |
| QC | Option 2 or 3. The IAB-donor is the principal entity to determine the routing path. We can allow different paths for UL and DL but we should not have IAB-node decide one direction and IAB-donor the other. How should the IAB-node make that decision? IT has no global visibility of topology, path quality or laod. Side note: The IP address for DL traffic included by the IAB-node to the CU may neither be IP1 nor IP2 if IPsec tunnel mode is used. |
| Nokia | Option 1 How is this different to a normal wired DU, e.g. with have 2 Network Interface Cards? The gNB-DU just select one for the DL traffic. |
| KDDI | Share the view with Huawei |

## Issue 6: BAP address configuration to IAB-donor-DU

In last RAN3 meeting, the following agreement was achieved:

Donor-CU configures Donor-DU with the BAP address during the F1 Setup procedure between the Donor-DU and Donor-CU. FFS on whether include multiple BAP address.

About the number of BAP address configured for the IAB-donor DU, [3] propose to support up to 1024 to achieve some kinds of balance for the UL and DL, since the maximum number of IAB nodes can be 1024 according to the 10 bits BAP address.

Q6: Do we need to support multiple BAP address for the IAB-donor-DU, and the maximum number can be 1024?

| Company | Preference and Comments |
| --- | --- |
| Huawei | Configure one BAP address for an IAB-donor-DU is enough, there is no technical motivations for supporting multiple BAP addresses. |
| Samsung | We see the number imbalance between DL and UL. Thus, we prefer to allowing multiple BAP addresses at one IAB donor DU. Otherwise, one IAB donor DU can only support 1024 different routing paths, which is not our intention to define 10-bits for BAP address and 10 bits for path ID. |
| QC | The same question has been asked by Nokia in CB #5. We do not see the reason for multiple BAP addresses on the IAB-donor-DU. This may create additional problems as we have had with the allocation of multiple IP addresses for the IAB-node. One BAP address per donor DU is enough in Rel-16. Samsung’s claim is incorrect. In a spanning tree, one single BAP path ID is sufficient for all IAB-nodes since all routing entries point to the same next hop. For DAG, multiple path IDs are only needed if paths cross. In practice, the number of 1024 path IDs is already complete overkill. |
| Nokia | One BAP address is enough. If no objection, I will move your comments to my CB, so the Stage-3 TP can be prepared accordingly. |
| KDDI | One BAP address is enough. |

## Issue 7: BH mapping for re-routed packets if BH RLF is suffered.

RAN2 has agreed to allow IAB node do re-routing for some packets when BH RLF. But how to perform the BH mapping in the backup path is still not clear. In [3], 3 solutions are proposed:

Option 1. Assuming the regular BH RLC channel mapping on the backup link is also configured by the IAB donor CU before BH RLF.

Option 2. It is IAB node implementation to use any BH RLC channel on the backup egress link.

Option 3. A specific/default BH RLC channel to be used in case BH RLF is configured on the backup egress link.

Some of the above options may involve RAN3 impact, e.g. option 3 requires a specific BH RLC channel to be established in the backup link, and the IAB node should aware this BH RLC channel as a “specific/default” one. However, RAN2 will also discuss the same issue, so the moderator give the following suggestion: RAN3 can wait RAN2’s conclusion, and provide further design if necessary.

Q7: Can RAN3 wait RAN2’s conclusion about the BH mapping for re-routed packets in backup path, and provide further design if necessary?

| Company | Comments |
| --- | --- |
| Samsung | Let’s wait for RAN2 |
| QC | This is a RAN2 issue. It has been discussed in RAN2 and RAN2 has agreed on how to proceed in this case. Please let us not waste time in RAN3 on this. |
| Nokia | Wait for RAN2. |
| KDDI | Wait for RAN2. |

# Conclusions

# References

[1] R3-202309 (TP for NR-IAB BL CR for TS 38.473): Cleanups, Ericsson.

[2] R3-202085 (TP for NR_IAB BL CR for TS38.473):  BH mapping configuration for control PDU, Huawei.

[3] R3-202086 (TP for NR-IAB BL CR for TS 38.473): Remaining issues for BH RLC channel management, Huawei.

[4] R3-202064 (TP for NR-IAB BL CR for 38.473) Remaining issues except bearer mapping configuration, Samsung.

# Text boxes

BHChannelID ::= CHOICE {

lCID			LCID,

extendedLCID	ExtendedLCID,

...

}