3GPP TSG-RAN WG3 Meeting #107bis-e	R3-20xxxx

# Online, April 20th – 30th 2020

Agenda Item:	13.2.1.1

Source:	Ericsson

Title:	(TP for NR-IAB BL CR for TS 38.401): IP Address Allocation for IAB-nodes

Document for: 	Agreement

# Annex: TP for NR-IAB BL CR for TS 38.401

-------------------------------------------Change 1-------------------------------------------

## 8.9	Overall procedures involving E1 and F1

The following clauses describe the overall procedures involving E1 and F1.

>>>>>>>>>>>>>>> Unchanged parts are skipped<<<<<<<<<<<<<<<<

### 8.9.z	IP Address Allocation for IAB-nodes

An IAB-node may obtain IP address(es) either from the IAB-donor or from the OAM system (which may also include methods such as pre-configuration, DHCP etc.). In case IPSec tunnel mode is used in the IAB network it is the outer IP address(es) that is(are) allocated to an IAB-node by the OAM or IAB-donor by using the IAB-node IP address management procedures, while the inner IP address(es) is(are) allocated by using off-the-shelf methods that are outside of 3GPP scope. In case of IPsec transport mode, or if no IPsec is used, the IP address(es) is(are) allocated to an IAB-node by the OAM system or IAB-donor.

In case of IAB-donor-based IP address allocation, the IP address(es) may be allocated by the IAB-donor-CU or IAB-donor-DU. In both cases, the IAB-node requests the IP address(es) via RRC from the IAB-donor-CU, where a number of addresses is requested for a specific usage: F1-U, F1-C and non-F1. For IAB-donor-DU-based IP address allocation, upon receiving the IP address request, the IAB-donor-CU may trigger the IAB TNL Address Allocation procedure towards the IAB-donor-DU to request the IP address(es) on behalf of the IAB-node. Upon receiving the IP address(es) from the IAB-donor-DU, the IAB-donor-CU may send the allocated IP address(es) to the IAB-node via RRC. For IAB-donor-CU-based IP address allocation, upon receiving the IP address request from the IAB-node, the IAB-donor-CU sends the allocated IP address(es) to the IAB-node via RRC.

The entity in charge of IP address allocation (i.e. IAB-donor-CU/DU or the OAM) indicates the usages of allocated IP address(es). An IAB-node may be allocated full IPv4 address(es) and/or full IPv6 address(es) and/or an IPv6 prefix, where each IAB-node under one IAB-donor-DU receives a unique IPv6 prefix.

In case of OAM-based IP address allocation, before F1 transport has been set up, the IAB-node informs the IAB-donor-CU via RRC about its allocated IP address(es) and their respective usage(s). Based on the knowledge of allocated IP address(es) and their respective usage(s), for both OAM-based and IAB-donor-based IP address allocation, the IAB-donor-CU configures the IAB-donor-DU with the mapping between the IP address(es) allocated to the IAB-node and the corresponding DL BAP Routing ID(s). The configured mapping in the IAB-donor-DU may be based on the full IPv4 and/or IPv6 address(es) and/or IPv6 prefix assigned to an IAB node, where the full IPv6 address takes precedence over the corresponding prefix.

IP address update is performed using DL RRC signalling, where the updated address replaces the old one.

-------------------------------------------End of changes-------------------------------------------

# Comments

IAB network does not a mode of IPSec tunnel mode

The intention for this change is that:

IP address request via RRC is not necessarily combined with IP address request via F1AP.

IAB donor DU cannot indicate the usage to IAB node