3GPP TSG-RAN WG3 Meeting #107bis-e	R3-20xxxx

# Online, April 20th – 30th 2020

Agenda Item:	13.2.1.1

Source:	Ericsson

Title:	(TP for NR-IAB BL CR for TS 38.401): IP Address Allocation for IAB-nodes

Document for: 	Agreement

# Annex: TP for NR-IAB BL CR for TS 38.401

-------------------------------------------Change 1-------------------------------------------

## 8.9	Overall procedures involving E1 and F1

The following clauses describe the overall procedures involving E1 and F1.

>>>>>>>>>>>>>>> Unchanged parts are skipped<<<<<<<<<<<<<<<<

### 8.9.z	IP Address Allocation for IAB-nodes

An IAB-node may obtain IP address(es) either from the IAB-donor or from the OAM system. In case IPSec tunnel mode is used to protect F1 interface in the IAB network it is the outer IP address(es) that is(are) allocated to an IAB-node by the OAM or IAB-donor , while how the inner IP address(es) is(are) allocated is outside of 3GPP scope. In case of IPsec transport mode, or if no IPsec is used, the IP address(es) is(are) allocated to an IAB-node by the OAM system or IAB-donor.

In case of IAB-donor-based IP address allocation, the IP address(es) is(are) allocated by the IAB-donor-CU or IAB-donor-DU. In both cases, the IAB-node requests the IP address(es) via RRC from the IAB-donor-CU, where a number of addresses is requested for a specific usage: F1-U, F1-C and non-F1. The IAB-donor-CU may initiate the IAB TNL Address Allocation procedure towards the IAB-donor-DU to request the IP address(es). The IAB-donor-CU send the allocated IP address(es) to the IAB-node via RRC.

The entity in charge of IP address allocation (i.e. IAB-donor-CU/DU or the OAM) indicates the usages of allocated IP address(es). An IAB-node may be allocated full IPv4 address(es) and/or full IPv6 address(es) and/or an IPv6 prefix, where each IAB-node under one IAB-donor-DU receives a unique IPv6 prefix.

In case of OAM-based IP address allocation, before F1 transport has been set up, the IAB-node informs the IAB-donor-CU via RRC about its allocated IP address(es).

For both OAM-based and IAB-donor-based IP address allocation, the knowledge of allocated IP address(es) and their respective usage(s) are used by the IAB-donor-CU to configures the IAB-donor-DU with the mapping between IP header field(s) (IP address and/or DSCP and/or IPv6 flow label can be used) and the corresponding DL BAP Routing ID(s). The configured mapping in the IAB-donor-DU may be based on the full IPv4 and/or IPv6 address(es) and/or IPv6 prefix assigned to an IAB node, where the full IPv6 address takes precedence over the corresponding prefix.

The IAB’s IP address(es) can be updated using DL RRC signalling.

-------------------------------------------End of changes-------------------------------------------

# Comments

IAB network does not a mode of IPSec tunnel mode

is this referred to below sections?

The intention for this change is that:

IP address request via RRC is not necessarily combined with IP address request via F1AP.

CU may request a list of IP address from DU before any IAB connected, or when an IAB is connected.

Again, the CU may get the IP address from DU early. So no need to bind the IAB's request together with the CU's request.

This section is only about Donor-based IP address allocation, so it is not "may"

already covered by last sentence.

IAB donor DU cannot indicate the usage to IAB node

This may not necessary, and not agreed.

e.g. IAB node only report IP address for F1-C to CU, CU configures DL mapping for this IP address.

CU recognize the IP address for F1-U when F1-U tunnel is established and configure DL mapping related to this IP address then.

Routing ID is base on the IP header, not just the IP address. use the same text as integration section.

This sentence is not clear, it looks like one filed (e.g. the DSCP or flow label) can also be used to configure the mapping to the BAP routing ID.