3GPP TSG-RAN WG3 #107bis-e	R3-202560

20-30 April 2020

Online

Agenda Item:	8.3

Source:	Huawei

Title:	Summary of offline discussion on HO without SN config query

Document for:	Approval

# Introduction

This is the summary of offline discussion for the following CB:

CB: # 91_HO_without_SN_config_query

-  no CR agreeable at this time

- summarize company positions on this issue

- attempt if agreeable a reply to RAN2 (2457 as basis)

(HW - moderator)

Summary of offline disc R3-202560

reply LS R3-202561

# For the Chairman’s Notes [TBD]

Propose the following:

R3-202561 - agreed

Propose to capture the following:

xxx

# Discussion

In RAN2 #108 meeting, the summary of e-mail discussion [107bis#33][NR R15] Exchanging used IDs of SN terminated DRBs [1] was discussed online and the following agreements were achieved:

RAN2 confirms that for handover, there is a need to allow the source MN to indicate to the target MN that up-to-date information is not available for a list of DRBs, which are in use or potentially in use by the SN. Assume to send an LS to R3 to ask for signalling solution.

In the LS [2] from RAN2, the scenarios and the related requirement on RAN3 are listed. During last RAN3 meeting, this issue was discussed and the summary of offline was provided in [3].

## Issue 1

Whether the issue raised by RAN2 about not having up-to-date configuration of SN terminated bearers during handover should be solved?

| Company | Y/N | Comment |
| --- | --- | --- |
| HW | Y | As summarized in [1], it would either cause mismatch between the DRB configurations for the UE and network, or an invalid configuration for the UE. The way to solve this issue is by releasing all the SN DRBs, and the proposed solution is to let the source MN indicate to the target MN the list of DRB IDs of SN terminated bearers, which means the DRB IDs list can be explicitly transferred over the network interfaces. Furthermore, we don’t agree on the saying in the response paper that release of the SN terminated bearers is a wrong approach. The assumption of reasonable implementation may not be applicable for all. |

## Issue 2

Does the problem also need to be addressed for EN-DC?

| Company | Y/N | Comment |
| --- | --- | --- |
| HW | Y | It is true that the DRB information is included in the exchange between MN and SN, but the info is not transferred between source eNB and target eNB in this case. So X2 signaling change is still needed. |

## Issue 3

In which release does company think the solution can be taken into account?

| Company | Comment |
| --- | --- |
| HW | To align with RAN2’s LS, it is better to have the changes starting from R15. We keep open for R16 or onwards. |

# Conclusion, Recommendations

The draft reply LS is in R3-202561.

# References

- R2-1915570, Summary of E-mail discussion [107bis#33][NR R15] Exchanging used IDs of SN terminated DRBs, Huawei, HiSilicon.

- R2-1916622, LS on handover without SN configuration query, RAN2.

- R2-1911824, AS-ConfigNR at handover with (NG)EN-DC, Ericsson.