3GPP TSG-RAN WG3 Meeting #107bis-e	Draft R3-202585

# Online, 20th – 30th April 2020

Agenda Item:	9.3.8.1

Source:	Ericsson

Title:	Summary of offline discussion for E-RAB_ID_in_mod_procedure

Document for:	Approval

# Introduction

CB: # 98_E-RAB_ID_in_mod_procedure

-  Can a compromise solution be agreed? (any one?)

- if no compromise is agreeable, liaise SA2?

(E/// - moderator)

# For the Chairman’s Notes

TBD

# Discussion

There are two solutions proposed at this meeting

Solution 1: To introduce an explicit indicator, to indicate when the IE is “revoked”

Solution 2: to specify a rule, that for the concerned object to be modified, the complete configuration is provided. i.e. the receiver overwrites the related information received early.

Note: There are different wording proposed in [2], [8]. We can leave out the implementation details for now, the principle is the same, it is Solution 2.

Question 0: Which solution do you prefer?

(The company view according to the contribution are registered already)

| Company | Support for Solution 1: Explicit revoke indication, impact ASN.1 | Support for Solution 2: Procedural Text, no indication, no ASN.1 change |
| --- | --- | --- |
| Ericsson |  | YES |
| ZTE |  | YES |
| NOKIA | YES | YES, as compromise solution. The procedural text differs. |
| Huawei | YES |  |

The next question I would like to ask is if it is possible to agree on Solution 2 for you, with different wording, different rules? No explicit indicator is included.

Question 1: Is it possible to agree on Solution 2, with different wording, different rules, all to avoid introducing explicit revoking indication?

This question is only for the company who has not indicate support to Solution 2.

| Company | Comments |
| --- | --- |
| Huawei | We do not prefer solution 2 due to: Solution 2 requires to include all the QoS flow information (QoS Flow Identifier/QoS Flow Level QoS Parameters/E-RAB ID per QoS flow) to revoke e.g. only one E-RAB ID from only one QoS flow. Clearly this is not an efficient way. Solution 2 is an “overall rewrite” operation for a big IE (IE list) for UE-associated modification message. This is not seen in related specifications, and is not a normal way (the normal way is to modify a single IE, then only modify the IE, not anything else). |

Similarly I ask the same question for Solution 1.

Question 2: Is it possible to agree on Solution 1?

This question is only for the company who has not indicate support to Solution 1.

| Company | Comments |
| --- | --- |
| Ericsson | We do not prefer solution 1 for the below reasons: The solution 2 is much simpler for the sender and the receiver, just send and receive the complete information; There is no ASN.1 impact. |

If we are still in difficult to agree on ONE solution, then I would like to understand in your view, how liking the problem (revoking E-RAB ID) will occur.

Question 3: do you think the case of revoking the E-RAB ID is a common case/rare case?

| Company | It is a common case because … | It is a rare case because … |
| --- | --- | --- |
| Nokia |  | Should not be frequent. |
| Huawei | Depending on the detailed scenario, and can be case by case. | Depending on the detailed scenario, and can be case by case. |
| Ericsson |  | We think it is rare case. |

If we could not conclude at this meeting a solution, do you prefer to involve the other group, i.e. send LS to SA2, if so I could draft such LS.

Question 4: If we could not conclude, should we involve the other group, i.e. send LS to SA2?

| Company | Comments |
| --- | --- |
| Nokia | We should not drag on forever such kind of topics. We propose to agree R3-201963 and if not agreeable then R3-201757. |
| Huawei | No need to involve other groups. We propose to agree R3-201963. |
| Ericsson | We have no strong wish to involve SA2 either. If a solution needs to be agreed, it should be solution 2, |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-201756	Correction of revoke E-RAB ID, Nokia, Nokia Shanghai Bell

R3-201757	Correction of revoke E-RAB ID, Nokia, Nokia Shanghai Bell

R3-201758	Correction of revoke E-RAB ID, Nokia, Nokia Shanghai Bell

R3-201962	E-RAB ID revocation in modification procedure, Huawei

R3-201963	E-RAB ID revocation in modification procedure, Huawei

R3-201964	E-RAB ID revocation in modification procedure, Huawei

R3-202111	Discussions on handling E-RAB ID in Modification Procedure, Ericsson

R3-202024	Handling the IE in the modification messages, Ericsson, ZTE

R3-202026	Handling the IE in the modification messages, Ericsson, ZTE