3GPP TSG-RAN WG3 #107bis-e	R3-20XXXX

Online, 20th – 30th April 2020

Title:	[Draft] LS on AS rekeying handling

Response to:	-

Release:	Rel-15

Work Item:	NR_NewRAT-Core

Source:	CATT (To be RAN3)

To:	SA2, SA3

Cc:

Attachment:

Contact Person:

#### Name:	LIU Aijuan

E-mail Address:	liuaijuan (at) catt (dot) cn

1. Overall Description:

RAN3 discussed the behaviour of NG-RAN node if it receives one NGAP UE CONTEXT MODIFICATION REQUEST message that includes both the Security Key IE and the Emergency Fallback Indicator IE.

From RAN3 point of view, if the NG-RAN node performs the AS rekeying procedure as the highest priority, the emergency fallback will be delayed. Therefore it should be beneficial for the NG-RAN node to ignore the Security Key IE and only perform emergency fallback in this case.

From NGAP protocol, the IEs mentioned above are all optional and could be present in one message.

However, RAN3 is not sure whether such case is possible to happen, considering the AMF is possible to halt the trigger for AS rekeying (i.e. to decide not to include the Security Key IE) when it requests the NG-RAN node to perform emergency fallback.

Besides, RAN3 understands that AS re-keying procedure could be initiated by AMF via either UE CONTEXT MODIFICATION REQUEST message or PATH SWITCH REQUEST ACKNOWLEDGE message. One issue discussed in RAN3 is whether it should be supported for the NG-RAN node to inform the AMF of the re-keying failure in either of the two cases.

## 2. Actions:

ToSA3：

ACTION: RAN3 respectfully asks SA3 to feedback whether it is acceptable for the network to give up the AS re-keying procedure and only initiate the emergency fallback procedure when the two procedures collide.

Besides, RAN3 would like to ask SA3 to feedback whether it should be supported for the NG-RAN node to inform the AMF of the re-keying failure when NG-RAN node received an AS re-keying request via either UE CONTEXT MODIFICATION REQUEST message or PATH SWITCH REQUEST ACKNOWLEDGE message.

To SA2:

ACTION: RAN3 respectfully asks SA2 to feedback whether the case that both the Security Key IE and the Emergency Fallback Indicator IE are included within one NGAP UE CONTEXT MODIFICATION REQUEST message is abnormal or not

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #108-e	1st – 12th June 2020	Online

TSG-RAN3 Meeting #109	24th – 28th August 2020	Toulouse, France