3GPP TSG-RAN WG3 #107bis-e	R3-20XXXX

Online, 20th – 30th April 2020

Title:	[Draft] LS on AS rekeying handling

Response to:	-

Release:	Rel-15

Work Item:	NR_NewRAT-Core

Source:	CATT (To be RAN3)

To:	SA2, SA3

Cc:

Attachment:

Contact Person:

#### Name:	LIU Aijuan

E-mail Address:	liuaijuan (at) catt (dot) cn

1. Overall Description:

RAN3 discussed the behaviour of NG-RAN node if it receives one NGAP UE CONTEXT MODIFICATION REQUEST message including both the Security Key IE and the Emergency Fallback Indicator IE. From RAN3 point of view, if the NG-RAN node performs the AS rekeying procedure at the highest priority, the emergency fallback will be delayed. Therefore it may be beneficial for the NG-RAN node to ignore the Security Key IE for this case, which needs to be fed back to the core network.

However, RAN3 is not sure whether such case is possible to happen, considering the AMF is possible to halt the trigger for AS rekeying (i.e. to decide not to include the Security Key IE) when it requests the NG-RAN node to perform emergency fallback.

## 2. Actions:

To SA2/SA3:

ACTION: RAN3 respectfully asks SA2/SA3 to inform RAN3 whether there is a case that both the Security Key IE and the Emergency Fallback Indicator IE are included within one NGAP UE CONTEXT MODIFICATION REQUEST message, and if such case exists, how the NG-RAN node should react.

3. Date of Next TSG-RAN3 Meetings:

TSG-RAN3 Meeting #108-e	1st – 12th June 2020	Online

TSG-RAN3 Meeting #109	24th – 28th August 2020	Toulouse, France