3GPP TSG-RAN WG3 #107bis-e	R3-202487

20-30 April 2020

Online

Agenda Item:	14.3.2.2

Source:	Huawei (Moderator)

Title:	Summary of Offline Discussion on NBIOT-MTC4_Email_MTC_Inactive

Document for:	Approval

# Introduction

This paper provides the Summary of Offline Discussion on NBIOT-MTC4_Email_MTC_Inactive:

CB: # NBIOT-MTC4_Email_MTC_Inactive

-  include eDRX cycle in NGAP: Core Network Assistance Information for RRC INACTIVE IE? (Huawei, Nokia, Nokia Shanghai Bell, CMCC )

- extend XnAP Paging DRX IE used in RAN Paging, with new values 512rf and 1024rf ?  (Huawei, Nokia, Nokia Shanghai Bell, CMCC)

- rev if needed; check details

(HW - moderator)

Summary of offline disc R3-202487

# For the Chairman’s Notes

R3-201684 agreed

R3-201685 endorsed, as eMTC XnAP BL CR.

# Discussion [if needed]

There are two papers submitted on this topic, with one NGAP TP to BL CR#0172, and one XnAP CR:

| R3-201684 | (TP to BL CR#0172 “Introduction of eMTC connected to 5GC” for TS38.413) Paging aspects for RRC_INACTIVE state (Huawei, Nokia, Nokia Shanghai Bell, CMCC) | other |
| --- | --- | --- |
| R3-201685 | Introduction of eMTC connected to 5GC (Huawei, Nokia, Nokia Shanghai Bell, CMCC) | CR0343r, TS 38.423 v16.1.0, Rel-16, Cat. B |

## Issue 1 [NGAP TP]

In R3-201684, TP is provided to include eDRX cycle in NGAP: Core Network Assistance Information for RRC INACTIVE IE.

Please companies provide your view and comment (if any) on the TP R3-201684.

| Company | Comment |
| --- | --- |
| Huawei | Agree the TP provided in R3-201684 to BL CR#0172 “Introduction of eMTC connected to 5GC” for TS38.413 |
| Nokia | Same as Huawei. |
| Qualcomm | Looks fine, one minor comment is whether to add something in the semantics noting that this is for MTC UEs, but no strong view. |
| ZTE | Agree with the TP, which matches the RAN2 agreement. |

## Issue 2 [XnAP CR]

In R3-201685, CR is provided to extend XnAP Paging DRX IE used in RAN Paging, with new values 512rf and 1024rf.

Please companies provide your view and comment (if any) on the CR R3-201685.

| Company | Comment |
| --- | --- |
| Huawei | Endorse the CR as eMTC XnAP BL CR. |
| Nokia | Same as Huawei. |
| Qualcomm | Fine to endorse CR as BL. |
| ZTE | Agree with the TP, which matches the RAN2 agreement. |

# Conclusion, Recommendations [if needed]

If needed

//to be updated

# References

R3-201684 (TP to BL CR#0172 “Introduction of eMTC connected to 5GC” for TS38.413) Paging aspects for RRC_INACTIVE state (Huawei, Nokia, Nokia Shanghai Bell, CMCC)

R3-201685 Introduction of eMTC connected to 5GC (Huawei, Nokia, Nokia Shanghai Bell, CMCC)