3GPP TSG-RAN WG3 #107bis-e	R3-202546

20-30 April 2020 Online

Agenda Item:	16.4

Source:	Huawei (Moderator)

Title:	Summary of Offline Discussion on NPN mobility

Document for:	Approval

# Introduction

CB: # 31_Email_PRN_mobility_inactive

- Access verification:

The new NG-RAN node should verify whether the UE access is allowed (LG,HW)

New or old NG-RAN node verify the UE access to the CAG cell in the case of RNAU with or without UE context relocation, respectively (NEC)

No matter whether the UE  context retrieval is successful or not , the last serving (old) NG-RAN node performs CAG access control, e.g., verifying the access by checking exchanged cell supported CAG information between nodes (ZTE,SS)

- For RNAU without UE Context relocation, in case of UE access verification success at the old (last serving) NG-RAN, the old NG-RAN node:

Responds to the new (target) NG-RAN node with the Retrieve UE Context failure message and keeps the UE in RRC inactive state (NEC,HW)

Informs the CN of the failure by sending the UE Context Release Request message to the AMF, including an appropriate cause value, and release the UE (NEC)

- The cell supported NID and cell supported CAG List are not included into the RETRIEVE UE CONTEXT REQUEST message? (LG)

- In this release, the RNA should be configured within the serving SNPN? (LG)

- Reuse the cause values “PNI-NPN access denied” and “SNPN access denied” for mobility (same as for access control)? (Nok)

- Introduce a cause value “CAG ID invalid” for RRC resume procedure? (ZTE,HW)

- st2 aspects? (HW,LG)

(HW - moderator)

Summary of offline disc R3-202512

# For the Chairman’s Notes

Propose the following (TBD):

# Discussion

## Access verification for inactive UE

This was discussed at last RAN3#107-e meeting with the following summary.

- For mobility in inactive state, there seems to be various opinions where the checks are to be done, in fact depending on the scenario. On the other hand, many companies are not convinced that we need to add signaling for this (e.g. addition of new NPN information in the UE Context Retrieval). Therefore, at this stage the status quo seems to prevail i.e. do nothing at this stage. Of course, topic is not closed and to be continued contribution driven at next meeting.

Several contributions as seen in the section 5 further discuss this issue. In order to proceed, it is better to start with the simple questions.

There is a proposal for new NG-RAN to send the NPN information to old NG-RAN in RETRIEVE UE CONTEXT REQUEST message. While another proposal is that cell supported NID and cell supported CAG List are not included into the RETRIEVE UE CONTEXT REQUEST message.

Question 1.1: for mobility in inactive state, should the NPN broadcast information is included in RETRIEVE UE CONTEXT REQUEST to the last serving NG-RAN node?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | No | The cell supported NPN information is already exchanged in Xn interface messages. |
| Nokia | No | Same as above. |
| LG | No | Same as above |
| ZTE | No | In current XnAP specification, the list of cell supported CAG IDs of the NG-RAN node is exchanged between NG-RAN nodes during the Xn interface setup/update procedure. |
| Qualcomm | No | Same as above |
| Ericsson | No |  |
| Samsung | Yes | Can transfer the latest information in the RETRIEVE UE CONTEXT REQUEST information, then old can perform the verification. |
| CATT | No |  |

Question 1.2: for mobility in inactive state, should the last serving NG-RAN node performs access control check upon the reception of RETRIEVE UE CONTEXT REQUEST?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | The last serving NG-RAN node can perform access control based on: the NPN restriction information in MRL, and the new cell supported NPN information. If access fails, the last serving NG-RAN node can send the UE to be idle state. |
| Nokia | Yes | Same as above. |
| LG | Yes | Both nodes perform access control check. |
| ZTE | Yes | In the case of UE context retrieval success, the old NG-RAN node can perform access control by checking exchanged cell supported CAG information between nodes. In the case of old NG-RAN node rejects the UE context retrieval procedure, only the old NG-RAN node can verify the UE access. |
| NEC | Yes | As we mentioned in R3-201760, both the new NG-RAN node and the last serving NG-RAN node can verify the UE access to the CAG cell, depending on the outcome of the UE context retrieval procedure. In the case of UE access failure, at the last serving NG-RAN, the last serving NG-RAN node needs to inform the CN of the access failure, and release the UE. |
| Qualcomm | Yes | This seems business as usual, would expect both nodes to perform some checking, and for sure the old node still has the same function as a handover source node. |
| Ericsson | Yes |  |
| Samsung | Yes |  |
| CATT | Yes for initial check | The last serving NG-RAN node may not get the updated cell supported NPN information if NPN broadcast information is not included in RETRIEVE UE CONTEXT REQUEST. So, the access control by last serving NG-RAN node may not be correct. Propose the new node to perform final access control. |

Question 1.3: for mobility in inactive state, should the new NG-RAN node performs access control check upon the reception of RETRIEVE UE CONTEXT RESPONSE?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | We think it is reasonable for the new NG-RAN node to check again and decides whether the state transition is needed by itself. |
| Nokia | No | It is not clear why the new NG-RAN node should re-check again. This additional check could be put FFS. |
| LG | Yes | Same view with Huawei |
| ZTE | No | For simple procedure, no matter whether the UE context retrieval is successful or not, the old NG-RAN node performs CAG access control. |
| NEC | Yes | The new NG-RAN node can verify the UE access to the CAG cell in the case of UE context relocation. |
| Qualcomm | Maybe | We do not specify in handover that the target checks; this is basically the same. It can, but we do not have to specify this. |
| Ericsson | Yes | However, the “yes” does not advocate explicit specification. Each node is responsible to get only the good joes in and leave the others out. |
| Samsung | No | If the verification is made in the old, no need to do it again. |
| CATT | Yes | New node gets the MRL for RETRIEVE UE CONTEXT RESPONSE and can perform access control check. |

Question 1.4: for mobility in inactive state, should the access control check be described in TS 38.300?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | A new section on inactive mobility can be added, e.g. see our paper in [R3-202341] |
| Nokia | Yes. | But should only describe the check in old node. |
| LG | Yes |  |
| ZTE | Partly ok. | The access control check should be described in last serving NG-RAN node rather than in target NG-RAN node. |
| NEC | Yes | As mentioned in the answer to Question 1.2, both NG-RAN nodes can perform UE access verification. So, we prefer keeping text description on both nodes in R3-202341. Additionally, we think that an indication of UE access failure to the AMF is needed. Refer to the updated text on R3-202341 (in the CB folder). |
| Qualcomm | Maybe | This is not unique to NPN. At least for example the case of forbidden TA could also happen i.e. UE surfaces in an adjacent TA that is forbidden. So if needed (and we should also check what we say about handover), we should consider whether the text should be kept general. |
| Ericsson | No for now | As already mentioned in another CB, the new NPN section deserves a thorough review, especially lines creating duplicated text. And if it turns out, that the RRC_INACTIVE chapter in 38.300 doesn’t mention any access restriction, there is no justification for an NPN variant of that story either. |
| Samsung | Maybe |  |
| CATT | no | Agree with Ericsson. |

Question 1.5: for mobility in inactive state, should the access control check be described in TS 38.423?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | This can be described in Retrieve UE Context procedure. |
| Nokia | Yes | But should only describe the check in old node. |
| LG | Yes | Add a simple sentence to refer T8.300 |
| ZTE | Yes | The same as Nokia. |
| NEC | Yes | Agree with HW. We provided the related text in R3-201761 under Retrieve UE Context procedure. The text can be updated following the conclusion in this CB, on the issue that UE access verification can be performed by both NG-RAN nodes, last serving NG-RAN node, or new NG-RAN node. |
| Qualcomm | Yes | Probably only from point of view of receiver of the first message (msg 1), and just hint that rejection may be due to mobility restrictions without needing to be more specific. So not as in 1761: what we should have is a general statement on context retrieval failure maybe with some text borrowed from handover regarding on how mobility restrictions are used. |
| Ericsson | No | The current specification does not include any specification text, so for the non-NPN case there seems to be no need for that. Why to create an exception for NPN? We are not available for such approach. Think twice! |
| Samsung | Yes | Agree with Nokia. |
| CATT | Not necessary | There is no access control description for MRL in TS 38.423 now. For NPN, maybe we could follow the similar principle. |

## Stage 2 for TS 37.340

[R3-202343] proposes to include MR-DC impact for NPN, e.g. in Secondary Node Addition, Secondary Node Change procedure.

Question 2: Should the NPN mobility in MR-DC be described in TS 37.340?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | Given that only one sentence is captured in TS 38.300 BL CR, the detailed support of NPN for MR-DC should be described in TS 37.340. R3-202343 is suggested to be taken as baseline. |
| Nokia | No | Not needed. |
| LG | No | Not needed |
| ZTE | Yes | NPN should be supported in MR-DC case. |
| Qualcomm | No | Not needed |
| Ericsson | No | No, no, no, no, … |
| Samsung | No |  |
| CATT | No |  |

## Other issues

There are proposals in [R3-201816] to reuse the cause values for NPN mobility the same as for access control. The moderator understands the exact cause values can be discussed in e.g. CB#29 so that value(s) can be reused.

Company can provide any open issue which are not covered above.

| Company | Issue and comment |
| --- | --- |
| Nokia | Cause values for NG mobility can be discussed with CB#30 (access control, Init UE message). But it is proposed to agree here tdoc R3-201817 which introduces similar cause values for Xn mobility (PNI NPN access denied, SNPN access denied). |
| ZTE | See in CB#30. PNI-NPN and SNPN access failure should be defined. For the case that UE is rejected by CAG access only cell, then the cause value “CAG access only” seems also helpful. |
| NEC | Agree with ZTE comment on introducing a cause value of CAG-only (NPN-only) access. That is why in R3-201764 we propose introducing three cause values: “Not allowed CAG access”, “Not allowed SNPN access”, and “NPN-only access”. |
| Qualcomm | We are not clear that there is any need to differentiate SNPN and PNI-NPN causes. So something like “NPN access denied” would be enough. Note there is no logical cell sharing between SNPN and PLMN/PNI-NPN, so it is never ambiguous (e.g. in terms of cell counters). |
| Ericsson | Listen to Luis! |
| Samsung | Can discuss in CB#30. |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-201760 | (TP for NPN BL CR for TS 38.413) Mobility in Inactive State in NPN (NEC) | other Proposal 1: it is proposed that the new NG-RAN node or old NG-RAN node can verify the UE access to the CAG cell in the case of RNAU with or without UE context relocation, respectively. Proposal 2: it is proposed that for RNAU without UE Context relocation: • In case of UE access verification success at the old (last serving) NG-RAN, the old NG-RAN node responds to the new (target) NG-RAN node with the Retrieve UE Context failure message and keeps the UE in RRC inactive state. • In case of UE access verification failure at the old (last serving) NG-RAN, the old NG-RAN node informs the CN of the failure by sending the UE Context Release Request message to the AMF, including an appropriate cause value, and release the UE. Proposal 3: RAN3 is kindly asked to agree the TPs to TS 38.413 (below) and TS 38.423 in [4]. |
| --- | --- | --- |
| R3-201761 | (TP for NPN BL CR for TS 38.423) Mobility in Inactive State in NPN (NEC) | other |
| R3-201816 | (TP for NPN BL CR for 38.413) Correction of NPN Mobility over NG (Nokia, Nokia Shanghai Bell) | other Proposal 1: reuse the cause value “PNI-NPN access denied” for mobility (same as for access control). Proposal 2: reuse the cause value “SNPN access denied” for mobility (same as for access control). |
| R3-201817 | (TP for NPN BL CR for 38.423) Correction of NPN Mobility over Xn (Nokia, Nokia Shanghai Bell) | other |
| R3-201921 | Mobility in inactive state (ZTE Corporation) | discussion Proposal 1 : It is proposed that no matter whether the UE context retrieval is successful or not , the last serving NG-RAN node performs CAG access control, e.g., verifying the access by checking exchanged cell supported CAG information between nodes. Proposal 2: Introducing a cause value “CAG ID invalid” for RRC resume procedure. |
| R3-201922 | Consideration on selected CAG ID (ZTE Corporation) | discussion |
| R3-201939 | Discussion on NPN manual network selection (CATT) | discussion |
| R3-202284 | Clarification on mobility of NPN (LG Electronics) | discussion Proposal 1: The manual selected CAG ID is not propagated during the connected mode mobility. Proposal 2: The new NG-RAN should verify whether the UE access is allowed. Proposal 3: The cell supported NID and cell supported CAG List are not included into the RETRIEVE UE CONTEXT REQUEST message. Proposal 4: In this release, the RNA should be configured within the serving SNPN. Proposal 5: It is proposed to agree the corresponding CR in [5]. |
| R3-202285 | (TP for NPN BL CR for TS 38.300): Consideration on RRC-INACTIVE in NPN (LG Electronics) | other |
| R3-202341 | (TP for NPN BL CR for TS 38.300): Inactive mobility for NPN (Huawei) | other Proposal 1: For PNI-NPN, The Xn Retrieve UE Context Failure can be triggered by the last serving gNB when the supported CAG List related to the serving PLMN of the target cell is not compatible with the UE’s Allowed CAG List. The target gNB can verifies the UE access taking the PNI-NPN mobility restrictions received from the last serving gNB into account. New cause value “invalid CAG ID(s)” should be introduced on NG interface. Proposal 2: For SNPN, The Xn Retrieve UE Context Failure can be triggered by the last serving gNB when the supported SNPN(s) of the target cell does not match the serving SNPN. The target gNB can verifies the UE access checking whether the supported SNPN(s) of the target cell matches the serving SNPN. Proposal 3: The selected CAG ID may be added in NGAP initial context setup, but we need to wait for SA2’s decision. |
| R3-202342 | (TP for NPN BL CR for TS 38.423): Inactive mobility for NPN (Huawei) | other |
| R3-202343 | Mobility aspets of MR-DC NPN (Huawei) | draftCRr, TS 37.340 v16.1.0, Rel-16, Cat. |
| R3-202383 | (TP for NPN BL CR for 38.423) Access control for UE Context Retrieval in NPN (Samsung R&D Institute UK) | other Proposal 1: It is proposed new NG-RAN sends NPN information to old NG-RAN in RETRIEVE UE CONTEXT REQUEST message. The old NG-RAN can make the access control based on the received information and HRL. Proposal 2: It is proposed old NG-RAN reject the UE context retrieval if the access control is failed in the old NG-RAN with proper cause value. |