3GPP TSG-RAN WG3 #107bis-e	R3-202491

20-30 April 2020

Online

Agenda Item:	14.3.2.6

Source:	Ericsson

Title:		Summary of Offline Discussion on introduction of Pending Data and UE Differentiation for UP CIoT 5GS Optimization

Document for:	Approval

# Introduction

CB: # NBIOT-MTC8_Email_Pendingdata_UEdiffer

- introduce the Pending Data Indication IE in the following NGAP messages:INITIAL CONTEXT SETUP REQUEST, HANDOVER REQUEST, PATH SWITCH REQUEST ACKNOWLEDGE, NGAP UE CONTEXT MODIFICATION REQUEST and DOWNLINK NAS TRANSPORT (with FFS)?

- introduce the UE differentiation Information IE in the following NGAP messages: INITIAL CONTEXT SETUP REQUEST, HANDOVER REQUEST, PATH SWITCH REQUEST ACKNOWLEDGE and DOWNLINK NAS TRANSPORT?

- rev if needed; check details

(E/// - moderator)

Summary of offline disc R3-202491

# For the Chairman’s Notes

Propose the following:

- (Draft) agree to TP R3-202188 [1] to NGAP BL CR 0153 Common CP/UP aspects of CIoT.

# Discussion

## Pending Data Indication

Do companies agree to introduce the Pending Data Indication IE in the following NGAP messages: INITIAL CONTEXT SETUP REQUEST, HANDOVER REQUEST, PATH SWITCH REQUEST ACKNOWLEDGE, NGAP UE CONTEXT MODIFICATION REQUEST and DOWNLINK NAS TRANSPORT (with FFS)

| Company | Comment |
| --- | --- |
| Nokia | No. Don’t see the need. |
| Huawei | Agree to introduce. |
| Ericsson | PDI is a crucial indication and NGAP should be aligned with what we have in EPS. Can Nokia please explain why they don’t see the need? |
| ZTE | Yes. We agree to align the NGAP specification to S1AP specification. |
| Nokia | The messages listed move the UE to connected state allowing transfer of the data with no problem, so I don’t understand why you need to indicate PDI to NG-RAN? |

## UE Subscription-based Differentiation

Do companies agree to introduce the UE differentiation Information IE in the following NGAP messages: INITIAL CONTEXT SETUP REQUEST, HANDOVER REQUEST, PATH SWITCH REQUEST ACKNOWLEDGE and DOWNLINK NAS TRANSPORT

| Company | Comment |
| --- | --- |
| Nokia | This is OK. |
| Huawei | Agree to introduce. Similar to S1AP, it is needed to also introduce UE differentiation Information in NGAP: CONNECTION ESTABLISHMENT INDICATION, UE INFORMATION TRANSFER messages. |
| Ericsson | Thanks for Huawei’s comment. Will ask for a tdoc revision to introduce the IE in those messages. |
| ZTE | Yes, agree. |

# Conclusion, Recommendations

The following is proposed:

- (Draft) agree to TP R3-202188 to NGAP BL CR 0153 Common CP/UP aspects of CIoT.

# References

R3-202188, Introduction of Pending data indication and UE subscription-based differentiation to support CIoT connected to 5GC, Ericsson, RAN3#107bis-e