3GPP TSG-RAN WG3 #107bis-e	R3-202521

20-30 April 2020

Online

Agenda item:		17.2.2

Source: 				CATT

Title: 	Summary of offline discussion on CB: # NRIIOT3_Email_NRIIoT_PDCPdup_ctr

Document for:		Approval

# Introduction

CB: # NRIIOT3_Email_NRIIoT_PDCPdup_ctrl

-  UL transmission for multiplication over up to 4 RLCs:

- enable signalling where the nodes coordinate which RLCs each of them controls? (Nok)

- the hosting node to decide about the split of RLCs in the UE between the nodes, fix number or coordination solution? (Nok, ZTE, HW)

- initial UL activation state of each RLC entity, and the pre-configured LCID for each RLC entity shall be indicated by assisting node via control plane signaling? (ZTE) or indicate initial RLC duplication activation state of the secondary RLC entities in reqeuset ? (HW)

- the UL duplication activation status of all RLC entities can be exchanged via user plane between two nodes? (ZTE, CATT) or the UL duplication activation suggestion and LCH ID can be exchanged via user plane between two nodes?(HW)

- exchange the Radio Quality Assistance Information/UL Radio Quality Index between two nodes? (ZTE, HW)

- each node decides its own UL RLC selection? (Nok, CATT, ZTE), or PDCP decides UL RLC selection? (HW)

-  DL transmission for multiplication over up to 4 RLCs:

- allows the hosting node to inform the assisting node about the min and max number of copies to be sent towards the UE? (Nok)

- Reuse the PDCP Duplication Activation Suggestion per RLC entity for DL Duplication coordination between two nodes? (Nok, CATT, ZTE, CMCC)

- clarification on radio quality assistance information& PDCP Duplication Activation Suggestion per DRB or per RLC entity? (HW, CMCC)

- reply LS to RAN2 on Network Coordination for UL PDCP Duplication, if agreeable? (HW, Nok)

- attempt to converge on minimum agreeable set; if so, revise/merge as needed, split work

(CATT - moderator)

Summary of offline disc R3-202521

This contribution will initial the email discussion and summarize the status of this discussion during the meeting.

The email discussion owner would like to trigger email discussions as below steps:

- Summarize the contributions which are submitted in section 17.2.2 in the meeting agenda.

- Group the topic and analysis the solutions

- For the issues on which we have same view from all the contributions, directly give out the agreement proposal

- For the issues on which we have different view, list all the solutions and questions for discussion.

- Converge the different the solutions during the email discussion, if get agreement, convert to agreement proposal.

- If we cannot get the convergence for the difference, we will leave them as open issues.

In this email discussion, we try to get the agreement for the solutions for all topics. Companies are welcome to provide answer for the questions by Apr. 23, 13:00 UTC. We can make the second version base one the answers. We may optimize the topic in the second version for further discussion and finish the discussion by Apr. 27, 13:00 UTC. Then we can make the agreement proposal for the TP generation and work split base on the discussion. So we may have one day to modify the TPs base on the discussion summary before the CB deadline Apr. 28, 13:00 UTC.

# For the Chairman’s Notes

Propose the following:

TBD

Propose to capture the following:

TBD

Issue 1: no consensus

TBD

# Discussion

## Summarize the contributions

#### DL Duplication

The proposal for DL duplication coordination is list as below:

| Item No. | Topic | Proposal | Spec impact | Message/PDU | Company |
| --- | --- | --- | --- | --- | --- |
| 1-1 | 1.DL Activation RLC quantity suggestion | The hosting node to inform the assisting node about the min and max number of copies to be sent towards the UE | 38423 |  | Nok |
| 1-2 | 2.DL PDCP Duplication Activation Suggestion | DL PDCP Duplication Activation Suggestion per DRB in one DATA frame | 38425 | ASSISTANCE INFORMATION DATA | CATT |
| 1-3 |  | Add Indication per RLC entity for PDCP duplication activation suggestion | 38425 | ASSISTANCE INFORMATION DATA | HW,CMCC |
| 1-4 | 3.DL radio quality assistance information | Add Indication per RLC entity for the corresponding node signal the DL radio quality assistance information to host node | 38425 | ASSISTANCE INFORMATION DATA | HW,CMCC |

Totally there are tree topics touched by the contributions. Item 1-2 and item 1-3 point to one topic but different solution is provided

Please give your comments for these topics in the below tables:

- Item No. 1-1 DL Activation RLC quantity suggestion

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| CMCC | No | In DL, we support the hosting node to perform duplication based on following observations: -For DL duplication, the four-tunnel option can provide better reliability performance than two-tunnel option. -For DL duplication, compared to four-tunnel option, re-transmitted packets will delay the fresh data with higher possibility for two-tunnel option. -For a DRB including both DL and UL traffics, the DL traffic will be delayed due to the latency increase of UL traffic by using two-tunnel option. -The DL overhead increase introduced by additional tunnels on related interface is not the bottleneck of the network. Therefore, there’s no need to signal max and min copies in DL for the hosting node. |
| ZTE | NO | PDCP duplicates copies and sends the duplicated PDCP PDU to the RLC hosting node, so there is no need to inform the assisting node how much copies shall be duplicated. |
| Nokia | Yes | This allows the assisting node to activate/deactivate multiplication much faster and with greater accuracy. Thus the efficiency of resource utilization will be highly improved. As it concerns delays, as discussed elsewhere, we are somewhat surprised why retransmission of a single copy of the PDU would cause additional delays on the interface? |

- Item No. 1-2 and item No.1-3  DL PDCP Duplication Activation Suggestion

| Company | Support (item1-2/ item 1-3) | Comment |
| --- | --- | --- |
| CMCC | Item 1-3 | Item 1-3 is a solution that can solve the backward compatibility issue. |
| ZTE | 1-3 | It is benefit to include UL activation status of all RLCs in one ASSISTANCE INFORMATION DATA frame to construct the synchronized MAC CE for UE at both nodes with low-latency, but it is not necessary to include the DL duplication suggestion of all RLCs in one frame. |
| Nokia | - | Not needed if the DL control mechanism as discussed above is introduced. |

- item No.1-4 DL radio quality assistance information

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| CMCC | Yes | If we could agree that DL radio quality index should be provided as per RLC entity, this solution can be supported. |
| ZTE | YES |  |
| Nokia | Yes | This is useful even with the mechanism above – it helps the hosting node to decide how many RLCs may be allowed to tbe used in DL in the assisting node. |

#### UL Duplication

The proposal for UL duplication coordination is list as below:

| Item No. | Topic | Proposal | Spec impact | Message/PDU | Company |
| --- | --- | --- | --- | --- | --- |
| 2-1 | 1.Which node control the UL duplication activation of RLC entity | The hosting node split and signalling the information of RLC controlled by sending node. | 38423 |  | Nok |
| 2-2 | 2.UL Activation RLC quantity suggestion | The maximum/minimum number of activated RLC entities used for PDCP UL duplication | 38423 |  | ZTE |
| 2-3 | 3.Initial UL activation state sent by assisting node | Initial UL activation state of each RLC entity, and the pre-configured LCID for each RLC entity shall be indicated by assisting node | 38423/38473/38463 |  | ZTE |
| 2-4 | 4.Initial UL activation state sent by Hosting node | initial RLC duplication activation state of the secondary RLC entities and the number of the secondary RLC entities in PDCP hosting gNB | 38423/38473/38463 |  | HW |
| 2-5 | 5.Exchange UL PDCP Duplication Activation state | UL PDCP Duplication Activation Flag by Host node and assist node | 38425 | DL USER DATA/ ASSISTANCE INFORMATION DATA | CATT |
| 2-6 |  | UL RLC activation selection information exchanged between two nodes | 38425 | DL USER DATA/ ASSISTANCE INFORMATION DATA | ZTE |
| 2-7 | 6.UL PDCP Duplication Activation Suggestion | Add Ind. per RLC and LCH ID in the ASSISTANCE INFORMATION DATA and resue the bit of DL PDCP Duplication Activation Suggestion UL PDCP Duplication Activation Suggestion and LCH ID in the DL USER DATA (PDU Type 0)from CU to DU in case of CU-DU split | 38425 | DL USER DATA/ ASSISTANCE INFORMATION DATA | HW |
| 2-8 | 7.Exchange UL Radio Quality Index | exchange UL Radio Quality Index information between two nodes | 38425 | DL USER DATA | ZTE |
| 2-9 | 8.Per RLC entity Assistance info | Add UL Assistance Info. Ind per RLC and LCH ID in the ASSISTANCE INFORMATION DATA (PDU Type 2). | 38425 | ASSISTANCE INFORMATION DATA | HW, |
| 2-10 |  | Add the Radio Quality Assistance Information and LCH ID in the DL USER DATA (PDU Type 0).from the CU to the DU | 38425 | DL USER DATA | HW |
| 2-11 |  | Assistance Information per RLC | 38425 | ASSISTANCE INFORMATION DATA | Nok |

Totally there are 8 topics discussed by the contributions. Topic 8 and topic 5 have different view about the solution. For other topic, there is only one contribution provided

Please give your comments for these topics in the below tables:

- Which node control the UL duplication activation of  RLC entity

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| CMCC | No | We are concerned about the progress if this solution is adopted since it needs coordination with RAN2, and may impact the progress of RAN2. |
| ZTE | NO | Each RLC hosting node, e.g., MN or SN may decide UL RLC activation for its own cell group. |
| Nokia | RAN3 must address the issue | This is not optional RAN3 feature – we received an LS from RAN2 at #107-e asking us to enable the mechanism. Without addressing it, UL multiplication will not work at all. |

- UL Activation RLC quantity suggestion

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| ZTE | Yes | In order to ensure that UL coordination can be carried out in an efficient and low-latency manner, Partial coordination solution shall be selected for UL coordination, i.e., the maximum/minimum number of activated RLC entities used for PDCP UL duplication shall be configured for each node, and each node may decide the exact RLC selection for its own cell group. |
| Nokia | No | This is not enough. According to the LS received at #107-e, RAN2 expects RAN3 to enable a mechanism that allows the hosting and the assisting nodes to use the same set of RLCs in the UE, controlled with a single MAC CE value. Even though such mechanism is not feasible, RAN3 still has to enable some form of coordination of MAC CE setup. Plain max/min values do not help, because they do not tell which exactly RLCs in the UE are under the control of the assisting node. |

- Initial UL activation state sent by assisting node

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| CMCC | No | Following similar mechanism as in R15. |
| ZTE | YES | The initial UL state is associated for each RLC entity, When the PDCP hosting node requests to establish a DRB at assisting node, the PDCP hosting node does not yet know the LCID of the every RLC established at the assisting node, also don’t know which RLC is the primary RLC. (At least, the primary path shall be activated if UL duplication is applied), so the hosting node cannot sign the initial UL activation state to assisting node. The initial activation state of each RLC entity, and the pre-configured LCID for each RLC entity shall be decided and sent by assisting node. |

- Initial UL activation state sent by Hosting node

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| CMCC | Yes | Following similar mechanism as in R15. |
| ZTE | NO | The answer is same as Question3 |

- Exchange UL PDCP Duplication Activation state

This question includes two parts. Please answer in turn.

| Company | Support (Yes/No)? Which one prefers (2-5/2-6)? | Comment |
| --- | --- | --- |
| ZTE | YES, No strong opinion for 2-5/2-6 | It is OK for us to use separate bit to indicate every RLC UL state, or to indicate all RLCs UL state in a flag field. |

- UL PDCP Duplication Activation Suggestion

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| ZTE | NO | In HW R3-202325, “The ASSISTANCE INFORMATION DATA frame may include the PDCP Duplication Activation Suggestion for uplink, which informs the node hosting the NR PDCP entity of the suggestion from the corresponding node on whether to activate or not activate UL PDCP duplication for the corresponding LCH ID. The node hosting the NR PDCP entity may take this information into account to take a decision on whether to activate or not activate UL PDCP duplication for the corresponding LCH ID.” Therefore, we need to discuss whether the node hosting PDCP decides the selection of UL RLC (centralized control, full coordination) or whether the node hosting RLC decides the selection of UL RLC of its own cell group (de-centralized control, partial coordination). From our point of view, In order to ensure that UL coordination can be carried out in an efficient and low-latency manner, partial coordination solution shall be selected. |

- Exchange UL Radio Quality Index

| Company | Support(Yes/No) | Comment |
| --- | --- | --- |
| CMCC | Yes | It may help the other node to make better decision on number of copies needed to be transmitted in UL. |
| ZTE | YES | The UL Radio Quality information for one node can help the other node make a better decision on UL RLC selection. |

- Per RLC entity Assistance info

This question includes three parts. Please answer in turn.

| Company | Support (Yes/No)? Which one prefers (2-9/2-11)? Is item 2-10 needed? | Comment |
| --- | --- | --- |
| CMCC |  | Our understanding is that 2-11 is a solution intended for DL. |
| ZTE | YES, prefer 2-9 (but LCID not needed), 2-10 is needed ( we think only UL radio quality index is needed at this stage) |  |
| Nokia |  | Same as CMCC. Also, please note, that any signaling concerning the RLCs used for UL shall not be done over the user plane, where PDUs may be lost! |

# Conclusion, Recommendations

If needed

# References

- R3-201664	Coordination of UL and DL transmission for multiplication over up to 4 RLCs	Nokia, Nokia Shanghai Bell

- R3-201665	(TPs for NR_IIoT BL CRs for TS 38.423): Enabling coordination for DL and UL multiplication over up to 4 RLCs	Nokia, Nokia Shanghai Bell

- R3-201666	(TPs for NR_IIoT BL CRs for TS 38.425): Enabling assistance information for DL coordination of the multiplication over up to 4 RLCs	Nokia, Nokia Shanghai Bell

- R3-201667	Response LS on Network Coordination for UL PDCP Duplication	Nokia, Nokia Shanghai Bell

- R3-201699	(TP for Introduction of NR_IIOT support to TS 38.423) PDCP duplication coordination	ZTE

- R3-201700	(TP for Introduction of NR_IIOT support to TS 38.473) PDCP duplication coordination	ZTE

- R3-201701	(TP for Introduction of NR_IIOT support to TS 38.463) PDCP duplication coordination	ZTE

- R3-201702	(TP for Introduction of NR_IIOT support to TS 38.425) PDCP duplication coordination	ZTE

- R3-201952	Discussion on Dynamic control of PDCP Duplication	CATT

- R3-201953	(TP for [NR_IIOT] BL CR for TS 38.425)Discussion on Dynamic control of PDCP Duplication	CATT

- R3-202321	(TP for NR_IIOT BL CR for TS 38.423): PDCP duplication with more than 2 entities	Huawei

- R3-202322	(TP for NR_IIOT BL CR for TS 38.463): PDCP duplication with more than 2 entities	Huawei

- R3-202323	(TP for NR_IIOT BL CR for TS 38.473): PDCP duplication with more than 2 entities	Huawei

- R3-202324	(TP for NR_IIOT BL CR for TS 38.425): Assistance information for DL PDCP duplication with more than 2 entities	Huawei, CMCC

- R3-202325	(TP for NR_IIOT BL CR for TS 38.425): Dynamic control of UL duplication- activation suggestion	Huawei

- R3-202326	(TP for NR_IIOT BL CR for TS 38.425): Dynamic control of UL duplication - assistance information	Huawei

- R3-202327	[DRAFT] Reply LS on coordination for UL duplication	Huawei

- R3-202437	Dynamic control of PDCP duplication	China Mobile International Ltd