3GPP TSG-RAN WG3 #107bis-e	R3-202523

20-30 April 2020 Online

Agenda Item:	17.2.4.1

Source:	Huawei (Moderator)

Title:	Summary of Offline Discussion on NRIIoT Stage2

Document for:	Approval

# Introduction

CB: # NRIIOT5_Email_NRIIoT_HLmulticonn_st2

-  whether stage2 BL CR for TS37.340 is needed?

- if agreeable, check details and revise as needed

(HW - moderator)

Summary of offline disc R3-202523

# For the Chairman’s Notes

Propose the following (TBD):

# Discussion

## Whether the stage2 BL CR for TS37.340 is needed?

Currently in the BL CR for TS 38.300, the two higher layer multi-connectivity solutions are captured as follows.

- 16.1.x.1 Redundant user plane paths based on dual connectivity

- 16.1.x.2 Redundant data transmission via single UPF and single RAN node.

Companies can first discuss: whether the BL CR for TS 37.340 is needed or not.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Huawei | Yes | Generally we thinks for URLLC services and TSC communication, the TS 37.340 needs to capture the basic impacts on MR-DC. For example, The higher layer solution 1 relies much on RAN dual-connectivity to establish user plane paths, which should be specified in TS 37.340 specifically targeting the MR-DC operations. Also the solution 2 has impact on MR-DC. Note that even for RAN sharing, there are general descriptions in section 11.2 of TS 37.340 (E-UTRAN and NG-RAN aspects of network sharing are specified in TS 36.300 [2] and TS 38.300 [3].). Then following the same logic, it should also capture MR-DC support of URLLC/TSC. |

## How the stage2 BL CR for TS37.340 is organized?

[1] proposes to add multiple connectivity descriptions in the following sections and procedures.

- In SN addition procedure, and PDU session split procedure;

- In section 11 on service related aspects.

11 Service related aspects …… 11.4 Higher layer multi-connectivity for URLLC sevices NG-RAN aspects of higher layer multi-connectivity for URLLC services are specified in TS 38.300 [3].

If the answer to section 3.1 is yes, company can provide comments how the descriptions are organized.

Companies’ views can be provided in the following Table.

| Company | Comment |
| --- | --- |
| Huawei | It is suggested to take R3-202329 as baseline. The basic functions to support URLLC and TSC for MR-DC can be specified in section 11Service related aspects And in the detailed procedures, the two higher layer solutions can be specified accordingly. |

# Conclusion, Recommendations [if needed]

If needed

# References

- R3-202329 Higher layer duplication for TS 37.340,  Huawei