| 3GPP TSG RAN WG3 Meeting #11 | Document | R3-000888 |
| --- | --- | --- |
| Nice, France, 28th Jan-3rd Mar 2000 |  | e.g. for 3GPP use the format TP-99xxx or for SMG, use the format P-99-xxx |
| CHANGE REQUEST | Please see embedded help file at the bottom of this page for instructions on how to fill in this form correctly. |
|  | 25.401 | CR | 7 | Current Version: | 3.1.0 |  |
| GSM (AA.BB) or 3G (AA.BBB) specification number ( |  | ( CR number as allocated by MCC support team |
| For submission to: | TSG RAN #7 | for approval | X |  | strategic |  | (for SMG |
| list expected approval meeting # here ( | for information |  |  | non-strategic |  | Use only) |
| Form: CR cover sheet, version 2 for 3GPP and SMG The latest version of this form is available from: ftp://ftp.3gpp.org/Information/CR-Form-v2.doc |
| Proposed change affects: | (U)SIM |  | ME |  | UTRAN / Radio | X | Core Network |  |
| (at least one should be marked with an X) |
| Source: | Mitsubishi Electric | Date: | Feb 2000 |
| Subject: | Transport layer in Iub U-Plane. |
| Work item: |  |
| Category: | F Correction | X | Release: | Phase 2 |  |
|  | A Corresponds to a correction in an earlier release |  |  | Release 96 |  |
| (only one category | B Addition of feature |  |  | Release 97 |  |
| shall be marked | C Functional modification of feature |  |  | Release 98 |  |
| with an X) | D Editorial modification |  |  | Release 99 | X |
|  |  |  |  | Release 00 |  |
| Reason for change: | In R99, AAL2 is used for Iub U-Plane data. References to AAL5 are therefore removed. |
| Clauses affected: | 11.2 |
| Other specs | Other 3G core specifications |  | ( List of CRs: |  |
| affected: | Other GSM core specifications |  | ( List of CRs: |  |
|  | MS test specifications |  | ( List of CRs: |  |
|  | BSS test specifications |  | ( List of CRs: |  |
|  | O&M specifications |  | ( List of CRs: |  |
| Other comments: |  |

<--------- double-click here for help and instructions on how to create a CR.

## 11.2	Protocol Model (Informative)

The following section is a informative section which aim is to provide an overall picture of how the MAC layer is distributed over Uu, Iub and Iur for the RACH, FACH and DCH.

### 11.2.1	RACH Transport Channel

Figure 11 shows the protocol stack model for the RACH transport channel when the Controlling and Serving RNC are co-incident.

For the RACH transport channel, Dedicated MAC (MAC-d) uses the services of  Common MAC (MAC-c).

# Figure 11: RACH: Coincident Controlling and Serving RNC

The Common MAC (MAC-c) entity in the UE transfers MAC-c PDU to the peer MAC-c entity in the RNC using the services of the Physical Layer.

An Interworking Function (IWF) in the NodeB interworks the RACH frame received by the PHY entity into the RACH Frame Protocol (RACH FP) entity.

The RACH Frame Protocol entity adds header information to form a RACH FP PDU which is  transported to the RNC over an AAL2  connection.

At the RNC, the RACH FP entity delivers the MAC-c PDU to the MAC-c entity.

Figure 12 shows the protocol model for the RACH transport channel with separate Controlling and Serving RNC. In this case, Iur RACH Frame Protocol (DchFP) is used to interwork the Common MAC (MAC-c) at the Controlling RNC with the Dedicated MAC (MAC-d) at the Serving RNC (The exact Iur FACH Frame Protocol is FFS)

# Figure 12: RACH: Separate Controlling and Serving RNC

### 11.2.2	FACH Transport Channel

Figure 13 shows the protocol model for the FACH transport channel when the Controlling and Serving RNC are co-incident.

# Figure 13: FACH Co-incident Controlling and Serving RNC

The Common MAC (MAC-c) entity in the RNC transfers MAC-c PDU to the peer MAC-c entity in the UE using the services of the FACH Frame Protocol (FACH FP) entity.

The FACH Frame Protocol entity adds header information to form a FACH FP PDU which is  transported to the NodeB over an AAL2  connection.

An Interworking Function (IWF) in the NodeB interworks the FACH frame received by FACH Frame Protocol (FACH FP) entity into the PHY entity.

FACH scheduling is performed by MAC-c in the CRNC.

Figure 14 shows the protocol model for the FACH transport channel with separate Controlling and Serving RNC. In this case, Iur FACH Frame Protocol is used to interwork the Common MAC (MAC-c) at the Controlling RNC with the Dedicated MAC (MAC-d) at the Serving RNC (The exact Iur RACH Frame Protocol is FFS)

Figure 14: FACH: Separate Controlling and Serving RNC

### 11.2.3	DCH Transport Channel

Figure 15 shows the protocol model for the DCH transport channel when the Controlling and Serving RNC are co-incident.

Figure 15: DCH: Co-incident Controlling and Serving RNC

The DCH transport channel introduces the concept of distributed PHY layer.

An Interworking Function (IWF) in the NodeB interworks  between the DCH Frame Protocol (DCH FP) entity and the PHY entity.

Figure 16: DCH: Separate Controlling and Serving RNC

Figure 16 shows the protocol model for the DCH transport channel with separate Controlling and Serving RNC. In this case, the  Iub DCH FP is terminated in the CRNC and interworked with the Iur DCH FP through a PHY function. This function performs optional soft handover or can be a null function.

### 11.2.4	DSCH Transport Channel

Figure 17 shows the protocol model for the DSCH transport channel when the Controlling and Serving RNC are co-incident.

Figure 17: DSCH Co-incident Controlling and Serving RNC

The Shared MAC (MAC-sh) entity in the RNC transfers MAC-sh PDU to the peer MAC-sh entity in the UE using the services of the DSCH Frame Protocol (DSCH FP) entity. The DSCH FP entity adds header information to form a DSCH FP PDU which is  transported to the Node B over an AAL2  connection.

An Interworking Function (IWF) in the Node B interworks the DSCH frame received by DSCH FP entity into the PHY entity. DSCH scheduling is performed by MAC-sh in the CRNC.

Figure 18 shows the protocol model for the DSCH transport channel with separate Controlling and Serving RNC. In this case, Iur DSCH Frame Protocol is used to interwork the MAC-sh at the Controlling RNC with the MAC-d at the Serving RNC.

Figure 18: DSCH: Separate Controlling and Serving RNC

### 11.2.5	USCH Transport Channel

Figure 19 shows the protocol model for the USCH transport channel when the Controlling and Serving RNC are co-incident.

Figure 19: USCH Co-incident Controlling and Serving RNC

The Shared MAC (MAC-sh) entity in the RNC receives MAC-sh PDU from the peer MAC-sh entity in the UE using the services of the Interworking Function in the NodeB, and the USCH Frame Protocol (USCH FP) entity. The USCH FP entity in the NodeB adds header information to form a USCH FP PDU which is transported to the RNC over an AAL2 connection.

An Interworking Function (IWF) in the Node B interworks the received USCH PHY entity into an USCH frame to be transmitted by the USCH FP entity over the Iub interface. USCH scheduling is performed by MAC-sh in UE and by C-RRC in the CRNC.

Figure 20 shows the protocol model for the USCH transport channel with separate Controlling and Serving RNC. In this case, Iur USCH Frame Protocol is used to interwork the MAC-sh at the Controlling RNC with the MAC-d at the Serving RNC.

Figure 20: USCH: Separate Controlling and Serving RNC