3GPP TSG-RAN WG3 #110e	R3-206890

Online, 2-12 November 2020

Agenda Item:	10.3.2.2

Source:	CATT (moderator)

Title:	Summary of Offline discussion on MDT for MR-DC

Document for:	Approval

# Introduction

CB: # 1014_SONMDT_MDTMR-DC

-  Topics to discuss:

- You may discuss the Xn (6140) and X2 (6149) TPs directly

(CATT - moderator)

Summary of offline disc R3-206890

# For the Chairman’s Notes

Propose the following:

# Discussion

## Support of immediate MDT for MR-DC

In RAN3#109 meeting, it was agreed that for MDT in NGEN-DC and NE-DC, the SN receiving the management based immediate MDT and the signalling based immediate MDT in EN-DC is taken as baseline. Based on the agreement, MDT Configuration-NR and MDT Configuration-EUTRA have been introduced in XnAP. However, the information on user consent is still missing in XnAP.

In [1], it is propose to include Management Based MDT PLMN List IE in S-NODE ADDITION REQUEST message.

If companies have different view, please comments below

| Company | Yes/No | Comment |
| --- | --- | --- |

In [1], it is propose to introduce Cell Traffic Trace procedure in Xn AP

If companies have different view, please comments below

| Company | Yes/No | Comment |
| --- | --- | --- |

## Support of log MDT in EN-DC

RAN2 has agreed that log MDT should be supported in MR-DC scenario. Based on that, in [2], it is proposed to remove the restriction that only immedaite MDT is supported in EN-DC.

If companies have different view, please comments below

| Company | Yes/No | Comment |
| --- | --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

R3-206140 (TP on MDT in MR-DC for 38.423) Addition of immediate MDT in NGEN-DC and NE-DC (CATT)

R3-206149 (TP on MDT enhancement for 36.423) Support of MDT enhancement for EN-DC (CATT)