3GPP TSG-RAN WG3 #110e	R3-20xxxx

Online, 2-12 November 2020

Agenda Item:	10.3.2.2

Source:	CATT (moderator)

Title:	Summary of Offline discussion on MDT for MR-DC

Document for:	Approval

# Introduction

CB: # 1014_SONMDT_MDTMR-DC

-  Topics to discuss:

- You may discuss the Xn (6140) and X2 (6149) TPs directly

(CATT - moderator)

Summary of offline disc R3-206890

# For the Chairman’s Notes

Propose agree the follows:

Proposal1: It is proposed to add Management Based MDT PLMN List IE in S-NODE ADDITION REQUEST message. It could be discussed in phase 2 on the IE details and whether/how to add editor's note.

Proposal2: It is proposed to add Cell Traffic Trace procedure in Xn AP.

Proposal3: It is proposed to agree R3-206149 which remove the restriction that only immedaite MDT is supported in EN-DC.

Proposal for next phase:

It is proposed to discuss the details on TP R3-206140 which reflects agreement 1 and 2.

# Discussion for second round

It is prosed to agree the TP in Draft_R3-20XXXX_original_R3-206140_TP for XnAP

If there are different views, companies are invited to provide comments here.

| Company | Yes/No | Comment |
| --- | --- | --- |

# Discussion for first round

## Support of immediate MDT for MR-DC

In RAN3#109 meeting, it was agreed that for MDT in NGEN-DC and NE-DC, the SN receiving the management based immediate MDT and the signalling based immediate MDT in EN-DC is taken as baseline. Based on the agreement, MDT Configuration-NR and MDT Configuration-EUTRA have been introduced in XnAP. However, the information on user consent is still missing in XnAP.

In [1], it is propose to include Management Based MDT PLMN List IE in S-NODE ADDITION REQUEST message.

If companies have different view, please comments below

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | YES |  |
| Huawei | yes |  |
| Qualcomm | Yes |  |
| ZTE | Yes |  |
| Samsung | Yes |  |
| Nokia | Editor's note may be needed | The TP also enables management based MDT for the NR-DC scenario, and not only NE-DC and NGEN-DC. Need to further check the risk of colliding configurations. Editor's note to remind about this should be enough at this meeting, and checking can be done at next meeting. |
| CMCC | Yes |  |
| Ericsson | Yes |  |

Moderator’s summary: All companies agreed to include Management Based MDT PLMN List IE in S-NODE ADDITION REQUEST message.One company propose to add an editor’s note.

Proposal:It is proposed to add Management Based MDT PLMN List IE in S-NODE ADDITION REQUEST message.It  could be discussed in phase 2 on the IE details and whether/how to add  editor's note.

In [1], it is propose to introduce Cell Traffic Trace procedure in Xn AP

If companies have different view, please comments below

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | YES |  |
| Huawei | Yes |  |
| Qualcomm | Yes |  |
| Samsung | Yes |  |
| Nokia | Yes | This is linked, but the editor's note mentioned above should be enough. |
| CMCC | Yes |  |
| Ericsson | Yes |  |

Moderator’s summary: All companies agreed to Cell Traffic Trace procedure in Xn AP..

Proposal:It is proposed to add Cell Traffic Trace procedure in Xn AP

## Support of log MDT in EN-DC

RAN2 has agreed that log MDT should be supported in MR-DC scenario. Based on that, in [2], it is proposed to remove the restriction that only immedaite MDT is supported in EN-DC.

If companies have different view, please comments below

| Company | Yes/No | Comment |
| --- | --- | --- |
| CATT | YES |  |
| Huawei | Yes, or wait till RAN2 agrees sth. |  |
| Qualcomm | Yes |  |
| ZTE | Share the view with HUAWEI |  |
| Samsung | Yes |  |
| Nokia | Share the view with Huawei, ZTE | It seems that RAN2 made the overall agreement, but the actual solution is under discussion. |
| CMCC | No strong view remove the restriction or later | This can be done when the solution is clear |
| Ericsson | Yes |  |

Moderator’s summary:There are no objection to remove the restriction that only immedaite MDT is supported in EN-DC.

Proposal: It is proposed to agree R3-206149 which remove remove the restriction that only immedaite MDT is supported in EN-DC.

# Conclusion, Recommendations [if needed]

If needed

# References

R3-206140 (TP on MDT in MR-DC for 38.423) Addition of immediate MDT in NGEN-DC and NE-DC (CATT)

R3-206149 (TP on MDT enhancement for 36.423) Support of MDT enhancement for EN-DC (CATT)