3GPP TSG-RAN WG3#110 	R3-207001

# E-Meeting,  02 – 12 November 2020

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 38.413 | CR | 0488 | rev | 1 | Current version: | 16.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network | X | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correction of UE Release Request |
| --- | --- |
| Source to WG: | Nokia, Nokia Shanghai Bell, Orange |
| Source to TSG: | R3 |
| Work item code: | NR_newRAT-Core, TEI16 |  | Date: | 2020.11.02 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | RAN WGs and SA/CT WGs use the terms of “active PDU session” with different meanings. In case of user inactivity in NG-RAN, TS 23.502 section 4.2.6 request the NG-RAN to include the “list of PDU Session IDs with Active N3 User plane” in the UE Context Release Request/Complete message. When NG-RAN sends UE Release Request for “user inactivity” reason, this can be interpreted as the list of PDU Session IDs should NOT be included (given the inactivity). However from 5GC viewpoint, 5GC may instead expect the list of PDU Session IDs, given that the PDU Sessions are established in NG-RAN node. |
| Summary of change: | It is clarified that the optional list of PDU Session IDs in the UE Context Release Request message is the full list of PDU Sessions established in the NG-RAN, regardless whether they are “active” or not “from a RAN point of view”. Impact assessment towards the previous version of the specification (same release): This CR has an isolated impact towards the previous version of the specification (same release). This CR only has an impact on the UE Context Release procedure. |
| Consequences if not approved: | Interoperability issue due to the fact that some AMF fail if NG-RAN node does not include the list of PDU Sessions in UE Reelase Request message when the message is sent for user inactivity in RAN. |
| Clauses affected: | 8.3.2.2, 8.3.3.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

#### 8.3.2.2	Successful Operation

Figure 8.3.2.2-1: UE context release request

The NG-RAN node controlling a UE-associated logical NG-connection initiates the procedure by sending a UE CONTEXT RELEASE REQUEST message towards the affected AMF.

The UE CONTEXT RELEASE REQUEST message shall indicate the appropriate cause value, e.g., "TXnRELOCOverall Expiry", "Redirection", for the requested UE-associated logical NG-connection release.

If the PDU Session Resource List IE is included in the UE CONTEXT RELEASE REQUEST message, the AMF shall consider the indicated PDU Sessions as the full list of PDU Sessions established in the NG-RAN and handle this information as specified in TS 23.502 [10].

#### Next change

#### 8.3.3.2	Successful Operation

Figure 8.3.3.2-1: UE context release: successful operation

The AMF initiates the procedure by sending the UE CONTEXT RELEASE COMMAND message to the NG-RAN node.

The UE CONTEXT RELEASE COMMAND message shall contain both the AMF UE NGAP ID IE and the RAN UE NGAP ID IE if available, otherwise the message shall contain the AMF UE NGAP ID IE.

Upon reception of the UE CONTEXT RELEASE COMMAND message, the NG-RAN node shall release all related signalling and user data transport resources and reply with the UE CONTEXT RELEASE COMPLETE message.

If the PDU Session Resource List IE is included in the UE CONTEXT RELEASE COMPLETE message, the AMF shall consider the indicated PDU Sessions as the full list of PDU Sessions established in the NG-RAN and handle this information as specified in TS 23.502 [10].

If the User Location Information IE is included in the UE CONTEXT RELEASE COMPLETE message, the AMF shall handle this information as specified in TS 23.502 [10].

If the Information on Recommended Cells and RAN Nodes for Paging IE is included in the UE CONTEXT RELEASE COMPLETE message, the AMF shall, if supported, store it and may use it for subsequent paging.

For each PDU session for which the Secondary RAT Usage Information IE is included in the PDU Session Resource Release Response Transfer IE, the SMF shall handle this information as specified in TS 23.502 [10].

If the Paging Assistance Data for CE Capable UE IE is included in the UE CONTEXT RELEASE COMPLETE message, the AMF shall, if supported, store it and use it for subsequent paging, as specified in TS 23.502 [10].