3GPP TSG-RAN WG3 #110	R3-207005

02-12 November 2020

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on UE Release Request

Document for:	Approval

# Introduction

This is the report of the following email discussion.

CR0488r, TS 38.413 v16.3.0, Rel-16, Cat. A

CB: # 106_UEreleaseReq

- agreeable to capture agreement as Rel-16 CR?

- need to liaise SA2?

(Nok - moderator)

rev in R3-207001

draftLS to SA2 R3-207002

Summary of offline disc 7005

# For the Chairman’s Notes

Propose the following:

Agreement: it is agreed to.

Agreement: it is agreed to.

New xxx. To be continued release 17…

# Discussion

## Correction of UE Context Release Request

Tdoc R3-206226 explains IOT issue occurred due to the two possible interpretations of whether the list of PDU session IDs should be included in UE Release Request.

- One interpretation considers the term “inactive” to be read according to TS 38.413 and therefore think that the list of PDU sessions should NOT be included in the UE Context Release Request message because the PDU sessions are inactive according to TS 38.413 section 9.3.1.2:

| User inactivity | The action is requested due to user inactivity on all PDU sessions, e.g., NG is requested to be released in order to optimise the radio resources. |
| --- | --- |

- Another interpretation instead considers the term “inactive” to be read according to TS 23.502 and therefore think that the list of PDU sessions should be included in the UE Context Release Request message because the PDU sessions are established in the NG-RAN.

A majority of companies seem to think that the second interpretation should be followed. However, as explained above, this is not the one immediately deduced from TS 38.413 and IOT issue occurred. Therefore, we propose to capture this in TS 38.413. The compromise in RAN3 meeting since this can be seen as a clarification, is to have release 16 CR. The release 16 CR in R3-206230 has been revised in R3-207001 changing the category from A to F.

R3-207001 has now been made available in CB folder.

Any final comment to R3-207001?

| Company | Comment |
| --- | --- |
| Nokia | No comment. |
| Huawei | Ok to have R16-only CR for clarification. |

## LS to SA2

The next question is if we send LS to SA2 to clarify this. Assuming RAN3 CR in R3-207001 agreed we do not think needed to have further LS sent to SA2 since stage 3 will be clear. Also, the clarification proposed in R3-207001 is actually the one following the reading according to TS 23.502 and therefore the advantage of choosing this solution is that it is aligned with TS 23.502 making clarification in TS 23.502 no more necessary.

Assuming RAN3 CR agreed we propose to not send an LS to SA2.

Is it OK to NOT send an LS to SA2 or you prefer not send?

| Company | Comment |
| --- | --- |
| Nokia | OK assuming consensus on R3-207001. |
| Huawei | No need to send any LS to SA2. |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

# Conclusion

The following is proposed:

Proposal 1: It is proposed to agree to only.

# References

R3-20xxxx