3GPP TSG-RAN WG3 #108-e	R3-206862

Online, 1-11 June 2020

Agenda Item:	9.3.7.1

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion CB: # 23_NTN_RegUpdate_and_Paging

Document for:	Approval

# Introduction

This is Summary of offline discussion on CB: # 23_NTN_RegUpdate_and_Paging

Please provide your view by 6th Friday CET 10am.

Friday a first status will be provided online with an update, some first agreements and a Way Forward (WF) for next step, if any.

Following last meeting agreements, see below, the discussion is separated in two discussion; the paging enhancement and the LS to SA2/RAN2:

Paging enhancements are FFS (e.g. using location information, etc.)

Further discussion and coordination with SA2/RAN2 are needed.

# For the Chairman’s Notes TBC

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

R3-20xxxd rev [in xxxh] – agreed

R3-20xxxe rev [in xxxi] – agreed

R3-20xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

## Paging Enhancement

The following paging enhancement are proposed:

- It is feasible and beneficial for paging stationary UE based on specific SSB beam in GEO NTN cell and LEO with earth fixed cell. [1, 2, 3]

- It’s beneficial to introduce some kind of paging enhancement for transparent LEO with moving cells to minimize the signalling overhead of the paging.[4, 8]

- the similar paging optimization mechanism as LTE and NR R15 could be reused, by using of the UE location info (GNSS info) as the assistance info. [4, 8]

- Provide the schedule of the TAC for the moving cells. [6]

- Revert the WA to not different TA that contains NTN cells in order to allow some optimisation  [6]

- The existing paging mechanism for NTN is enough for R-17.[7]

Question #1: Please provide comment, support or request for clarification on each solution, if possible…

| Company | Comment |
| --- | --- |

Expectation, summary and/or conclusion:

- The intention is to see if a majority view has interest for further investigation on some solutions… If yes we can proceed with draft CR, if not we keep the status quo of last meeting.

## Coordination with SA2/RAN2

Question #2: Please provide view on the following proposal: Liaise with SA2 and RAN2 to confirm the assumptions that for moving cells, the UE is supposed to be configured with the geographical area definition of cell IDs. [5]

| Company | Comment |
| --- | --- |

Expectation, summary and/or conclusion:

- Check Friday online if a LS could be sent this meeting

Question #3: Please provide view on the following proposal: Liaise with RAN2 to confirm the requirement for the moving cell case, that the UE would need to provide information about the selected cell ID (with Tracking Area and PLMN ID in case of ambiguities) corresponding to UE’s current geographical location.[5]

| Company | Comment |
| --- | --- |

Question #4: Please comment the following proposal and if it should be part of the RAN2 LS: Proposal 4: Further discuss the possibility consider multiple TAC for a cell if earth-moving cell ID [6]

| Company | Comment |
| --- | --- |

Expectation, summary and/or conclusion:

- Check Friday online if a LS could be sent this meeting

# Conclusion, Recommendations [TBC]

If needed

# References

R3-206044	Discussion on paging UE per SSB beam in NTN cell	Samsung

R3-206045	CR to 38413 for paging UE per SSB beam in NTN cell	Samsung

R3-206046	CR to 38473 for paging UE per SSB beam in NTN cell	Samsung

R3-206276	Discussion on potential paging enhancement for NTN	CATT

R3-206382	Handling of Registration and Paging with moving cells	Ericsson

R3-206599	Some consideration on RAN3 agreements	Huawei

R3-206686	Further Discussion on Paging Enhancement for NTN	ZTE

R3-206277	Support of UE location based Paging for NTN	CATT