3GPP TSG-RAN WG3#110                                             	                     R3-207055

E-Meeting, 02 – 12 November 2020

Agenda item:	22.2.3

Source:	Nokia, Nokia Shanghai Bell

Title: 	MBS Stage 2 for PTM- PTP switching

Document for:	Approval

# TP for TS 38.300

## 16.x	NR Multicast and Broadcast

### 16.x.1	General

- Editor’s Note: General aspects to be covered here.

### 16.x.2	Architecture

- Editor’s Note: Architecture aspects to be covered here.

### 16.x.3	Session Management

- Editor’s Note: Session Management aspects to be covered here.

### 16.x.4	PTP-PTM Switching

- Editor’s Note: covers both PTP to PTM switching and PTM to PTP switching.

### The PTP-PTM Switching function is only applicable for a multicast MBS Session and resides in NG-RAN node. It enables the NG-RAN node to decide for which UEs to use PTP or PTM (PTP, PTM to be defined with RAN2) for the MBS session. The NG-RAN node takes its decision based on information such as MBS Session QoS requirements, number of joined UEs, UE individual feedback on reception quality, and other criteria. The same QoS requirements apply regardless of the decision.

### PTP and PTM modes can be used simultaneously in the same cell. For Broadcast only PTM is applicable. For Multicast both PTP and PTM are applicable.

### 16.x.5	MBS Mobility

- Editor’s Note: Mobility aspects to be covered here.