3GPP TSG-RAN WG3 #110	R3-206909

02-12 November 2020

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on MBS PTP- PTM Dynamic Change

Document for:	Approval

# Introduction

This paper presents the result of the following email discussion:

CB: # 60_MBS_PTP-PTMdynChg

SS 6029

CU should take decision of PTP and PTM switch

Intel 6207

…

Assistance information for the PTP/PTM decision from 5GC is not needed.

Co-existence of PTP and PTM in a same cell should be allowed.

Chair:

- Clarify terminology first; service transport from CN vs. delivery within RAN

- PTP/PTM decision within the RAN: DU, vs. CU with assistance info from DU? Check RAN2 progress before making final decision?

- Any assistance info needed from CN to make PTP/PTM decision? Liaise SA2?

(Nok - moderator)

Summary of offline disc R3-206909

# For the Chairman’s Notes

Propose the following:

Agreement: it is agreed to.

Agreement: it is agreed to.

New xxx. To be continued release 17…

# Discussion

## Clarification of terminology of PTP and PTM

Do you agree to restrict the terms PTP and PTM for RAN internal delivery decision for the various mode?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | Yes |
| Intel | Yes |

Do you agree that for unicast only PTP is applicable, for broadcast only PTM and for multicast both PTP and PTM are applicable?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | Yes |
| Intel | Yes |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

## Co-existence of PTP and PTM modes in a cell

Can we assume that PTP and PTM modes can be used simultaneously in a cell?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | Yes |
| Intel | Yes |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

## Decision Node for PTP PTM switching

Do you agree that NG-RAN node should make the PTP – PTM switch decision?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | We agreed gNB make decision for NG-U shared delivery. |
| Intel | Yes |

Moderator’s summary:

in our specifications.

## Signalling for switching the mode to the UE

Should the switch of the mode be done via RRC signaling as proposed in 6487?

| Company | Comment |
| --- | --- |
| Nokia | RAN2 should decide this. |
| Samsung | RAN2 to decide it. |
| Intel | RAN2’s domain |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

## Disaggregated architecture: Decision Node CU or DU

In disaggregated architecture, which node should be the decision node between CU or DU according to you?

| Company | Comment |
| --- | --- |
| Nokia | We need to wait for RAN1/2 evaluation. As explained in tdoc 6250 this depends which types of measurements are used. |
| Samsung | We think CU makes the decision. While it is fine to wait for RAN1/RAN2 evaluation. It is related to the user plane protocol as well. |
| Intel | Agree with Nokia |

Moderator’s summary:

in our specifications.

## F1-U tunnel

In case the switching decision is in DU, if the UE is configured with both PTP and PTM, how many GTP-U tunnels should be setup over F1-U?

| Company | Comment |
| --- | --- |
| Nokia | One shared GTP tunnel. One extra individual GTP tunnel may be setup only if there is PDCP retransmission for the UE. |
| Samsung | One shared GTP tunnel for PTM transmission. One dedicated GTP tunnel for each PTP transmission. |
| Intel | Agree with Nokia |

Moderator’s summary:

in our specifications.

## F1-C impact

In case the switching decision is in DU, what are the F1-C impacts?

| Company | Comment |
| --- | --- |
| Nokia | Need to transfer MBS context in UE context (agreed last time). Need to transfer PDCP feedback if agreed in RAN2. Pre-configuration of PTP-PTM modes and signaling switch if the switch is signaled to the UE via RRC. |
| Samsung | FFS |
| Intel | FFS |

Moderator’s summary:

in our specifications.

## Need of assistance information from 5GC for PTP-PTM switching

Do you see need of some parameters from 5GC to help NG-RAN take the decision of PTP-PTM switching?

| Company | Comment |
| --- | --- |
| Nokia | No. We don’t see the need for the assistance parameters suggested so far. However, if new parameters come up during the work item phase we can reconsider the question. |
| Samsung | No. |
| Intel | Too early to say no need for assistance parameters from CN. Keep it open until RAN2/RAN1 conclude with PTP/PTM switching design |

Moderator’s summary:

x companies strongly.

# TPs

Is it ok to capture some stage 2 agreements obtained so far for TS 38.300 such as text from the tdocs 6250 and 6387?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Intel | Yes |

Is it ok to capture in TS 38.401 that the PTP-PTM switch decision is in DU as in 6412?

| Company | Comment |
| --- | --- |
| Nokia | It is a bit premature as we must wait RAN2 before deciding if DU makes the switching decision (see above). |
| Intel | Agree with Nokia |

# Conclusion

The following is proposed:

Proposal 1: It is proposed to agree to only.

Proposal 2: It is proposed meeting.

Proposal 3: Given that.

# References

R3-20xxxx