3GPP TSG-RAN WG3 #110	R3-206909

02-12 November 2020

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on MBS PTP- PTM Dynamic Change

Document for:	Approval

# Introduction

This paper presents the result of the following email discussion:

CB: # 60_MBS_PTP-PTMdynChg

SS 6029

CU should take decision of PTP and PTM switch

Intel 6207

…

Assistance information for the PTP/PTM decision from 5GC is not needed.

Co-existence of PTP and PTM in a same cell should be allowed.

Chair:

- Clarify terminology first; service transport from CN vs. delivery within RAN

- PTP/PTM decision within the RAN: DU, vs. CU with assistance info from DU? Check RAN2 progress before making final decision?

- Any assistance info needed from CN to make PTP/PTM decision? Liaise SA2?

(Nok - moderator)

Summary of offline disc R3-206909

# For the Chairman’s Notes

Propose the following:

Agreement: it is agreed to.

Agreement: it is agreed to.

New xxx. To be continued release 17…

# Discussion

## Clarification of terminology of PTP and PTM

Do you agree to restrict the terms PTP and PTM for RAN internal delivery decision for the various mode?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | Yes |
| Intel | Yes |
| Huawei | Yes |
| Lenovo and Motorola Mobility | Yes |
| ZTE | Yes |
| Ericsson | What ever “PTP” and “PTM” stands for in the context of NR MBS, those terms denote RAN internal functions. |
| CATT | Yes. |

Do you agree that for unicast only PTP is applicable, for broadcast only PTM and for multicast both PTP and PTM are applicable?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | Yes |
| Intel | Yes |
| Huawei | Yes |
| Lenovo and Motorola Mobility | Yes |
| ZTE | Yes |
| Ericsson | What is “unicast”? I would not like to use that term in the context of NR MBS, where only “multicast” and “broadcast” should be used. We agree roughly for multicast and broadcast, but would need to learn RAN2 concepts first. |
| CATT | Yes. However,could we consider PTP mode for broadcast if there are only one or several UEs listening to the broadcast service? |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

## Co-existence of PTP and PTM modes in a cell

Can we assume that PTP and PTM modes can be used simultaneously in a cell?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | Yes |
| Intel | Yes |
| Huawei | Yes |
| Lenovo and Motorola Mobility | Yes |
| ZTE | Yes |
| Ericsson | Depends on what ptp and ptm stands for. If “ptp” stands for “DRB”, then we say “no”, if “ptp” stands for UE dedicated functions of the MRB the we would agree. But this depends on RAN2. |
| CATT | Yes |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

## Decision Node for PTP PTM switching

Do you agree that NG-RAN node should make the PTP – PTM switch decision?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Samsung | We agreed gNB make decision for NG-U shared delivery. |
| Intel | Yes |
| Huawei | Yes, already agreed last meeting. |
| Lenovo and Motorola Mobility | Yes, already agreed in both RAN2 and RAN3 |
| ZTE | Yes |
| Ericsson | In the context of RAN2 discussions on the definitions of the MRB (as far as we can know for now), “switching” refers to the question to what extent and for which UEs “UE dedicated” functions of the MRB are configured. |
| CATT | Yes |

Moderator’s summary:

in our specifications.

## Signalling for switching the mode to the UE

Should the switch of the mode be done via RRC signaling as proposed in 6487?

| Company | Comment |
| --- | --- |
| Nokia | RAN2 should decide this. |
| Samsung | RAN2 to decide it. |
| Intel | RAN2’s domain |
| Huawei | It is up to RAN2 decision. |
| Lenovo and Motorola Mobility | RAN2 should decide it. |
| ZTE | RAN2 issue. |
| Ericsson | very much RAN2 |
| CATT | RAN2 to decide how to inform the UE. |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

## Disaggregated architecture: Decision Node CU or DU

In disaggregated architecture, which node should be the decision node between CU or DU according to you?

| Company | Comment |
| --- | --- |
| Nokia | We need to wait for RAN1/2 evaluation. As explained in tdoc 6250 this depends which types of measurements are used. |
| Samsung | We think CU makes the decision. While it is fine to wait for RAN1/RAN2 evaluation. It is related to the user plane protocol as well. |
| Intel | Agree with Nokia |
| Huawei | We think DU can make the decision. As DU knows the accurate radio resource status. It is also fine to wait RAN1/RAN2 progress. |
| Lenovo and Motorola Mobility | It is up to the gNB-CU makes the decision on which modes is configured to the UE i.e. PTP mode only, SC-PTM mode only, MC-PTM mode only, or both PTP and SC-PTM/MC-PTM modes. Dynamic PTM and PTP Switching function resides in gNB-DU to enable more dynamic switching between PTM and PTP mode. |
| ZTE | DU decides. It is obvious that, based on the analysis from companies, “DU decides” features lower latency and enables shorter service interruption. RAN3 can start the evaluation from the architectural/signaling latency point of view, and LS RAN1/2 about the result or preference based on companies’ contribution. This is an architectural issue and shall be solved in RAN3 first. RAN1/2 can further study whether current measurement is good enough or enhancement is needed. |
| Ericsson | we should observe discussions in RAN2 and talk to our colleagues there. And agree with Samsung, there are UP aspects where we can look at, e.g. for UE individual PDCP PDU retransmissions. But we expect kind of configuration of “ptm” and “ptp” aspects of an MRB to be performed in the CU to create the possibilities for the DU to decide when active “ptp” aspects, e.g. based on individual feedback on L1/MAC/RLC level. “ptp” aspects of PDCP would be handled via retransmissions in the CU-UP. |
| CATT | To wait RAN1/2 evaluation seems beneficial. |

Moderator’s summary:

in our specifications.

## F1-U tunnel

In case the switching decision is in DU, if the UE is configured with both PTP and PTM, how many GTP-U tunnels should be setup over F1-U?

| Company | Comment |
| --- | --- |
| Nokia | One shared GTP tunnel. One extra individual GTP tunnel may be setup only if there is PDCP retransmission for the UE. |
| Samsung | One shared GTP tunnel for PTM transmission. One dedicated GTP tunnel for each PTP transmission. |
| Intel | Agree with Nokia |
| Huawei | One shared GTP-U tunnel should be setup for PTM transmission. Separate GTP-U tunnel could be setup for each PTP transmission. |
| Lenovo and Motorola Mobility | One shared F1-U GTP-U tunnel is used for both PTM and PTP modes corresponding to an MBS radio bearer. |
| ZTE | One shared GTP-U tunnel for the initial transmission from PDCP entity (no matter PTP, PTM or both) for one specific MRB. If PDCP retransmission is needed for specific UE, there will be one GTP-U tunnel for each additionally. |
| Ericsson | So far we see on shared GTP tunnel for the “main” transmission and GTP tunnel(s) for per UE PDCP PDU retransmissions. |
| CATT. | One shared tunnel for PTM (DL), and individual tunnels for PTP, including PDCP status report (UL) and retransmission (DL). |

Moderator’s summary:

in our specifications.

## F1-C impact

In case the switching decision is in DU, what are the F1-C impacts?

| Company | Comment |
| --- | --- |
| Nokia | Need to transfer MBS context in UE context (agreed last time). Need to transfer PDCP feedback if agreed in RAN2. Pre-configuration of PTP-PTM modes and signaling switch if the switch is signaled to the UE via RRC. |
| Samsung | FFS |
| Intel | FFS |
| Huawei | Need to transfer PDCP status report if agreed in RAN2. FFS if F1 interactions for RRC related information and mode switching notification needed. |
| Lenovo and Motorola Mobility | FFS |
| ZTE | CU to DU: MBS context including the associated UE list. DU to CU: the lower layer configuration of the associated delivery modes if it has not been configured to UE through RRC signaling yet. Basically we see comparable F1-C spec impacts between the two options (CU or DU decides). |
| Ericssion | concepts would have first to settle in RAN1/2. |
| CATT | Too early to discuss this, and may be more suitable to be discussed in CB#61, not here. |

Moderator’s summary:

in our specifications.

## Need of assistance information from 5GC for PTP-PTM switching

Do you see need of some parameters from 5GC to help NG-RAN take the decision of PTP-PTM switching?

| Company | Comment |
| --- | --- |
| Nokia | No. We don’t see the need for the assistance parameters suggested so far. However, if new parameters come up during the work item phase we can reconsider the question. |
| Samsung | No. |
| Intel | Too early to say no need for assistance parameters from CN. Keep it open until RAN2/RAN1 conclude with PTP/PTM switching design |
| Huawei | So far no. |
| Lenovo and Motorola Mobility | Ni |
| ZTE | Yes. Explicit delivery policy which can not be conveyed in QoS profile could help RAN make better decision. It can be part of the MBS context info from 5GC, we can wait for SA2’s more evaluation in WI phase. |
| Ericsson | no, no, no |
| CATT | RAN2 is also discussing on this topic, similar view as intel, maybe we could keep it open until there is conclusion in RAN2 |

Moderator’s summary:

x companies strongly.

# TPs

Is it ok to capture some stage 2 agreements obtained so far for TS 38.300 such as text from the tdocs 6250 and 6387?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Intel | Yes |
| Huawei | ok |
| Lenovo and Motorola Mobility | Yes |
| ZTE | Yes with minor suggestions: - use “Multicast session” instead of “multicast” in 6250 or “multicast MBS Sessions” in 6387, to be aligned with TR 23.757. - align the NG-RAN behaviors between the two TP. 6387 seems a more complete one: “according to MBS Session QoS requirements, number of joined UEs, optionally UE individual feedback on reception quality, lost user data, and other criteria.” |
| Ericsson | our TP in 6387 captures our understanding of what “ptp”/”ptm” “switching” is about, without using the terms “ptm” or “ptp” or “mode” in the definition. I would appreciate to follow this overall “wording design”. |
| CATT | The TP is ok for us, but we suggest clarifying its two sub-cases: cell-level dynamic switch and UE-level dynamic switch. |

Is it ok to capture in TS 38.401 that the PTP-PTM switch decision is in DU as in 6412?

| Company | Comment |
| --- | --- |
| Nokia | It is a bit premature as we must wait RAN2 before deciding if DU makes the switching decision (see above). |
| Intel | Agree with Nokia |
| Huawei | Anyway the TP to 38.401 is needed, how about have a try and add FFS on it? |
| Lenovo and Motorola Mobility | Fine with Huawei’s proposal, adding FFS |
| ZTE | Yes, fine with Huawei’s proposal with the FFS inside. |
| Ericsson | our TP in 6387 for 38.300 captures our understanding of what “ptp”/”ptm” “switching” is about, without using the terms “ptm” or “ptp” or “mode” in the definition. I would appreciate to follow this overall “wording design” also for 38.401 and to not repeat definitions. TP for 38.401 should refer to 38.300 and concentrate on CU and DU roles. |
| CATT | Fine with Huawei’s proposal, adding FFS |

# Conclusion

The following is proposed:

Proposal 1: It is proposed to agree to only.

Proposal 2: It is proposed meeting.

Proposal 3: Given that.

# References

R3-20xxxx