3GPP TSG-RAN WG3 Meeting #110-e	R3-206910

E-meeting, 2 - 12 Nov 2020

Agenda Item:	22.2.4

Source:	Huawei (moderator)

Title:	Summary of discussion on Bearer Management over F1/E1

Document for:	Approval

# Introduction

CB: # 61_MBS_F1-E1bearerMgmt

SS 6027

set up UE dedicated tunnel for MBS PTP transmission and a common tunnel for MBS PTM transmission.

define MBS specific procedure in F1 to setup PTM configuration in the DU.

E/// 6388

consider E1 and F1 as “followers” from basic discussions on session management, support of mobility, support of “transmission mode switching” and foremost, especially for F1, input from RAN2 discussions.

further review progress on the outlined topics and further develop F1/E1 concepts, probably not spending too much meeting time for now.

HW 6413

provide MBS context information from gNB-CU to gNB-DU via F1AP: UE CONTEXT MODIFICATION REQUEST message.

gNB-DU assigns the G-RNTI, and gNB-DU provides the assigned G-RNTI to gNB-CU via F1AP: UE CONTEXT MODIFICATION RESPONSE message.

use shared F1-U transport to support PTM transmission.

support shared GTP-U Tunnel method (gNB-DU to assign the DL GTP-U Tunnel info) over F1-U.

introduce non UE associated F1AP procedures to setup/release the shared F1-U transport.

ZTE 6529

Single F1-U tunnel for one specific MRB between one specific DU and CU.

For specific UE with retransmission in PDCP level (in PTP manner), a separate F1-U for the UE is established to transmit the PDCP PDU.

Non-UE associated (or MBS associated) E1/F1 signaling is used for the bearer and MBS context management, respectively. FFS on the signaling details.

CATT 6835

gNB-CU is responsible for configuring SDAP and PDCP layers of NR PTM logical channel, while gNB-DU is responsible for configuring other layers such as RLC, MAC, PHY.

A new non-UE associated procedure needs to be introduced into F1 interface to independently transfer the configuration information for NR PTM logical channel and MBS session related information, such as Qos profile, etc.

gNB-CU is responsible for configuring SDAP and PDCP layers of NR PTP logical channel, while gNB-DU is responsible for configuring other layers 6835such as RLC, MAC, PHY.

UE context on F1 should contain MBS context information，which is related to PTP logical channel.

If PTP mode over Uu interface is applied, a F1 individual MBS transport tunnel should be established for each MBS session of UE between CU and DU.

If PTM mode over Uu interface is applied, a F1 shared MBS transport mode should be established for each MBS session between CU and DU.

Individual and shared MBS transport mode can exist over F1 interface simultaneously.

configuration information of SDAP and PDCP layers for each NR PTM logical channel should be transferred between gNB-CU-CP and gNB-CU-UP

configuration information of SDAP and PDCP layers for each NR PTP logical channel should be transferred between gNB-CU-CP and gNB-CU-UP

A new non-UE associated MBS bearer management procedure needs to be introduced into E1 interface to independently transfer the configuration information for NR PTM logical channel and MBS session related information, such as Qos profile, etc.

Current BEARER CONTEXT SETUP REQUEST procedure can be reused to transfer MBS context information，which is related to PTP logical channel, to gNB-CU-UP

Chair:

- whether to progress NG aspects first and then align F1/E1 handling?

- Any assumptions that could be made already now, e.g. on information needed to be signaled between CU-CP and CU-UP?

- consensus for new non-UE-associated procedures to set up transport for E1/F1? WA agreeable?

(HW - moderator)

Summary of offline disc R3-206910

# For the Chairman’s Notes

About Shared F1-U tunnel:

- Use a shared F1-U tunnel for PTM transmission of an MBS radio bearer for an MBS Session within one cell.

- If multiple MBS radio bearers could be established for an MBS Session, a shared F1-U tunnel should be used for PTM transmission of these MBS radio bearers of the same MBS Session within one cell.

- It is FFS whether a shared F1-U tunnel can be used for the same MBS Session established in multiple cells of the same DU.

- Use non-UE associated F1/E1 procedures to setup the shared F1-U tunnel.

About F1-U transport establishment

- Support the method that gNB-DU assigns the DL F1-U GTP-U tunnel info, provides it to gNB-CU-CP and then gNB-CU-CP forwards it to gNB-CU-UP.

- FFS if IP multicast method is supported or not.

About MBS Context

- Provide the MBS Session id, Qos profile from gNB-CU to gNB-DU.

- Provide the MBS Session id, Qos profile from gNB-CU-CP to gNB-CU-UP.

About MBS Bearer management

- WA: MBS Bearer management procedure waiting for SA2/RAN2 progress.

About G-RNTI

- WA: gNB DU assignes the G-RNTI, pending to RAN2 confirmation.

# Discussion

RAN2 has discussed L2 Architecture for NR MBS, and some conclusions are achieved (not officially agreed yet), from our understanding, we can take these into account when we discuss the bearer management over F1/E1.

Figure 1 depicts RAN2 discussions and the related conclusion could be understood as below:

Figure 1: Diagram for RAN2 L2 Architecture discussion

- SDAP: no SDAP functions other than “mapping from QoS flows to radio bearers” and “transfer of user plane data” are supported for MBS. This working assumption can be revisited when SA2 concludes the QoS model for MBS.

- PDCP: L2 architecture with one PDCP entity associating with two RLC entities is used as baseline for further discussion. The PDCP functions supported for NR MBS include: reordering, in-order delivery, transfer of data, maintenance of PDCP SNs and duplicate discarding. Besides, PDCP status reporting and retransmission is needed for NR MBS at least in the case of mobility. FFS for other cases.

- RLC: RLC TM is not supported for both PTP transmission and PTM transmission of NR MBS. RLC UM can be supported for both PTP and PTM transmission. For RLC AM, it is supported for PTP transmission but FFS for PTM transmission.

- MAC/PHY: In MAC, it is discussed if multiplexing/de-multiplexing logical channels carrying data from different MBS flows of one MBS session can be supported but no conclusion was achieved. In PHY, PTM transmission uses an MBS specific RNTI (e.g. G-RNTI), PTP transmission uses per-UE RNTI (e.g. C-RNTI).

## F1-U tunnel for PTP and PTM

As it was agreed in last meeting that for 5GC shared MBS traffic delivery of user data to a NG-RAN, shared NG-U transport, regardless of delivery method over the radio shall be used. With the similar consideration, a shared F1-U transport tunnel may be used to support PTM transmission.

Question 1: Do you agree to support a shared F1-U tunnel for PTM transmission?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | Yes |  |
| Samsung | Yes |  |
| Huawei | Yes | As it was agreed in last meeting that for 5GC shared MBS traffic delivery of user data to a gNB, shared NG-U transport, regardless of delivery method over the radio shall be used. With the similar consideration, in our view the shared F1-U transport shall also be used to support PTM transmission. |
| ZTE | Yes |  |
| Ericsson | ? | If we assume RAN2 agrees on a MBS radio bearer to be used for UP transmission on Uu for an MBS Session resource, then we assume one F1-U tunnel to be established for that MRB. We may discuss whether this F1-U tunnel is shared for all MRBs established in a DU. |
| LGE | Yes |  |
| CATT | Yes |  |
| Intel | Yes |  |
| Lenovo, Motorola Mobility | Yes | We also need to discuss the shared tunnel is per cell basis or per DU basis. |
| Qualcomm | Yes |  |

Moderator's summary:

Sorry for the inaccurate question, at least, all companies should agree the minimized scenario, i.e. use a shared F1-U tunnel for PTM transmission of an MBS radio bearer for an MBS Session within one cell.

And then, it seems straight forward that if multiple MBS radio bearers could be established for an MBS Session, a shared F1-U tunnel should be used for PTM transmission of these MBS radio bearers of the same MBS Session within one cell.

It is FFS whether a shared F1-U tunnel can be used for the same MBS Session established in multiple cells of the same DU.

Proposal to Chairman notes:

Use a shared F1-U tunnel for PTM transmission of an MBS radio bearer for an MBS Session within one cell.

If multiple MBS radio bearers could be established for an MBS Session, a shared F1-U tunnel should be used for PTM transmission of these MBS radio bearers of the same MBS Session within one cell.

It is FFS whether a shared F1-U tunnel can be used for the same MBS Session established in multiple cells of the same DU.

If a shared F1-U tunnel for PTM transmission, further optimization may be considered about whether PTP and PTM for the same UE can use the same shared F1-U transport.

Question 2: Do you agree to support a shared F1-U tunnel for PTP and PTM for the same UE?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | No | We cannot take this decision now. This actually depends whether CU or DU makes the PTP-PTM switching decision. And this in turn depends on the RAN1/RAN2 work outcome on measurements…(see CB60) |
| Samsung | No | Agree with Nokia. In order no to introduce new function to DU, we think dedicated tunnel for PTP tranmsisison is better. The data transmitted via a tunnel can be sent to the correct RLC without further handling in DU. |
| Huawei | No | It is better to use dedicated tunnel for PTP transmission. PTP can be used to retransmit the MBS data which is initially transmitted via PTM, the data transmitted via a dedicated tunnel can be sent to DU without further optimization. |
| ZTE | Yes | One thing needs to be clarified here is the so called PTP and PTM here are only for initial transmission from PDCP level. For such case, it is beneficial to apply a shared F1-U tunnel for whatever delivery mode (PTP, PTM, or the combination of both. Please note that in current stage, we see no need to limit the number of simultaneous delivery instance in a single DU, i.e., there might be multiple PTP for more than one UEs, or multiple PTM delivery for more than one cells or even in one cell): - resource efficient. A single PDCP PDU is delivered to DU, and DU takes the MBS context into consideration, submit the PDCP PDU to the corresponding RLC entity or entities. - scalable. As has been clarified, there might be more than one delivery instances in the DU, a single tunnel can serve them all. - a single shared tunnel minimizes the transmission gap between cells and different modes. No efforts needed. - the more tunnels exist between F1, the more signaling is needed to maintain the tunnel. Therefore, a single shared tunnel is preferred. |
| Ericsson | ? | The question sounds like a contradiction: how can a shared tunnel relate to “the same UE”? Please clarify. |
| LGE | No | Agree with Nokia |
| CATT | No | For split mode (PTP+PTM), the “split” point between PTM and PTP should be PDCP, If PDCP feedback is supported, it seems more suitable to deliver the retransmitted packets over the PTP leg. |
| Intel | See comment | Agree with Nokia, need RAN2 to conclude their L2 protocol stack, then we decide whether CU or DU make the PTM/PTP decision, then we can come back to this. |
| Lenovo, Motorola Mobility | Yes | Agree with ZTE. a single shared tunnel is used for both PTM and PTP. |
| Qualcomm |  | Depending which PTP/PTM switching solution is used. If switching is at PDCP, we need two tunnels. If switching is in RLC and lower layer, one tunnel is fine. |

Moderator's summary: majority companies agree with Nokia that we cannot take this decision now.

Proposal to Chairman notes: nothing.

Besides, it may be considered to support PTP of different UEs can use the same shared F1-U transport tunnel.

Question 3: Do you agree to support a shared F1-U tunnel for PTP of different UE?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | No | Cannot decide now. Same as above. |
| Samsung | No |  |
| Huawei | No |  |
| ZTE | Yes | For initial transmission (from PDCP perspective), the benefits we have shared in Q2 apply here as well. For re-transmission (PDCP level) if there are any, UE specific tunnels are needed. |
| Ericsson | ? | Again, the question sounds like a contradiction. In principle one can imagine F1-U tunnel that multiplex every kind of traffic, but UP protocol design should make some sense. |
| LGE | No |  |
| CATT | No | For PTP mode, it should establish a separate channel per UE. |
| Intel | See comment | Same comment as last question |
| Lenovo, Motorola Mobility | Yes | Same as above |
| Qualcomm | No |  |

Moderator's summary:  several companies said no, and some of them think cannot decide now, two companies said yes, no consensus.

Proposal to Chairman notes: nothing.

Based on TR 23.757 V1.0.0 [1], to support shared NG-U transport, both IP Multicast method (NG-RAN node to join the IP multicast) and shared GTP-U Tunnel method (NG-RAN node to assign the DL GTP-U Tunnel info) shall be supported. To achieve shared F1-U transport, it is also needed to consider whether both these two methods need to be supported.

- Method 1: (IP Multicast method) gNB-CU-UP assigns the multicast address and provides it to gNB-CU-CP, gNB-CU-CP forward it to gNB-DU, and then gNB-DU joins the IP multicast group;

- Method 2: (DL GTP-U Tunnel method) gNB-DU assigns the DL F1-U GTP-U tunnel info, provides it to gNB-CU-CP and then gNB-CU-CP forwards it to gNB-CU-UP;

Question 4: Which method do you prefer to be supported to achieve the shared F1-U transport?

| Company | Method # | Comment |
| --- | --- | --- |
| Nokia | Method 2 and Method 1 standardized | Support and standardization are different things. We assume here that the question is which method to be standardized? If that is the case we can simply do like NG-U i.e. standardize both. |
| Samsung | Method 2 |  |
| Huawei | Method 2 |  |
| ZTE | 1 and 2 | Both work for the F1-U. |
| Ericsson |  | slight feeling that method 2 might be sufficient, but for now we could keep both open. |
| LGE | Method 2 |  |
| CATT | Method 2 and Method 1 |  |
| Intel | 1 and 2 |  |
| Lenovo, Motorola Mobility | Method 2 |  |
| Qualcomm | Both 1 and 2 |  |

Moderator's summary: all 10 companies support method 2, and 5 companies would like to also support method 1.

Proposal to Chairman notes:

About F1-U transport establishment:

Support the method that gNB-DU assigns the DL F1-U GTP-U tunnel info, provides it to gNB-CU-CP and then gNB-CU-CP forwards it to gNB-CU-UP.

FFS if IP multicast method is supported or not.

In order to support the shared F1-U transport, it is also needed to discuss how to setup the shared F1-U tunnel, there are two options:

- Option 1: non-UE associated F1/E1 procedures

- Option 2: UE associated F1/E1 procedures

Question 5: Which option do you prefer to setup the shared F1-U tunnel?

| Company | Option# | Comment |
| --- | --- | --- |
| Nokia | Option 1 |  |
| Samsung | Option 1 | We think MBS specific messages need to be defined in F1, as proposed in 6028. |
| Huawei | Option 1 |  |
| ZTE | 1 | For the shared F1-U tunnel, non-UE associated F1/E1 procedures (or per MBS procedure) works fine without relying and messing up existing UE associated signaling. The below one might be out of scope of Q5, we add it here as this was discussed by companies in the papers. - For cases of PTP tunnel used for per UE PDCP retransmission, e.g., during mode switching or intra-DU mobility, both UE associated F1/E1 procedures and non-UE associated F1/E1 procedures could work. - However, we slightly prefer non-UE associated way, it enables operations to more than one UE with less signaling overhead. |
| Ericsson | ? | depends on what is meant by “UE associated”. If this denotes a kind of “connection oriented” exchange of AP IDs, then we would prefer an “xy associated” signaling. |
| LGE | Option 1 |  |
| CATT | Option 1 |  |
| Intel | Option 1 |  |
| Lenovo, Motorola Mobility | Option 1 |  |
| Qualcomm | Both | When first UE joins, the shared tunnel can be established using UE associated signaling. |

Moderator's summary: all companies support to use non UE associated F1/E1 procedures to setup the shared F1-U tunnel, one of them thinks that when first UE joins, the shared tunnel can be established using UE associated signaling.

Proposal to Chairman notes:

Use non-UE associated F1/E1 procedures to setup the shared F1-U tunnel.

## MBS context information

In both SA2 Solution#2 and Solution#3, it is needed to provide the MBS context information from gNB-CU to gNB-DU, and it was agreed in last RAN3 meeting that the F1AP UE context should contain MBS context information. As described in SA2, Multicast session context is identified by a Multicast Session context ID and is used to represent information about group of UEs receiving Multicast flows with the same Multicast Session context ID. Multicast flows represents QoS flows within a Multicast Session context. Thus MBS information signaled via F1 may take the following factors as baseline:

- Multicast Session Context ID

- Multicast address

- UEs that joined multicast session providing multicast communication service

- Multicast QoS profile (e.g. Multicast Flow ID)

- Multicast Service ID(i.e. TMGI)

Question 6: Do you agree to signal the above MBS info from gNB-CU to gNB-DU? If there are any other information, please elaborate.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | Partly | MBS session ID and QoS Profile to start. Other FFS. |
| Samsung |  | We assume the MBS context is setup via MBS dedicated message between CU and DU. We can start with minimum set included in this message, e.g. TMGI, Session ID, TNL information, MBS Bearer ID and QoS parameter. |
| Huawei |  | We think the necessary MBS related info should be included in this message, e.g. multicast group identity (e.g. multicast address) in case IP multicast is supported and used, Multicast Session context ID, and multicast QoS profile (e.g. Multicast Flow ID). |
| ZTE | Clarification is needed. | Multicast Session Context ID. Not sure if it is the same context ID from CN, a local ID might just work. An unique MBS ID is needed anyway. Multicast address. There are two interpretations of such multicast address: the service ID in service layer (according to te lastest SA2 progress, Multicast address is one of the solutions to identify the MBS service), or the IP multicast address used in N3. If it is IP multicast in N3, indicating the Multicast address is possibly fine: DU joins the IP multicast directly. UE list is needed to explicitly indicate to DU the joined UE info for better scheduling the Multicast service, i.e., mode switching, or enabling the HARQ feedback. QoS profile is needed. Service ID is needed as well, however it might overlap with the MBS session context ID. Only one unique ID is needed. Or if the service ID in service layer like TMGI is needed by DU, e.g., broadcast on air interface, it is needed then. |
| Ericsson | ? | SA2 are discussing CU and DU? Agree with Nokia, slow start ... |
| LGE |  | Multicast Session Context ID, Multicast QoS profile, Multicast Service ID, TNL information, and MBS bearer ID |
| CATT | Yes | Agree with Huawei. These information is baseline. |
| Intel | See comment | Agree with Nokia |
| Lenovo, Motorola Mobility | Yes | Agree with Huawei. These information is baseline. |
| Qualcomm | Yes |  |

Moderator's summary:

All companies agree to provide the MBS Session id, Qos profile from gNB-CU to gNB-DU.

Proposal to Chairman notes:

Provide the MBS Session id, Qos profile from gNB-CU to gNB-DU.

Similarly like F1AP, the MBS information may also need to be signaled from gNB-CP to gNB-CU-UP.

Question 7: Do you agree to signal the above MBS info from gNB-CU-CP to gNB-CU-UP? If there are any other information, please elaborate.

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | Partly | MBS session ID and QoS Profile to start. Other FFS. |
| Samsung | FFS | Gerernally, above minimum set should be notified to CU-UP too. But how to notify is related to user plane protocol. Can further discuss based on RAN2 progress. |
| Huawei |  | The necessary MBS info mentioned above should be notified to gNB-CU-UP. |
| ZTE | Partly | Besides the content in Q6 we have provided, for E1, the QoS flow to MRB mapping info is needed; the UE list for which re-transmission is needed shall be included. |
| Ericsson |  | SA2 are discussing CU and DU? Agree with Nokia, slow start ... |
| LGE |  | Agree with Nokia |
| CATT |  | Agree with Huawei |
| Intel |  | Agee with Nokia |
| Lenovo, Motorola Mobility | Yes | Agree with Huawei. |
| Qualcomm |  | Agree with Nokia, Huawei |

Moderator's summary:

All companies agree to provide the MBS Session id, Qos profile from gNB-CU-CP to gNB-CU-UP

Proposal to Chairman notes:

Provide the MBS Session id, Qos profile from gNB-CU-CP to gNB-CU-UP.

## MBS Bearer management

From RAN2 L2 architecture discussions, the radio bearer resource in the gNB-CU-UP consist of an SDAP and PDCP entity which need configuration for the NR MBS radio bearer. Thus E1AP may need to provide means for configuring a PDCP entity that support MBS data transmission to more than one DU as well as receive UE PDCP status report and re-transmit PDCP PDU to UEs, which need RAN2 further discussion. Besides, it is under discussion in SA2 that a MBS PDU session would be associated to a unicast PDU session and MBS session for MBS session management and support of mobility. Correspondingly, a MBS radio bearer may be associated to a DRB, which would impact the NR MBS radio bearer configuration via F1AP.

Considering F1AP and E1AP aspects for MBS Bearer management need more RAN2 and SA2 inputs, we suggest not to spend too much time for now and RAN3 should give discussions on MBS bearer management after SA2 and RAN2 provide further progress.

Question 8: Do you agree that RAN3 discussion on MBS bearer management should wait for SA2 and RAN2 further progress?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | Yes | Seems reasonable. |
| Samsung | Yes | Fine to wait. |
| Huawei | Yes |  |
| ZTE | Not necessary to wait. | There are already majority consensus from RAN2 like the UP options, and anchor layer for mode switching. Discussion about the F1-U tunnel and potential options for signaling can be started. |
| Ericsson | no | This is not SA2 dependent. And also not RAN2 dependent. The association to a unicast PDU session is only for interworking with non-supporting nodes and not relevant for supporting nodes and not relevant at this state of discussions. I hope no one ever considers to establish within a supporting node a DRB for an MBS Session. |
| LGE | Yes |  |
| CATT | Yes |  |
| Intel | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| Qualcomm | Yes |  |

Moderator's summary: 8 companies agree to wait SA2 and RAN2 progress before discuss the MBS Bearer management procedures. 2 companies disagree.

Proposal to Chairman notes: WA: MBS Bearer management procedure waiting for SA2/RAN2 progress.

## G-RNTI aspects

To transfer MBS data from NG-RAN to UEs, G-RNTI is needed to address the PDCCH for MBS. As we know, C-RNTI is assigned by gNB-DU in NR, thus it could also be the gNB-DU to assign G-RNTI by for NR MBS.

Question 9: Do you agree that the gNB-DU to assign the G-RNTI?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | OK |  |
| Samsung | FFS | Related to G-RNTI allocation and usage. It is pending to RAN2 discussion. |
| Huawei | Yes | C-RNTI is assigned by gNB-DU. It is simple to also assign G-RNTI by gNB-DU for NR MBS. |
| ZTE | Yes |  |
| Ericsson | ? | what is the scope of a G-RNTI? |
| LGE | FFS | It is better to wait for RAN2 further progress related to G-RNTI allocation and usage. |
| CATT | FFS | It is pending to RAN2 discussion |
| Intel | Yes | But need RAN2 confirmation |
| Lenovo, Motorola Mobility | Yes |  |
| Qualcomm | Yes | But need RAN2 confirmation |

Moderator's summary:

6 companies agree that gNB DU assignes the G-RNTI and pending to RAN2 confirmation，3 companies FFS, 1 ?

Proposal to Chairman notes: WA: gNB DU assignes the G-RNTI, pending to RAN2 confirmation.

In NR, gNB-DU provides the assigned C-RNTI to gNB-CU via F1AP: UE CONTEXT MODIFICATION RESPONSE message. Thus if G-RNTI is assigned by gNB-DU for MBS, gNB-DU may also need to provide the G-RNTI to gNB-CU.

Question 10: If gNB-DU assigns the G-RNTI, do you agree to provide the G-RNTI from gNB-DU to gNB-CU?

| Company | Yes/No | Comment |
| --- | --- | --- |
| Nokia | Yes |  |
| Samsung | FFS | It is pending to RAN2 discussion. |
| Huawei | Yes | Simple to use the same method as C-RNTI does. |
| ZTE | Yes | The G-RNTI associated with the MBS (either Broadcast or Multicast) will be sent to UE in RRC signaling which is generated by CU-CP. |
| Ericsson | ? | What is the scope of a G-RNTI? |
| LGE | FFS | It is better to wait for RAN2 further progress. |
| CATT | FFS | It is pending to RAN2 discussion |
| Intel | FFS | Pending RAN2 discussion |
| Lenovo, Motorola Mobility | Yes |  |
| Qualcomm | Yes |  |

Moderator's summary:

5 companies agree that gNB DU assignes the G-RNTI，4 companies FFS, 1 ?

Proposal to Chairman notes: nothing.

## Others

If you have other issues to be discussed, please elaborate:

| Company | Yes/No | Comment |
| --- | --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References