3GPP TSG-RAN WG3#110			R3-207085

E-Meeting, 2 – 12 November 2020

Title:	Reply LS on End Marker in NG-RAN initiated QoS Flow mobility

Response to:	LS on End Marker in NG-RAN initiated QoS Flow mobility (C4-204340, R3-205913)

Release:	Rel-15 onwards

Work Item:	5GS Phase 1

Source:	RAN3

To:	CT4

Cc:	SA2

Contact Person:

#### Name:	Philippe Godin

Tel. Number:	+33 1 6040 0304

E-mail Address:	philippe.godin@nokia.com

Attachments:	R3-207047, R3-207048

1. Overall Description:

RAN3 would like to provide feedback on the three proposed alternatives for the UPF sending end marker packets which are listed in CT4 LS:

- UPF sends one or more End Marker messages without any QFI included;

- UPF sends one or more End Marker messages including one QFI of those QoS flows be switched to the new N3 tunnel;

- UPF sends one or more End marker messages including the QFI for each of those QoS flows be switched to the new N3 tunnel;

RAN3 would like to feed back that the 1st option outlined is aligned with our understanding. Furthermore,

RAN3 has agreed the attached CRs to clarify above in TS 37.340 where the QoS Flow mobility is specified in detail.

2. Actions:

To CT4 group:

ACTION: 	RAN3 would like to ask CT4 to take the above into account.

3. Date of Next TSG-RAN WG3 Meetings:

TSG-RAN WG3#111-e                       25 January – 04 February 2020			E-meeting