3GPP TSG-RAN WG3#110			R3-20xxxx

E-Meeting, 2 – 12 November 2020

Title:	Reply LS on End Marker in NG-RAN initiated QoS Flow mobility

Response to:	LS on End Marker in NG-RAN initiated QoS Flow mobility (C4-204340, R3-205913)

Release:	Rel-15 onwards

Work Item:	5GS Phase 1

Source:	RAN3

To:	CT4

Cc:	SA2

Contact Person:

#### Name:	Philippe Godin

Tel. Number:	+33 1 6040 0304

E-mail Address:	philippe.godin@nokia.com

Attachments:	R3-20xxxx, R3-20xxxx

1. Overall Description:

RAN3 would like to provide feedback on the three proposed alternatives for the UPF sending end marker packets which are listed in CT4 LS:

- UPF sends one or more End Marker messages without any QFI included;

- UPF sends one or more End Marker messages including one QFI of those QoS flows be switched to the new N3 tunnel;

- UPF sends one or more End marker messages including the QFI for each of those QoS flows be switched to the new N3 tunnel;

RAN3 would like to clarify that alternative 1 is to be used.

RAN3 has agreed the attached CRs to clarify this point in TS 37.340 section 10.14 where the QoS Flow mobility is specified in detail.

2. Actions:

To CT4 group:

ACTION: 	RAN3 would like to ask CT4 to take the above into account.

3. Date of Next TSG-RAN WG3 Meetings:

TSG-RAN WG3#111-e                       25 January – 04 February 2020			E-meeting