3GPP TSG-RAN WG3 #110	R3-206949

02-12 November 2020

Online

Agenda Item:

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion on Direct Forwarding

Document for:	Approval

# Introduction

CB: # 83_DirectFwding

-  already captured in Chair notes: is a CR needed?

(Nok - moderator)

Summary of offline disc R3-206949

# For the Chairman’s Notes

Propose the following:

Agreement: it is agreed to.

New xxx. To be continued release 17…

# Discussion

## Capture RAN3#108 agreement in TS 38.300

Do you agree that RAN3#108 agreed that in 5g to 4g direction packets are forwarded without SDAP header?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Huawei | Yes |

If answer above is “yes”, do you see any show-stopper to capture it clearly in TS 38.300?

| Company | Comment |
| --- | --- |
| Nokia | No. It is helps visibility to design people rather than having to fetch inside Chair meeting’s minutes. |
| Huawei | No. But this is common understanding. Also the original words “QFI information” has no any ambiguities to us. |

Can we agree the CR in tdoc R3-206221?

| Company | Comment |
| --- | --- |
| Nokia | Yes. |
| Huawei | Given the discussion that we have before: MCC has clear minutes in the Chairman note, this CR is not very necessary. |

Moderator’s summary:

Consensus can be….

Proposal 1: It is proposed to …

# Conclusion

The following is proposed:

Proposal 1: It is proposed to agree to only.

# References

R3-20xxxx