3GPP TSG-RAN3 Meeting #110-e	R3-207226

Online, 2nd  - 12th  November 2020

Title:	Draft LS on broadcasting gNB ID length in system information block

Release:	Rel-17

Work Item:	TEI17

Source:	Ericsson (To be RAN WG3)

To:	RAN WG2

Cc:	SA WG3  TSG RAN

Contact Person:

#### Name:	Angelo Centonza

E-mail Address:	angelo.centonza@ericsson.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

RAN3 re-opened the discussion on how to retrieve the gNB ID length from a CGI in order to enable full utilization of the variable gNB length ID, as defined in TS 38.413.

RAN3 has taken the following agreements regarding this topic:

RAN3 confirms that exploiting the use of flexible gNB-ID lengths within the same network is beneficial to address the cases of ANR, RAN sharing, gNB-ID exhaustion

RAN3 confirms that a solution should be specified to allow acquisition of gNB-IDs as part of ANR

RAN3 discussed that a way to solve this issue could be to partition in a fixed way the cell ID numbering space. However, this prevents full utilization of the available node/cell ID’s numbering space.

To have a fully flexible mechanism, RAN3 is considering the following potential solutions:

- Solution 1: Network signalling based solution

- Solution 2: OAM based solution

- Solution 3: Broadcasting the gNB ID length within system information blocks (possibly in cellAccessRelatedInfo IE in SIB1).

There is so far no consensus in RAN3 on the preferred solution. Some companies think that OAM based solutions may bring burden to operators while some other companies think that network signaling based solution may increase complexity. However, RAN3 has not yet reached a conclusion on this topic.

As part of this discussion, RAN3 would like to respectfully ask RAN WG2 to check the feasibility of broadcasting the gNB ID’s length in system information blocks and related UE behaviour including reporting for ANR purposes.

2	Actions

RAN3 WG respectfully asks RAN2 WG to check the feasibility of broadcasting the gNB ID’s length in system information blocks and related UE behaviour including reporting for ANR purposes.

3	Dates of next TSG SA WG3 meetings

RAN3#111	25th January – 5th February 2021	Online