3GPP TSG-RAN WG3 #113-e	draft R3-214265

Online, 16 – 26 August, 2021

Agenda Item:	9.3.4.2

Source:	NEC (moderator)

Title:	CB: # 112_Stage2Corrections – Summary of e-mail discussion

Document for:	Decision

# 1 	Introduction

CB: # 112_Stage2Corrections

- Check stage2 essential corrections, approve the corresponding draftCR/CRs if agreeable

- Ignore editorial updates

(NEC - moderator)

Summary of offline disc in R3-214265

Let me try to have a first round of the deadline on:  20/Aug (Fri)  11:59:59 UTC.

The second round of discussion is set to : 24/Aug (Tue) 11:59:58 UTC.

# 2	For the Chairman’s Notes

To be Provided…

# 3

1st round of discussion (deadline is 20-Aug (Fri) 11:59 UTC)

Moderator proposes: to note R3-214266. (The contribution is not an CR in fact.)

Moderator proposes: to note R3-213309. The rapporteur of 38.401 to handle this editorial update.

Moderator proposes: to note R3-213572 and R3-213573. The rapporteur of 37.340 to handle this editorial update..

For R3-213375 / R3-213376 continue to discuss in 2nd round if ok to have only Rel-16 CR.

The rest of the proposed pure stage 2 CRs to continue discussion in 2nd round.

2nd round of discussion (deadline is 24-Aug (Tue) 11:59 UTC)

Please continue either in e-mail or insert your new comment in the table of each set of proposed CRs.

| R3-213103 | Clarification on RRC inactive to other RRC state transition procedure (Radisys) | Discussion Rev in R3-214266 (add Reliance Jio as co-source company) |
| --- | --- | --- |

Proposal to add Note under Step 7 for clarification in TS 38.401 Section 8.6.2 RRC inactive to Other states:

Note: In Step 7 optionally CU shall send RRCReject and RRCRelease to DU via F1 UE Context Release Command instead of DL RRC Message Transfer. The RRC message is encapsulated in UE CONTEXT RELEASE COMMAND to the gNB-DU by gNB-CU. gNB-DU forwards RRC message to UE and responds with UE Context Release Complete message to gNB-CU.”

Q1: Please give your view on this discussion paper.

| Company | Comment |
| --- | --- |
| Google | No strong opinion but the current protocol does not break by using the DL RRC Message Transfer |
| Ericsson | As previously discussed, Stage 2 cannot cover all possible cases. This seems already covered (also looking at corresponding Stage 3 parts). This CR is not needed. |
| Radisys | We think this additional note is needed for working in an inter vendor environment with open F1 interface. We find the current text in step 7 restrictive, as it only talks about sending RRC Reject and RRC Release over DL RRC Message Transfer. In an inter vendor scenario where CU and DU belong to different vendors, the RRC Reject and RRC Release can be either in DL RRC Message Transfer or UE Context Release Command. Hence in order to avoid interoperability issues, we would like to have additional clarification in the specification to state that, RRC Reject and RRC Release shall also be carried over F1 UE Context Release Command. As OpenRAN vendors, we prefer to have additional clarification in the specification to justify the RRC Reject and RRC Release callflow over open F1 interface. Also this proposal is similar to R3-213362 and R3-213363 talking about different scenarios for inter vendor operation. |
| Intel | No strong opinion, but this seems signalling optimization rather than correction or addressing critical use case. |
| Huawei | Seems an optimization on F1 message flows for RRC inactive UEs. No any problem foreseen if not have this. |
| ZTE | This CR is not needed, because current specs has no any problem without this CR. |
| Nokia | The specifications already allow carrying the RRC message as part of UE Context Release Command. There is no need to introduce description of additional variants to stage 2. |

Moderator summary: the proponent would like to have a CR. 2 has no strong opinion, 4 do not agree to have any CR.

Moderator proposes: to note the R3-214266. (The contribution is not an CR in fact.)

| R3-213235 | Correction on the usage of SN Reconfiguration Complete (ZTE Corporation, Google, Intel Corporation, Lenovo, NEC) | discussion |
| --- | --- | --- |
| R3-213236 | Correction on the usage of SN Reconfiguration Complete in Rel-15 (ZTE Corporation, Google, Intel Corporation, Lenovo, NEC) | draftCR |
| R3-213237 | Correction on the usage of SN Reconfiguration Complete in Rel-16 (ZTE Corporation, Google, Intel Corporation, Lenovo, NEC) | draftCR |

Proposal 1: In case of MN initiated SN modification procedure, add a note to indicate that in case the MN rejects the configuration requested by the SN, the MN instead informs the SN via SN Reconfiguration Complete message with the rejected cause.

Q2: Please give your view on these CRs.

| Company | Comment |
| --- | --- |
| Google | The existing stage 3 spec lacks of description for the applicable usage so it should be helpful to clarify it in stage 2. Some more points for information: There are cases in TS37.340 to describe the failure case such as in the following step of the CR - “In case the UE is unable to comply with (part of) the configuration included in the RRCConnectionReconfiguration message, it performs the reconfiguration failure procedure.” For the configuration rejection by the “MN” (please check 9.1.2.4 S-NODE RECONFIGURATION COMPLETE in TS38.423), the MN may be able to infer from the parameters in the CG-Config or in the IEs of the SN Modification Acknowledgement other than the RRC message itself (which should be transparent to MN). Otherwise, there seems to be no use case. |
| Ericsson | The proposed note describes a failure case, but Stage 2 typically does not describe failure cases. Where needed, failure cases are described “atomically” for the single protocol, in Stage 3. This CR is not needed. |
| Radisys | We understand that the text in stage 3 points to UE rejecting the configuration sent by SN and not the MN. Also MN sending a rejection of the SN configuration in SN Reconfiguration Complete message without triggering the RRC Reconfiguration does not make sense. We think this scenario does not fit in the SN Reconfiguration Complete message. Hence, we think that the stage 2 clarification is not needed. |
| Intel | We support these CRs to fill the gap between stage-2 and stage-3. It is clearly described in stage-3 that MN sends SN Reconfiguration Complete message in case MN rejects the configuration requested by SN. This has been there from very early days. Namely, the same class-2 "message" is used for both successful and unsuccessful cases. This is not about a typical class-1 procedure that a failure response is automatically assumed by a different message. Now, in our stage-2, SN Reconfiguration Complete is described only for the successful case. It should be clearly described in stage-2 to avoid confusion on the usage of this class-2 procedure that can be used for both successful and failure cases. And I don't understand the point that MN should not reject SN's request before sending RRC Reconfiguration. NW should not bother the UE unless coordination is successful between MN and SN. |
| Huawei | Seems not necessary, stage2 spec normally only captures the successful case. Share the view with Ericsson. |
| ZTE | This CR cosigned by 5 companies is needed. The change has not been described in stage 3 so that it shall be captured in stage 2. Without the clarification in this CR, it is misleading that when MN receiving ACK message from SN including bad configuration, the MN has to send RRC Reconfiguration message to UE, which is bad. With this CR, the SN modification procedure can be ended. This CR does not capture failure/reject case, it is used to stop the procedure even if receiving successful response but including unsuitable SN configuration. |
| Nokia | We’re confused concerning the described failure scenario. In short, in what situation the MN may want to reject the RRC reconfiguration provided from the SN? Please note, in EN-DC, the MN is not even able to read the RRC config provided from the SN! Wasn’t this the reason why it is not described in stage-3 or stage-2 so far? |

Moderator summary: 3 do not agree to have the CR, 3 support the CR, 1 is confused.

Moderator proposes: continue to discuss in 2nd round.

In the 1st round, the main concern is whether the MN can send SN reconfiguration complete message including reject cause to SN before sending RRC message to UE. The following discussion is use to further discuss on this issue.

In TS38.423 section 8.3.2, the SN Reconfiguration Complete message may contain information that

-	Case 1: the UE has successfully applied the configuration requested by the SN node.

-	Case 2: the configuration requested by the SN has been rejected.

| Response Information |  |
| --- | --- |
| >CHOICE Response Type |  |
| >>Configuration successfully applied | Case 1 |
| >>>M-NG-RAN node to S-NG-RAN node Container | Includes the RRCReconfigurationComplete message as defined in subclause 6.2.2 of TS 38.331 [10] or the RRCConnectionReconfigurationComplete message as defined in subclause 6.2.2 of TS 36.331 [14]. |
| >>Configuration rejected by the M-NG-RAN node | Case 2 |
| >>>Cause |  |
| >>>M-NG-RAN node to S-NG-RAN node Container | Includes the CG-ConfigInfo message as defined in as defined in subclause 11.2.2 of TS 38.331 [10]. |

In current procedure 10.3 Secondary Node Modification in TS37.340, only the Case 1 is captured but the Case 2 is missing.

This CR is used to add Case 2, i.e., the MN can send SN Reconfiguration Complete message to SN, after Step 2 and before Step 3, then the SN modification procedure can be stops and the UE will not be bothered.

NOTE 01:	In case the MN rejects the configuration requested by the SN, the MN may inform the SN via SgNB Reconfiguration Complete message with the rejected cause after step 2. The procedure ends.

Case 1 is captured in TS 37.340

According to TS38.331 section 5.3.5 RRC reconfiguration and 5.3.5.8 Reconfiguration failure, The UE in step 4 will send the RRCConnectionReconfigurationComplete if able to comply with all RRC-config or send the RRCReestablishmentRequest if unable to comply with all RRC-config.

Observation 1: If MN sends SN reconfiguration complete message with RRCReconfigurationComplete container, it means that MN receives RRC reconfiguration complete message from UE. It is the Case 1 as above.

Observation 2: If UE unable to comply with all RRC-config, the UE initiates RRC re-establish procedure, then the MN cannot sends SN reconfiguration complete message. Seen the description of step 3-5 of TS37.340.( In case the UE is unable to comply with (part of) the configuration included in the MN RRC reconfiguration message, it performs the reconfiguration failure procedure.)

Case 2 is missing in TS 37.340

SN sends SN modification request ACk message, including SN-InterNode-config and SN-RRC-config. SN-RRC-config checked by UE:  This IE is transparently forward to UE, then UE will check the SN-RRC-config whether (un)able to comply with. This is Case 1.

SN-InterNode-config checked by MN: For instance, if the MN is unable to comply with inter node coordination (MR-DC Resource Coordination Information), the MN can send SN reconfiguration complete message to SN, including reject reason, not bothering UE, stop the procedure. This is Case 2.

Observation: For Case 2 in stage 3 specs, the MN can sends SN Reconfiguration Complete message if the configuration requested by the S-NG-RAN node has been rejected, but it is not indicated what time to send this message (i.e., either before or after sending RRC message to UE) during SN modification procedure.

Proposal: For Case 2, the stage 2 specification is a suitable place to indicate it.

Q2: Please give your view on these CRs.

| Company | Comment |
| --- | --- |

| R3-213280 | DC in same and differ ent DUs (NEC, ZTE, Google Inc.) | CR0180r, TS 38.401 v16.6.0, Rel-16, Cat. F Rev in R3-214238 (added Nokia as co-signing company) |
| --- | --- | --- |

Add the description of possible DC configuration in the single gNB-DU or separate gNB-DUs in the same gNB-CU

Q3: Please give your view on this CRs.

| Company | Comment |
| --- | --- |
| Google | It is helpful to clarify it to reflect the change made to TS37.340 |
| Ericsson | a) the added text is not even in correct English. b) this scenario is not precluded by current Stage 2 text (37.340 says “can also be used when…”, which is perfectly fine). Therefore, no need to add a description for something which is already allowed. This CR is not needed. |
| Radisys | Agree to have this change |
| Intel | Since already reflected in 37.340, we think there is no need to repeat such high-level description in 38.401. In 38.401, DC related behaviors were already referred to 37.340. However, we may need some clarification on our "8.3.1 Centralized Retransmission in Intra gNB-CU Cases" in 38.401, which is described between two gNB-DUs, because, now in case of NR-DC, this is possible under one gNB-DU. |
| Huawei | No strong view, it seems that in RAN2, "DC can also apply in a single gNB-DU" was acknowledged. With this agreement, seems nothing wrong with this CR. |
| NEC | Reply to Ericson and Intel, the current Stage 2 text (37.340) says “can also be used when a UE is connected to a single gNB...” but it does not show anymore one gNB-DU or two DU. Before the RAN2 CR (R2-2102002) the description was there, after the RAN2 CR the information is lost. So we try to bring it back, but gNB-CU/DU thing is more RAN3, so we propose to add in in 38.401, hope this clarify and thanks for understanding. For the 8.3.1 pointed out by Intel, not sure if this relevant to this CR. |
| ZTE | We support this CR, with this CR, TS38.401 can align with TS37.340. Other, it is easy to mislead when reading different stage2 specs. |
| Nokia | This clarification is needed |

Moderator summary: 5 support the CR, 1 has no strong opinion. 2 see no need the CR

Moderator proposes: Continue to discuss in 2nd round..

| R3-213309 | Corrections on the abbreviation of OAM (China Telecommunication) | CR0181r, TS 38.401 v16.6.0, Rel-16, Cat. F |
| --- | --- | --- |

1) Change the abbreviation “O&M” into “OAM”;

2) Change the full spelling “Operation and Maintenance” into “Operation, Administration, and Maintenance”.

Q4: Please give your view on this CRs.

| Company | Comment |
| --- | --- |
| Google | Fine for the change |
| Ericsson | This CR is purely editorial (alignment with definitions, etc.): it should be noted. The corresponding issues (if acknowledged) should be left to the specification Rapporteur to address. |
| Radisys | Editorial Change. Upto to the Rapporteur to address. |
| Intel | It is true this is purely editorial change. We are fine either by this CR or by rapporteur. |
| Huawei | ok |
| ZTE | Fine with the CR |
| Nokia | This could be handled as part of Rapporteur corrections in Rel 17. |

Moderator summary: 2.5 are ok with the CR, 3.5 see this is editorial then can be handled by the rapporteur.

Moderator proposes: to note R3-213309. The rapporteur of 38.401 to handle this editorial update...

| R3-213361 | RRC Re-establishment and inter-vendor CU operation (Ericsson, Verizon Wireless) | discussion |
| --- | --- | --- |
| R3-213362 | RRC Re-establishment and inter-vendor CU operation CR 38.401 (Ericsson, Verizon Wireless) | CR0164r3, TS 38.401 v16.6.0, Rel-16, Cat. A |
| R3-213363 | RRC Re-establishment and inter-vendor CU operation CR 38.401 (Ericsson, Verizon Wireless) | CR0163r5, TS 38.401 v15.9.0, Rel-15, Cat. F |

Clarify that if UE access the same gNB-DU, then other vendor CU will trigger UE Context Setup procedure towards the same gNB-DU

Q5: Please give your view on these CRs.

| Company | Comment |
| --- | --- |
| Google | Fine for the change |
| Radisys | This CR again talks about different scenarios or failure cases in case of Inter Vendor environment. This CR is similar to R3-213103. We think such clarifications are needed in stage 2 to work seamlessly over Open F1 interface. Hence we think both R3-213103 and this CR is needed for clarification for open F1. |
| Intel | This is about critical handling where DU cannot retrieve UE context due to e.g. memory overload issue. Though we don't agree the approach described in R3-213361 (the way to trigger CU to initiate UE Context setup is by DU-initiated UE Context release request, which release and re-establishes F1 UE logical connection, but here F1 UE logical connection is not the problem. The problem is simply on DU who could not retrieve UE context properly based on the existing F1 UE logical connection), we are generally fine for the proposed changes in 3362 and 3363. |
| Huawei | We tend to think that such abnormal scenario should not happen in a normal implementation, and should not be captured in st2, thus it is not needed |
| ZTE | In the example sequency, since DU can not find the ue context, instead of UE context modifiction response, DU need to provide UE context failure to the CU with appopriate cause value. With such process, the CU can aware the failure in the DU and can decide whether to setup the UE context or drop it. |
| Nokia | Do not agree with the proposal. This topic had already been discussed in prior meetings. In our view, this scenario should not occur and the context would have been released upon expiry/corruption/etc. |
| Ericsson | We support this case and we believe that the condition described is a perfectly possible one, namely where a UE context at the same gNB-DU cannot be accessed. We do acknowledge that the case is not “normal”, but the specifications as they are today do not admit for such type of error at all, which is unreasonable as this error can occur. Comment to ZTE: in our paper in R3-213361 we do not mention a UE context Modification Response. We follow what ZTE commented, i.e. that the DU issues a UE context Release Request. All we want to ensure with the CR is that there is a commonly agreed procedure for a failure to retrieve an old UE context at re-establishment to the old serving gNB-DU. Failure to clarify this may lead to intervendor interoperability problems. Note that an operator is also supporting the proposal, meaning that the issue is of relevance in inter vendor cases |

Moderator summary:3 are ok with the CR, 3 do not agree.

Moderator proposes: continue to discuss in 2nd round.

| R3-213375 | Suspend Configuration (Ericsson, Intel, CATT, Google) | CR0169r2, TS 38.401 v15.9.0, Rel-15, Cat. F |
| --- | --- | --- |
| R3-213376 | Suspend Configuration (Ericsson, Intel, CATT, Google) | CR0170r2, TS 38.401 v16.6.0, Rel-16, Cat. A |

Addition of the reference to the suspend configuration that needs to be carried by the RRC release message

Q6: Please give your view on these CRs.

| Company | Comment |
| --- | --- |
| Google | Fine for the change |
| Radisys | Agree with this change |
| Huawei | ok |
| ZTE | Fine with the change. |
| Nokia | Overall see this clarification as not unnecessary. If introduced, it should also be limited to Rel 16. |
| Ericsson | We are fine with this correction, which clarifies the specifications |

Moderator summary: 4 are ok with the CR, 1 prefer to have only Rel-16 CR.

Moderator proposes: continue to discuss in 2nd round if ok to have only Rel-16 CR.

| R3-213515 | Clean-up on Xn-U Address Indication procedure (Intel Corporation, ZTE) | draftCR |
| --- | --- | --- |
| R3-213516 | Clean-up on Xn-U Address Indication procedure (Intel Corporation, ZTE) | draftCR |

1. In 10.4.2, a typo is fixed.

2. In 10.5.2, a missing Xn-U Address Indication from MN to T-SN is added with the corresponding description. A typo in the Figure 10.5.2-1 is also fixed.

3. In 10.7.2, a missing Xn-U Address Indication from the target MN to the (target) SN is added with the corresponding description.

4. In 10.9.2, a missing Xn-U Address Indication from the T-MN to the T-SN is added with the corresponding description.

Q7: Please give your view on these CRs.

| Company | Comment |
| --- | --- |
| Google | Fine for the change |
| Ericsson | Typo should be fixed by Rapporteur; all other additions are not true for all bearer types, so we risk introducing inconsistencies. Better left alone. CR is not needed. |
| Radisys | We understand that Xn-U Address Indication is not needed after SN Addition (as mentioned in the CR) as there will not be any data left in the buffer for forwarding. |
| Intel | We think there is some misunderstanding from Ericsson and Radisys. This is not about "data forwarding". This is about SN terminated bearer using "MCG" resources where the MN must provide Xn-U DL TNL address info via Xn-U Address Indication. Otherwise, it won't work. The typo can be fixed by rapporteur, but the descriptions about SN terminated bearer using "MCG" resources should be implemented in all the relevant places (as in 10.2.2 and 10.3.2). |
| Huawei | ok |
| ZTE | We support this CR, some changes in this CR is correction and makes sense. |
| Nokia | All right |

Moderator summary: 5 are ok with the CR, 2 see the CR is not needed.

Moderator proposes: continue to discuss in 2nd round.

| R3-213572 | Correction on EN-DC messages (Huawei, China Unicom) | draftCR |
| --- | --- | --- |
| R3-213573 | Correction on EN-DC messages (Huawei, China Unicom) | draftCR |

Update the message names in EN-DC part of Inter-Master Node handover with/without Secondary Node change

Q8: Please give your view on these CRs.

| Company | Comment |
| --- | --- |
| Google | Fine for the change |
| Ericsson | This is an editorial CR. Not needed. |
| Radisys | Editorial Change. Upto to the Rapporteur to address. |
| Intel | It is true this is purely editorial change. We are fine either by this CR or by rapporteur. |
| Huawei | Fine for the changes, to correct the wrong message names, it is not editorial. |
| Nokia | The change is all right, but is a Cat D CR – should be reported to the rapporteur. |
| ZTE | This CR is not needed. The CR is not good because it will introduce lots of corresponding modification which is not needed at all. |

Moderator summary: 2.5 are ok with the CR, 3.5 see this is editorial. 1 see this CR is not needed at all.

Moderator proposes: to note R3-213572 and  R3-213573. The rapporteur of 37.340 to handle this editorial update..

| R3-213957 | Correction on conditional reconfiguration for PSCell (Google Inc., Intel Corporation, CATT, ZTE) | draftCR |
| --- | --- | --- |

The actual given change in the proposal is:

The MN forwards the NR RRC response message to the SN in the SgNB Modification Confirm message.

Q9: Please give your view on these CRs.

| Company | Comment |
| --- | --- |
| Google | The proposed change avoids an incorrect interpretation that the MN may receive a RRC reconfiguration without containing a SN RRC response either for immediate or conditional configuration from the SN. For more information, if checking the affected sections, the step before has described the successful scenario so it is not needed to mention "if received from the UE." 3. The UE applies the new configuration and replies with the RRCConnectionReconfigurationComplete message. 4. The MN forwards the NR RRC response message to the SN in the SgNB Modification Confirm message. And this is different from other sections such as 10.2.1 SN Addition where the unsuccessful case were mentioned so that the following step may still need "if received from the UE." 4. The UE applies the new configuration and replies to MN with RRCConnectionReconfigurationComplete message, including a NR RRC response message, if needed. In case the UE is unable to comply with (part of) the configuration included in the RRCConnectionReconfiguration message, it performs the reconfiguration failure procedure. 5. The MN informs the SN that the UE has completed the reconfiguration procedure successfully via SgNB ReconfigurationComplete message, including the encoded NR RRC response message, if received from the UE. |
| Ericsson | “…if received from the UE” does not hint that there’s a case where it is not received, but rather that the forwarded information is the one received from the UE (as opposed to, say, an available/previously received set). It is the opposite of “…if available in the node”, in other words. This alone justifies the current text, which is therefore “not wrong™”. For this reason, we prefer not to touch it. This CR is not needed. |
| Radisys | Agree with this change |
| Intel | "if received from the UE" is purely a wrong description. So, we support this stage-2 CR. |
| Huawei | Ok |
| ZTE | We support this CR. |
| Nokia | The change seems technically all right, but which group defined CPC in Rel.16? Wasn’t it RAN2? If it was RAN3, then fine, otherwise it should be provided to RAN2. |

Moderator summary: 1 see the CR is not needed. 1 has doubt if this RAN3 part. 5 are ok with the CR.

Moderator proposes: continue to discuss in 2nd round.

# 4	References

| R3-213103 | Clarification on RRC inactive to other RRC state transition procedure (Radisys) | Discussion Rev in R3-214266 (add Reliance Jio as co-source company) |
| --- | --- | --- |
| R3-213235 | Correction on the usage of SN Reconfiguration Complete (ZTE Corporation, Google, Intel Corporation, Lenovo, NEC) | discussion |
| R3-213236 | Correction on the usage of SN Reconfiguration Complete in Rel-15 (ZTE Corporation, Google, Intel Corporation, Lenovo, NEC) | draftCR |
| R3-213237 | Correction on the usage of SN Reconfiguration Complete in Rel-16 (ZTE Corporation, Google, Intel Corporation, Lenovo, NEC) | draftCR |
| R3-213280 | DC in same and differ ent DUs (NEC, ZTE, Google Inc.) | CR0180r, TS 38.401 v16.6.0, Rel-16, Cat. F Rev in R3-214238 (added Nokia as co-signing company) |
| R3-213309 | Corrections on the abbreviation of OAM (China Telecommunication) | CR0181r, TS 38.401 v16.6.0, Rel-16, Cat. F |
| R3-213361 | RRC Re-establishment and inter-vendor CU operation (Ericsson, Verizon Wireless) | discussion |
| R3-213362 | RRC Re-establishment and inter-vendor CU operation CR 38.401 (Ericsson, Verizon Wireless) | CR0164r3, TS 38.401 v16.6.0, Rel-16, Cat. A |
| R3-213363 | RRC Re-establishment and inter-vendor CU operation CR 38.401 (Ericsson, Verizon Wireless) | CR0163r5, TS 38.401 v15.9.0, Rel-15, Cat. F |
| R3-213375 | Suspend Configuration (Ericsson, Intel, CATT, Google) | CR0169r2, TS 38.401 v15.9.0, Rel-15, Cat. F |
| R3-213376 | Suspend Configuration (Ericsson, Intel, CATT, Google) | CR0170r2, TS 38.401 v16.6.0, Rel-16, Cat. A |
| R3-213515 | Clean-up on Xn-U Address Indication procedure (Intel Corporation, ZTE) | draftCR |
| R3-213516 | Clean-up on Xn-U Address Indication procedure (Intel Corporation, ZTE) | draftCR |
| R3-213572 | Correction on EN-DC messages (Huawei, China Unicom) | draftCR |
| R3-213573 | Correction on EN-DC messages (Huawei, China Unicom) | draftCR |
| R3-213957 | Correction on conditional reconfiguration for PSCell (Google Inc., Intel Corporation, CATT, ZTE) | draftCR |