3GPP TSG-RAN WG3 #113	R3-214271

16 - 26 August 2021

Online

Agenda Item:	9.3.4.1

Source:	Samsung - Moderator

Title:	Summary of Offline Discussion – F1-U Delay Measurement

Document for:	Approval

# Introduction

This is the summary document for the following come back:

CB: # 115_F1-UDelay

- The issue is acknowledged and discuss on the potential solutions?

- Whether co-ordination with SA5 is needed or not?

(Samsung - moderator)

Summary of offline disc in R3-214271

# For the Chairman’s Notes

Propose the following:

Agree CR … .

# Discussion

### Solution

For F1-U delay measurement, the measurement method is defined in TS28.552 as the time when receiving a GTP packet delivery status message from the gNB DU at the egress GTP termination, minus time when sending the same packet to gNB DU at the GTP ingress termination, minus feedback delay time in gNB DU, obtained result is divided by two. But the feedback delay time in gNB DU is unavailable.

Figure below illustrates the measurement procedure:

Figure 1: F1-U delay measurement

In Figure1, (T3-T2) is the feedback delay time in gNB DU, so that the F1-U delay is (T4-T1-(T3-T2))/2.

There are two options to solve this issue:

Solution 1: DU reports GTP-U packet receiving time stamp in DU (T2) and DDDS sending time stamp in DU (T3) to CU-UP via DDDS. As the feedback delay is T3-T2, these two time stamps are both from DU, so that it would not cause error for non-time-synchronized cases. Hence, this solution can work for both time-synchronized and non-time-synchronized cases.

Solution 2: DU reports GTP-U packet feedback delay (T3-T2) to CU-UP directly via DDDS.

Q1.1: Companies are invited to provide their views on above two solutions, which solution is preferred (time stamp or feedback delay).

| Company | Prefer Solution 1 (time stamp) or Solution 2 (feedback delay) | Comment |
| --- | --- | --- |
| Nokia | None | Introduction of additional signalling support is not needed for the F1-U delay measurement. Existing signalling is sufficient, see below. |
| Intel | Solution 2 | We think providing feedback delay time also works regardless of time-synchronized or not, and prefer a simpler solution. |
| Huawei | Either way | We are fine with both solution. |
| Samsung2 | Both OK. No strong preference. | Both two options are workable regardless of time-synchronized or not. As the concern that time-stamp one can not cover non-time-synchronized cases was raised during online meeting, the explanation for solution 1 is added above to response this concern. |

Q1.2: If preferring any other solution, please provide here.

| Company | Comment |
| --- | --- |
| Nokia | We prefer to use poll function, already supported by TS 38.425. Thus if CU-UP sends a packet over F1-U with polling flag set, the DU will reply with DDDS. Processing time in the DU of a poll request is considered to be negligible. |
| Samsung | Response to Nokia: Thanks for providing the scheme with less spec impact. But it may lead to the problem for the case that DU sends one DDDS before receiving the DL User Data with polling from UP, as the figure below. So the UP may misunderstand that the received DDDS is the one as the response to its polling. In such case, the (T4-T1)/2 is not the F1-U delay. |
| ZTE | Actually SA5 adopt the following note at last meeting. NOTE : The NR RAN container (DL USER DATA/ DL DATA DELIVERY STATUS) carried in the GTP-U packet over the F1-U interface is used for the measurement. However, we do not understand why SA5 does not send the LS to RAN3/RAN2 after giving Note. From the protocol point of view, it is obviously impossible to get a precise delay by using DDDS. In this case, SA5 should have considered similar problems when giving Note. Therefore, I understand that if the current user-plane protocol is not modified, and if the fixed delay calculation feedback delay (e.g., N ms) is adopted, the requirement of SA5 may also be achieved. Therefore, they do not send the liaison letter to RAN3. Considering that F1-U delay is an average value and a small part of end to end delay, the calculation accuracy of F1-U can only be clarified if it is SA5. Therefore, it is my understanding that the specific solution will be discussed after the SA5 determines that precise measurement is required. |
| Intel | Using polling is fine with us (and abides by the SA5 specification that DL USER DATA and DDDS are used for F1-U delay calculation), but Samsung is correct that any DDDS received after triggering polling could be wrongly used for calculating F1-U delay. If polling is used, DDDS should indicate which DL USER DATA is the one that polled this DDDS. Maybe we can simply add NR-U sequence number of that DL USER DATA in the DDDS. |
| Huawei | We are fine with the polling function together with the NR-U sequence number in DDS. |
| Samsung2 | Response to ZTE: Thanks for providing the concern. There is a statement in TS 28.552 as 5.1.3.3.2 Average delay DL on F1-U … d) Each measurement is a real representing the mean delay in 0.1 millisecond. The number of measurements is equal to the number of PLMNs multiplied by the number of QoS levels or multiplied by the number of S-NSSAIs. 0.1 millisecond is the calculation accuracy for F1-U delay measurement. |
| Samsung2 | To avoid UP and DU recording the time-stamps for each packet, polling is OK for us. But for reusing the current one, it may leads to the waste if UP just wants to get a DDDS without feedback delay information. How about this compromised solution following the measurement method defined in TS 28.552 as below: Define a dedicated polling in DL USER DATA for feedback delay requesting. When DU receives the DL USER DATA frame with this dedicated polling, DU measures/collects the feedback delay or time stamps (which one to select depends on the Q1.1) of the GTP-U packet with “DL User Data with a dedicated polling”. And DU reports the measured or collected feedback delay or time stamps of the GTP-U packet with “DL User Data with a dedicated polling” to CU-UP via DDDS. And this solution is more efficient since a dedicated polling is 1 bit, while a NR-U sequence number is 3 octets. |
| CATT | We prefer polling function together with the NR-U sequence number in DDS. |

### Coordination with SA5

As the measurement method is defined by SA5, some companies prefer to coordinate with SA5 for F1-U delay measurement issue.

Q2: Companies are invited to provide their views on whether RAN3 should send a LS to SA5.

| Company | Yes/No | Comment (If yes, please provide the view about LS content) |
| --- | --- | --- |
| Nokia | Yes | RAN3 can send an LS to SA5 indicating that the poll function described in TS 38.425 can be used for the F1-U delay measurement. SA5 may then update their specification as required. |
| ZTE | Yes | To clarify the precise requirement of F1-DU. |
| Intel | No | It is already clear in SA5 TS 28.552 is that DL USER DATA and DDDS are used for calculating F1-U delay. Using polling has no problem. |
| Huawei | no | SA5 is clearly enough, no need any further LS. |
| Samsung2 | Seems no need | It seems TS 28.552 is clear. |
| CATT | Seems no need | Similar view as Intel |

Moderator’s summary:

Majority of companies think …

Proposal 1: CR...

# Conclusion

The following is proposed:

Proposal 1: CR...

# References

R3-213709, Discussion on F1-U Delay Measurement for QoS Monitoring, Samsung, Verizon Wireless

R3-213710, Correction of F1-U delay measurement for QoS monitoring 1, CR0122r TS 38.425, Samsung, Verizon Wireless

R3-213711, Correction of F1-U delay measurement for QoS monitoring 2, CR0123r TS 38.425, Samsung, Verizon Wireless