3GPP TSG-RAN WG3 #113-e	R3-214151

16 – 26 Aug 2021

Agenda Item:	9.3.2.2

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on Mobility Between DC and SA

Document for:	Approval

# Introduction

CB: # 17_DirectDataFwd_DC

- Discuss which of the two options is preferable for configuration of direct path availability in the involved nodes?

Option 1: Source MeNB is configured by OAM with all the direct path availability information for data forwarding:

Option 2: Source MeNB and source SgNB are configured by OAM on whether each node has a direct path available to the target NG-RAN node.

If RAN3 prefers Option 2, analyze on the signaling solution for source MeNB to obtain from source SgNB its direct path availability information? Qualcomm

- Source MN decides direct forwarding path availability between the source SN and the target NG-RAN node without additional OAM configuration complexity should be selected? Support direct forwarding with: The target MN provides the source RAN node ID to the target SN; The target SN notifies the direct data forwarding availability indication to the target MN. The source MN provides the source SN ID to the target node; The target node provides the direct data forwarding availability indication to the source MN? Samsung, Huawei

- Capture agreements and provide CRs if agreeable

(HW - moderator)

Summary of offline disc in R3-214151

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion – 2nd round

After the first round discussion, there is still no convergence. The moderator proposes to have 2nd round discussion, with the following questions raised during the 1st round, or more focused.

Agree the following proposal:

Proposal 1: The additional scenarios (i.e. intra-system SN change, and intra-system handover involving MR-DC) are considered, and it is expected to have a common design for all handover scenarios involving MR-DC.

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. |
| Samsung | Yes |
| Nokia | As discussed before: we can surely discuss any scenario, but the solution design depends on particular needs. |

More questions are given in section 3.1/3.2/3.3.

## For direct data forwarding from NR SA to EN-DC HO

Question: Is it allowed that the target en-gNB is configured with direct path availability with its neighbor nodes by the OAM, so as to support the direct data forwarding between the source NG-RAN node and target en-gNB?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. In our understanding, this was already agreed/confirmed at last meetings, e.g., Scenario 1 (both MN and SN have direct forwarding): Direct data forwarding to/from SN is supported. |
| CATT | Yes |
| Samsung | Yes The target en-gNB may also serve as a standalone gNB for other UEs. Whether it has direct forwarding path with its neighbors should be configured. It’s an existing function. |
| Nokia | Yes, this is not prohibited, though it would be awkward to provide such configuration to the en-gNB, which is not allowed to control HOs. Regarding Samsung’s comment that the same node can serve at the same time as a en-gNB and SA gNB. I am not sure about it, but hasn’t RAN3 always assumed it is up to implementation and thus logically the two nodes remain separated? If not, can I be reminded relevant agreements in RAN3? |

Question: About the OAM complexity, two options are already discussed.

- Option 2: target MN - the target MeNB is configured by OAM with the direct forwarding path availability information between neighboring source nodes and the neighboring target SgNB nodes (i.e. not relevant to itself).

- Option 3: target SN - the target SN is configured by OAM with direct forwarding path between itself and neighboring source nodes. The neighbour target SgNBs must be configured separately with the direct forwarding path availability information to the possible targets of the MN.

Do you agree that that option 2 has higher burden than option 3 in terms of OAM complexity.

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. |
| CATT | Yes |
| Samsung | Yes |
| Nokia | The burden is the same – either of the nodes has to be configured. Actually, onsidering that the en-gNB does not control HO mobility, option 3 seems more awkward… |

## For direct data forwarding from EN-DC to NR SA HO

Question: Is it allowed that the direct data forwarding is possible between the source SN and target NG-RAN node?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. In our understanding, this was already agreed/confirmed at last meetings, e.g., Scenario 1 (both MN and SN have direct forwarding): Direct data forwarding to/from SN is supported. |
| CATT | Yes |
| Samsung | Yes The source SN may also serve as a MN for other UEs. Whether it has direct forwarding path with its neighbors should be configured. It’s an existing function. |
| Nokia | Yes. Direct data forwarding may surely be possible, but it does not mean the information about availability of the path is also in the en-gNB – that may be configured in the MN. |

Question: About the OAM complexity, two options are already discussed.

- Option 1: source MN - the source MN is configured by OAM with the direct forwarding path availability information between the source SN and the target node (i.e. not relevant to itself).

- Option 2/3: source SN/target node - the source SN or the target NG-RAN node is configured by OAM with the direct forwarding path between itself and neighboring nodes.

Do you agree that option 1 has higher burden than option 2/3 in terms of OAM complexity.

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. |
| CATT | Yes |
| Samsung | Yes |
| Nokia | The burden is the same – the number of relations to configure is the same, irrespectively which node is configured. |

## Potential way forward

Question: Do you still have strong concern to introduce specification update (e.g., option 3 for handover from NR SA to EN-DC HO)? If so, is Rel-17 specification update acceptable?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Nokia | The critical point of the discussion is: can en-gNB and SA gNB share information/configuration? Or perhaps it has already been agreed – I would then like to be reminded the relevant agreement. So far, it seems to me that RAN3 assumes them being separate logical nodes, don’t we? |

# Discussion – First round

The following agreements and progress have been made at last RAN3 meetings.

RAN3-111-e meeting Agreement: Consider solution for all the following data forwarding scenarios of handover between SA and NSA:

- Scenario 1: both MN and SN have direct forwarding

- Scenario 2: MN has direct forwarding, SN has no direct forwarding

- Scenario 3 (FFS): MN has no direct forwarding, SN has direct forwarding

- Scenario 4: neither MN nor SN has direct forwarding.

RAN3-112-e meeting agreements on SN data forwarding, and open issues:

Scenario 1 (both MN and SN have direct forwarding): Direct data forwarding to/from SN is supported.

-	In SA to NSA HO, target MN receives the SN forwarding address from SN Addition Request Ack and provides the address to source for direct data forwarding.

-	In NSA to SA HO, Source MN sends the received direct forwarding address for SN terminated bearer to source SN e.g. in SN Release Request.

Scenario 2 (MN has direct forwarding, SN does not have direct forwarding): SN data is forwarded via MN.

-	In SA to NSA handover, target MN provides its own forwarding address to source and forwards received data to SN.

-	In NSA to SA handover, source MN provides its own address to source SN for data forwarding e.g. in SN Release Request.

Scenario 3 (MN does not have direct forwarding, SN has direct forwarding): It is FFS whether signaling solution is needed

Scenario 4 (Neither MN nor SN has direct forwarding): no need for further enhancement.

In inter-system handover, source node does not consider the availability of SN direct forwarding in setting “Direct Forwarding Path Availability” IE of S1/NG Handover Required message.

1) Issues: which nodes may detect availability of direct routing automatically and how this is achieved? Is configuration of the availability of the direct routing easier in the involved nodes than in others? Is configuration of direct forwarding availability between neighbour and neighbour’s neighbour feasible?

2) Once the above is acknowledged and confirmed, FFS whether signaling solution is needed for any of the above scenarios?

To be continued...

In the following, we take each related question in a separate section.

## Direct data forwarding from NR SA to EN-DC HO

R3-213925 discussed and provided the following open issue, with three options.

The open issue is which node decides direct forwarding path availability between the source NG-RAN node and the target en-gNB and how.

- Option 1: Source NG-RAN node

- Option 2: Target MN

- Option 3: Target SN

Wherein it is analyzed that the option 1 is not possible, since the target node decides whether a SN and which SN will be configured. The moderator tends to agree and excludes it first.

### Option 2: Target MN

For option 2, this requires the target MeNB to be configured by OAM with the direct forwarding path availability information between its two neighbors i.e. between the source NG-RAN node and the target SgNB.

Many papers think it brings much burden to OAM.

- In R3-213925, the OAM configures the neighbour list relationship regarding the direct data forwarding is a new requirement. The configuration complexity should be evaluated. To cover all the scenarios and the number of base stations in high frequency, perhaps it’s a great burden for operators to configure the connectivity of two neighbours in one node.

- In R3-213369, depending on number of possible SgNBs which could be large in certain deployments – for example, a macro MN node with a number of pico SN nodes – the OAM configuration burden can be significant.

- In R3-213752, to cover all the scenarios and the number of base stations in high frequency, perhaps it’s a great burden for operators to configure the connectivity of two neighbours in one node.

Question: May option 2 introduce great burden towards OAM for direct data forwarding from NR SA to EN-DC?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. OAM could be always regarded as last resort or default approach. But in this particular case, indeed this brings much configuration burden. |
| Qualcomm | Yes. Target MN needs to be configured with neighbors’ neighbors’ direct forwarding availability information. The complexity would be increased from the order of N to the order of N^2. The burden would be even serious in inter-vendor deployment. |
| Samsung | In the macro base station coverage, there could be many small base stations for capacity improvement. It’s a big burden to configure the macro base station whether it’s two neighbors have direct interface considering the number of small base stations. To configure whether a node has direct interface with its neighbor is an existing function e.g. NRT in stage 2. But to configure a node whether it’s two neighbors has direct interface is an additional requirement. |
| Nokia | All options require exactly the same burden. The burden is the same irrespectively from the node that needs to be configured. If it is the target MN, it needs to have configured as many relations as the en-gNB, if it is the en-gNB. Please note, some companies assume the en-gNB must be always configured with the direct path availability, and they then consider configuring the MN as additional burden. This is incorrect assumption, in our opinion: the en-gNB is not independent node and it does not control HOs, so there is absolutely no reason to have it configured with the direct path availability. Therefore, the MN is the only node that requires configuration. |
| ZTE | Yes It will bring great burden. |
| Ericsson | Agree with Nokia. Examples given to justify that one node adds an higher burden on OAM if it needs to be configured with direct path availability are deployment-dependent. Such deployment are of course possible, but does not cover all the possibilities, where most of the time the burden is similar. And at equal complexity, MN configuration is preferred. |
| CATT | Yes |

Moderator’s summary:

Four companies agree that the option 2 (target MN decides) introduces great burden towards OAM for direct data forwarding from NR SA to EN-DC.

Two companies think that all options have equal burden, among which one company think that the en-gNB should not be configured with the direct path availability given it is not an independent node.

### Option 3: Target SN

For option 3, the target SN just decides whether it has direct forwarding path with the source node based on the OAM configuration. Note that for single-connectivity to single connectivity handover case, the node is already aware of the direct link with its neighbor nodes.

Question: Do you agree that the target SN decides whether it has direct data forwarding path with the source node for handover from NR SA to ENDC?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. The option 3 can be considered, either as a supplemental approach on top of OAM based, or a solution when OAM is not workable. |
| Qualcomm | Yes |
| Samsung | Yes |
| Nokia | No. What does it mean “it decides”? It doesn’t have any special method to detect the availability of the direct path (all the methods are equally available for the MN). Therefore, that “deciding” requires OAM-based configuration. And this is equally the same burden as in case of configuring the MN. On the other hand, configuring a non-standalone node that does not control any HOs is illogical. Having the choice of configuring the en-gNB or the MN, we think configuring the MN is more logical. |
| ZTE | Yes |
| Ericsson | No SN should not be able to take decisions on HO. MN is in charge. In general, splitting the responsibility between 2 independent nodes, when not necessary, brings complexity (e.g. error cases to implement all possible interactions, …) and interoperability issues. |
| CATT | Yes |

Moderator’s summary:

Four companies agree that target SN decides whether it has direct data forwarding path with the source node for handover from NR SA to ENDC, based on the OAM configuration.

Two companies don’t agree, and think configuring the SN with direct path is illogical/complicated.

For option 3, R3-213924 and R3-213752 provides the following specification change.

- The target MN provides the source RAN node ID to the target SN;

- The target SN notifies the direct data forwarding availability indication to the target MN.

R3-213369 has the following observation. Maybe the opponent company can provide more information.

- Observation 3. Regarding specification impact of Proposals 3-6 for supporting direct data forwarding, there are no ASN.1 changes involved but text changes for clarification are likely required (Table 2-2).

Question: For option 3, do you agree the following specification impact for direct data forwarding from NR SA to ENDC?

- The target MN provides the source RAN node ID to the target SN;

- The target SN notifies the direct data forwarding availability indication to the target MN.

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Qualcomm | Yes |
| Samsung | Agree |
| Nokia | No. It is not needed, if the configuration burden is the same for option 2 and option 3. |
| ZTE | Yes |
|  | Not needed |
| CATT | Yes |

Moderator’s summary:

Four companies agree this proposal, while two companies don’t. .

## Direct data forwarding from EN-DC to NR SA HO

R3-213925 discussed and provided the open issue, with the following options.

The open issue is which node decides direct forwarding path availability between the source SN and the target NG-RAN node and how.

There are three possible options:

- Option 1: Source MN

- Option 2: Source SN

- Option 3: Target NG-RAN node

### Option 1: Source MN

In option 1, this requires the source MN to be configured by OAM with the direct forwarding path availability information between its two neighbors i.e. between the source SN and the target NG-RAN node. For example, for scenario 1, the MN needs to know the direct path exists between the source SN and target NG-RAN node, but not for scenario 2.

Many papers propose it may bring much burden to the OAM.

- In R3-213925, to cover all the scenarios and the number of base stations in high frequency, perhaps it’s a great burden for operators to configure the connectivity of two neighbours in one node.

- In R3-213369, no signaling impact exists for this option. Source MeNB needs to be configured with direct path availability of each of the possible source SgNBs. The OAM configuration burden can then be significant.

- In R3-213752, to cover all the scenarios and the number of base stations in high frequency, perhaps it’s a great burden for operators to configure the connectivity of two neighbours in one node.

Question: May option 1 introduce great burden towards OAM for direct data forwarding from EN-DC to SA NR?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. Same comment as section 3.1.1: OAM could be always regarded as last resort or default approach. But in this particular case, indeed this brings much configuration burden. |
| Qualcomm | Yes. Same reason as SA to NSA HO in section 3.1.1. |
| Samsung | Yes. Same reason as SA to NSA HO in section 3.1.1. |
| Nokia | No. Same reason as SA to NSA HO in section 3.1.1. |
| ZTE | Yes |
| Ericsson | All options are equal in terms of configuration effort |
| CATT | Yes |

Moderator’s summary:

Four companies agree that option 1 (i.e. source MN decides) introduce great burden towards OAM for direct data forwarding from EN-DC to SA NR.

Two companies don’t agree.

### Option 2/3: Source SN/Target NG-RAN node

In option 2 and 3, the source SN or the target NG-RAN node decides whether itself has direct forwarding path with its neighbor.

Companies can provide views, and leave the detailed signaling to the next question, considering the answers to Section 3.2.1.

Question: Is the option2/3 based solution needed for direct data forwarding from ENDC to SA?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. Same comment as 3.1.2: The option2/3 based solution can be considered, either as a supplemental approach on top of OAM based, or a solution when OAM is not workable. |
| Qualcomm | Yes |
| Samsung | Yes |
| Nokia | No. Same reason as SA to NSA HO in section 3.1.1: neither the NG-RAN node nor the en-gNB can “decide”, because there is no single-connectivity mobility between them – they have to be configured in the same way as the MN. |
| ZTE | Yes |
| Ericsson | No. No benefit |
| CATT | Yes |

Moderator’s summary:

Four companies agree this proposal, while two companies don’t.

For option 2 (Source SN):

- In R3-213369, it cited the previous paper that the source MeNB uses the SN Modification procedure to obtain from source SgNB information regarding whether source SgNB has a direct path to the target NG-RAN

- In R3-213924, it will bring handover delay due the query procedure before handover.

For option 3 (The Target NG-RAN node):

In R3-213924 and R3-213752, the following specification changes are needed:

- The source MN provides the source SN ID to the target node;

- The target node provides the direct data forwarding availability indication to the source MN.

In addition, R3-213370 proposes changes for X2 to support DL direct data forwarding from source SgNB to target NG-RAN node in EN-DC to NR SA inter-system handover. Maybe the component company can provide more information.

Question: Is option 2 or option 3 or R3-213370 your preferred solution for direct data forwarding from ENDC to SA NR?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Option 3 |
| Qualcomm | Option 2 On “In R3-213924, it will bring handover delay due the query procedure before handover”, this is not an issue because source MN anyway needs to query source SN for SCG configuration by SN Modification procedure. A potential benefit of this querying is: the info may be used for source MN to decide “Direct Forwarding Path Availability” IE in Handover Required message, for scenario 3. |
| Samsung | Option 3 Option 2 has the following drawbacks: Handover delay. Regarding Qualcomm comments “…this is not an issue because source MN anyway needs to query source SN for SCG configuration by SN Modification procedure”. The query procedure is only used in some scenario, not ALWAYS. Direct forwarding can only be supported in case both MN and SN has direct forwarding path with the target. This will bring limitation for direct data forwarding. In case MN has direct forwarding path but SN hasn’t, data is forwarded from SN->MN->target for SN terminated bearers. |
| Nokia | Since configuration burden in all cases is the same, there is no need for special signalling. |
| ZTE | Option 3 Agree with Samsung. Option 2 may introduce handover delay. |
| Ericsson | Nothing is needed |
| CATT | Option 2 Besides the benefit raised by QC, there is following advantage of option 2: In case the source SN node has direct data forwarding path with target node while MN does not has, direct data forwarding could still be supported between source SN and target MN. Since we all know that for EN-DC scenario, most of the traffic may be configured in SN nodes, it is valuable to support the direct data forwarding between source SN node and target node. |

Moderator’s summary:

- vs 2 different companies views. No convergence yet.

## Additional scenarios and common design

In R3-213752, it proposes that the following scenario should be considered.

- Intra-system SN change for EN-DC and MR-DC connected with 5GC, as depicted in section 10.5 in TS 37.340

Meanwhile the moderator thinks that the intra-system handover involving the MR-DC should be considered as well. And a common design (either OAM or signaling based) is needed.

The moderator understands the agreed scenario imply that these new scenarios are already supported to some extent. But it is better to confirm this understanding among companies.

Question: Do you agree that the above scenarios (intra-system SN change, and intra-system handover involving MR-DC) should be considered? If so, a common design (either OAM or signaling based) is needed?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree, and a common design is necessary. |
| Qualcomm | Agree |
| Samsung | Agree |
| Nokia | This is all right, but should be decided only once common understanding of the situation with the inter-RAT HO is reached in RAN3. |
| ZTE | Agree |
| Ericsson | Fine. But not sure that this will change the situation |
| CATT | Agree |

Moderator’s summary:

It seems that we can agree that additional scenarios (intra-system SN change, and intra-system handover involving MR-DC) can be considered? And a common design is needed for all scenarios.

## Scenario 3 (MN has no direct forwarding, SN has direct forwarding)

The scenario 3 above is marked with FFS as follows. The moderator understands this is applicable both for EN-DC to NR SA handover, and NR SA to EN-DC handover.

- Scenario 3 (FFS): MN has no direct forwarding, SN has direct forwarding

R3-213752 proposes that scenario 3 is excluded from the analysis.

Question: Do you agree to exclude the scenario for direct data forwarding between ENDC and SA NR?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Qualcomm | This should be low priority. In this meeting, let’s focus on scenario 1 and 2. In scenario 2, MN helps SN for direct data forwarding. In scenario 3, theoretically, SN can help MN for direct data forwarding. |
| Samsung | No need to support this. Because 5GC will be impacted for supporting this scenario. |
| Nokia | Neutral. Technically speaking, this scenario may be as likely as other, so we can consider it. However, it does not impact the situation: still, the information about direct path availability needs to be configured in some node, and the most obvious one is the MN. |
| ZTE | Agree |
| Ericsson | Scenario is realistic so not sure why it should be excluded |

Moderator’s summary:

No need to exclude scenario3 now. Further discuss after scenario 1 and scenario 2 are clear.

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-213369 | SN direct data forwarding (Qualcomm Incorporated) | discussion |
| --- | --- | --- |
| R3-213370 | SN direct data forwarding (Qualcomm Incorporated) | CR1613r, TS 36.423 v16.6.0, Rel-16, Cat. B |
| R3-213752 | Direct data forwarding for mobility between DC and SA (Huawei, Samsung) | CR0553r2, TS 38.423 v16.6.0, Rel-16, Cat. F |
| R3-213924 | Direct data forwarding for mobility between DC and SA (Samsung, Huawei) | CR0651r, TS 38.413 v16.6.0, Rel-16, Cat. F |
| R3-213925 | Discussion on direct data forwarding for mobility between DC and SA (Samsung, Huawei) | discussion |

# Comments

The original question was incomplete, because it did not mention where the information about the direct routing is available.

There is no “single-connectivity to single-connectivity” between an NG-RAN node and an en-gNB – the latter can’t have single-connectivity.

[Moderator]:here it means that the target SN is configured by OAM about the direct link between itself and neighbor nodes.