3GPP TSG-RAN WG3 #113-e	R3-214152

Online, 16 – 26 August 2021

Agenda Item:	9.3.3

Source:	Samsung (moderator)

Title:	Summary of Offline Discussion on Lossless intra-system HO

Document for:	Approval

# Introduction

CB: # 18_ Lossless_Intra-systemHO

- For Lossless intra-system HO case:

Introduce new IEs to provide the “new mapping” configuration in a backwards compatible manner? Introduce an explicit data forwarding completion indication from CU-UP to CU-CP to trigger the remapping of DRBs, or release of unused resources? Nok

Or add QoS Flows Information To Be Updated? Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE

- Lossless Inter-gNB HO case and inter-RAT HO from NR to LTE case?

- Capture agreements and provide CRs if agreeable

(Samsung - moderator)

Summary of offline disc in R3-214152

# For the Chairman’s Notes

Propose the following:

Agreement:

Discuss how to indicate the Qos flow list accepted for data forwarding from source CU-CP to source CU-UP in CB#104.

# Discussion (2nd Round)

Based on feedback for 1st round, there is agreement to discuss how to indicate the Qos flow list accepted for data forwarding from source CU-CP to source CU-UP in CB#104.

For the first and second issue, there are no common understanding.

Considering the first issue is more critical, let continue to discuss the first issue in the second round.

For the solutions to provide both the old and new mappings to the target CU-UP during the bearer context setup procedure, there are three solutions:

Solution 1: Add a new “QoS Flows Information To Be Updated” IE to the E1AP BEARER CONTEXT SETUP REQUEST message, and the corresponding response “QoS Flows Information Updated” IE to the BEARER CONTEXT SETUP RESPONSE message. [5][6][7]

Solution 2: Add Enhanced DRB To Setup List to the E1AP BEARER CONTEXT SETUP REQUEST message, and the corresponding response “Enhanced DRB To Setup List Used” IE to the BEARER CONTEXT SETUP RESPONSE message. [1][2]

Solution 3: Using QoS Flows forwarded on the forwarding tunnel(s) in Data Forwarding Information Request to transmit the Qos flows which will be forwarded (source mapping) over the DRB tunnel. And using QoS Flows Information To Be Setup to transmit the Qos flows which are configured to this DRB at target side. In order to support scenario 3 (the number of DRB in source side is more than the number of DRB decided to be setup in the target side), a new IE e.g. “Source DRB Indication” is included in Bearer Setup Request message.

Companies are invited to reply whether they can accept Solution 1?

| Company | solution | comments |
| --- | --- | --- |
| Samsung | Yes | Solution 1 is clear one and doesn’t add redundant information. |
| Huawei | Yes |  |
| Nokia | No | As indicated in Q1 response, we see Solution 1 has fundamental issues. |

Companies are invited to reply whether they can accept Solution 2?

| Company | solution | comments |
| --- | --- | --- |
| Samsung | No | In order to transmit a Qos flow list, many unnecessary information are transmitted. |
| Huawei | No |  |
| Nokia | Yes |  |

Companies are invited to reply whether they can accept Solution 3?

| Company | solution | comments |
| --- | --- | --- |
| Samsung | Yes | Solution 3 reuse the existing IE as much as possible. |
| Huawei | First trying to understand how solution 3 works. | Solution 3 still needs specification update. So why not follow solution 1? Somehow it seems to us that the “ Source DRB Indication” is equivalent to the new QoS flow mapping list in solution 1. But not sure how to work for the following scenario. Source: DRB#1 – QFI1/QFI2; Target: DRB#1 - QFI1; DRB#2 – QFI2. So the CU-UP shall indicate to the CU-UP that DRB#1 is configured with the source DRB indication IE? |
| Nokia |  | At this point, it is unclear to us how Solution 3 is expected to work in different scenarios. |

# Discussion (1st Round)

## Solutions to provide both the old and new mappings to the target CU-UP during the bearer context setup procedure

For the solutions to provide both the old and new mappings to the target CU-UP during the bearer context setup procedure, there are two proposals:

Solution 1: Add a new “QoS Flows Information To Be Updated” IE to the E1AP BEARER CONTEXT SETUP REQUEST message, and the corresponding response “QoS Flows Information Updated” IE to the BEARER CONTEXT SETUP RESPONSE message. [5][6][7]

Solution 2: Add Enhanced DRB To Setup List to the E1AP BEARER CONTEXT SETUP REQUEST message, and the corresponding response “Enhanced DRB To Setup List Used” IE to the BEARER CONTEXT SETUP RESPONSE message. [1][2]

Solution 3: Using QoS Flows forwarded on the forwarding tunnel(s) in Data Forwarding Information Request to transmit the Qos flows which will be forwarded (source mapping) over the DRB tunnel. And using QoS Flows Information To Be Setup to transmit the Qos flows which are configured to this DRB at target side

Q1: Which solution are you ok in order to support lossless intra-system handover in CP-UP separation scenario?

| Company | solution | comments |
| --- | --- | --- |
| Samsung | Solution 1 | Solution 2 introduces too many redundant information. For lossless handover, the target needs to use the source Qos flow mapping to DRB mapping as the source for forwarded data. For other configurations e.g. RLC/MAC, the configuration at the target side could be used. So what is needed in the CU-UP is source and target mapping. In order to transmit a Qos flow list, many unnecessary information are transmitted. Therefore, Solution 2 is not preferred. |
| Intel | Solution 1 | Both works, but as for correction, we prefer the simplest approach with minimal impacts. |
| Huawei | Solution 1 | Agree with Samsung and intel. |
| Nokia | Solution 2 | As explained in R3-213479, The issue with Solution 1 is that not only is the existing meaning and handling of the legacy IEs modified, but it also introduces a new functional requirement to the gNB-CU-UP to be able to handle the same QFI value for multiple DRBs simultaneously and it also brings unclarity as to which DRBs belong to the “old mapping” and which refer to the “new mapping”. This is a new function for the gNB-CU-UP. Consider the following case. Old Mapping Configuration: DRB1: QFI1,QFI3 // DRB2: QFI2 New Mapping Configuration: DRB2: QFI1, QFI2 // DRB3: QFI3 With the encoding and procedural text proposed for Solution 1, DRB3 in the example above would be set as if it was part of the old configuration by using the legacy IEs even it is not, and also lead to a representation with duplicated QFI mappings to multiple existing DRBs. This is just one example, and there are several other scenarios that can also lead to these inconsistencies as well. This incurs new functional changes to existing gNB-CU-UP implementation, and which can be avoided with Solution 2. |
| ZTE | Solution 1 |  |
| Ericsson | Solution 3 | The only NBC concern brought by proponents of new signalling is that the QoS Flows forwarded on the forwarding tunnel(s) should be a subset of QoS Flows Information To Be Setup. But there is no specification text stating that this should be the case. The only drawback of solution 3 is that in some remapping cases (e.g. 3), only the QoS Flows forwarded on the forwarding tunnel(s) IE will contain relevant information. This can easily be solved by adding a QFI not established in other DRBs in the QoS Flows Information To Be Setup IE, or by asking the CU-UP to ignore this IE, or by indicating to the CU-UP that this DRB will be used for data forwarding only. Also, please note that stage-2 says “ Lossless delivery when a QoS flow is mapped to a different DRB at handover, requires the old DRB to be configured in the target cell”. Therefore, the old DRB has to be present in the target gNB, and this includes the target CU-UP. |

## “explicit data forwarding completion indication” from CU-UP to CU-CP

In order to timely release the unnecessary resources in the CU-UP, DU and the UE, a proposal is to include an explicit indication from CU-UP to CU-CP to notify that data forwarding has completed [1][2]. Subsequently, the CU-CP can trigger a modification accordingly to release the unused resources at CU-UP, DU and the UE.

Q2 do you think “explicit data forwarding completion indication” from CU-UP to CU-CP is needed?

| Company | Yes/No | Comments |
| --- | --- | --- |
| Samsung |  | We see the benefit to have this indication as claimed in the paper [1][2]. |
| Intel | Maybe | We also acknowledge the benefits to timely release the unused DRB in the UE and DU if the DRB is only used for handling forwarded datas in CU-UP and CU-CP decides no QoS flow is mapped after that. However, if we agree to have this explicit data forwarding completion indication, we think that it should be CU-CP who should configure CU-UP (per DRB basis) whether to send data forwarding completion indication or not. The reason is because (1) it is CU-CP who decides to perform next steps based on this indication; and (2) to ensure inter-operability. And if CU-UP is configured to do so, we prefer a new dedicated CU-UP initiated class-2 procedure, rather than re-using the class-1 CU-UP-initiated Bearer Context Modification procedure. |
| Huawei | No | We are not convinced to introduce the “ an explicit data forwarding completion indication from CU-UP to CU-CP” in solution 2. It seems the motivation is just for “release the unused resources at CU-UP, DU and the UE”, but the existing per DRB/session level inactivity notification seems sufficient. |
| Nokia | Yes, needed | Without this indication there are two shortcomings if we rely on the existing inactivity notification per DRB: The inactivity notification over E1 AP is controlled per UE, PDU or DRB. Therefore, if set per UE or PDU the notification would likely take much longer to be sent, given that all DRBs in the PDU, or in the UE need to be inactive for the configured time prior to sending this message. Thus, in multiple scenarios this signal will be issued too late. Even if the inactivity notification is set “per DRB”, there is no requirement that a gNB-CU-UP shall monitor inactivity for a DRB that is only used for data forwarding, Therefore, in an intervendor deployment, there is no guarantee that a gNB-CU-UP will ever send a message concerning the inactivity for DRBs that were established just for data forwarding. In this case as well, the resources would be left hanging at the gNB-CU-CP, gNB-DU and UE. In regard to the method on how to signal completion of data forwarding, we see acceptable both options (a) to reuse BEARER CONTEXT MODIFICATION REQUIRED as proposed, or (b) to introduce a new class 2 message. |
| ZTE | Neutral | The indication seems OK, but maybe not essential. |
| Ericsson | Not needed | If no fresh data from CN is arriving to the CU-UP for the old DRB, there is no drawback to keep it a bit longer (i.e. after all the data has been forwarded) in the CU-UP. CU-CP can then remove it by Bearer Configuration Modification, by taking some good margin, or by using inactivity monitoring. |

## How to indicate the Qos flow list accepted for data forwarding from source CU-CP to source CU-UP

Currently, it’s not possible for the source CU-CP indicated the Qos flow list accepted for data forwarding to the source CU-UP. [3][4] proposed a way forward.

Observation from Moderator:

The same problem was also identified in R3-213274/75/76 in agenda 9.3.4.1. Considering the issue is mainly related with PDU Session tunnel data forwarding. It’s better to discuss the issue in one place e.g in 9.3.4.1 together with R3-213274/75/76.

Q3 Is it ok to discuss this issue in 9.3.4.1 together with R3-213274/75/76?

| Company | OK/NOK | Comments |
| --- | --- | --- |
| Samsung | OK |  |
| Intel | OK | [3][4] are indeed a good catch. |
| Huawei | OK | This can be discussed in CB#104. As commented online, we acknowledge this issue. But the CR in [3,4] can not solve this. |
| Nokia | OK | OK to discuss as part of CB#104 |
| ZTE | OK |  |
| Ericsson | OK |  |

# Conclusion, Recommendations [if needed]

If needed

# References

| [1] R3-213479 | Discussion on Lossless intra-system HO in disaggregated architecture (Nokia, Nokia Shanghai Bell) |
| --- | --- |
| [2] R3-213480 | Lossless intra-system HO in disaggregated architecture (Nokia, Nokia Shanghai Bell) |
| [3] R3-213481 | Discussion on Lossless Inter-gNB HO data forwarding (Nokia, Nokia Shanghai Bell) |
| [4] R3-213482 | Lossless inter-gNB HO data forwarding (Nokia, Nokia Shanghai Bell) |
| [5] R3-213919 | Lossless intra-system HO in dis-aggregated gNB scenario (Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE) |
| [6] R3-213920 | Correction of intra-system HO in CP-UP separation scenario (Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE) |
| [7] R3-213921 | Correction of intra-system HO in CP-UP separation scenario (Samsung, Huawei, Intel Corporation, China Telecom, LGU+, ZTE) |