3GPP TSG-RAN WG3 #113-e	 R3-214201

16-26 Aug 2021

Online

Agenda Item:	19.2.2

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on CB: # 1902_Pos_RRC_INACTIVE

Document for:	Approval

# Introduction

This is the Sod for the following CB:

CB: # 1902_Pos_RRC_INACTIVE - Converge on whether RAN3 can proceed with solutions - If possible agree to TPs for Stg3 (HW - moderator) Summary of offline disc

# For the Chairman’s Notes

Propose the following:

# Discussion

Let’s go through the proposals from the papers in this AI one by one.

## Issues to be studied

In R3-213620, it is proposed RAN3 needs to work on solutions for following issues:

- How to deal with the UE-associated NRPPa message request when the UE is in Inactive state and camped within the last serving RAN.

- How to deal with the UE-associated NRPPa message request when the UE has reselected to a new gNB within the RNA in Inactive state.

- How to deal with UE reselecting to a new gNB (within RNA or not) when UE has already configured SRS transmission in Inactive state.

Comments on the proposal, please provided here.

| Company | Do you agree with the three issues to be studied? | Comment/Reason |
| --- | --- | --- |
| Samsung | Yes with comments | Our understanding is all of the three issues relates to NRPPa messages, which are triggered by UL related positioning, so this proposal can be summarized as “How to support UL positioning when UE is in RRC_INACTIVE state” as proposed by Samsung in section 3.9. |
| Huawei | Yes |  |

## UE resumes in last serving node in response to RAN paging

When NRPPa message is received for a inactive UE, the RAN node should trigger RAN paging in RNA. With this assumption, it is proposed that the NRPPa procedure would proceed normally when the UE resumes within the last serving RAN node in response to RAN paging.  No specification enhancements are required.

Comments on the proposal, please provided here.

| Company | Do you agree with the proposal above? | Comment/Reason |
| --- | --- | --- |
| Samsung | Yes to the “RAN paging” part. No to the “no enhancement are required” part | As shown in the paper R3-213620, “it is gNB’s decision to either keep the UE in Connected state (such as short report periodicity), or release UE back into Inactive state (such as long report periodicity).” If gNB decides to release UE back to Inactive state, In CU-DU split case, the CU should notify DU not release positioning related context to ensure positioning can be performed, as in currently spec, the DU will release all UE context when UE is sent to RRC_INACTIVE state, which means DU will not reserve UL resources for the positioning As samsung proposed in section 3.9 below: Proposal 3 gNB-CU should notify the gNB-DU not release the UE positioning context to support UL positioning in RRC_INACTIVE state. |
| Huawei | yes |  |

## UE resumes in a new node

There are two ways proposed for the enhancements to deliver the pending NRPPa message  in this case:

Option 1: The last serving RAN notifies the LMF by the failure message with a proper cause that the UE has moved out of the cell by NRPPa message and the LMF re-sends the request message to the serving RAN.

Option 2: The last serving RAN forwards the NRPPa message, such as the routing ID and the requested SRS transmission characteristics, to the new serving RAN via Retrieve UE context retrieve procedure.

Please provide your views and comments on above two options.

| Company | Which option do you prefer? | Comment/Reason |
| --- | --- | --- |
| Samsung | Option 1 with modification as follows: notify the LMF the serving cell is changed, FFS on message and IE Option 2 is also OK for us | I think this proposal is the same as samsung proposed in section 3.9 below: Proposal 4 RAN3 agree to discuss below options to support UL positioning in RRC_INACTIVE state when the serving gNB is changed: - Option 1, notify the LMF the serving cell/gNB is changed, and the LMF initiates a new UE associated connection with the new serving gNB, the NRPPa messages can be reused for the following procedures. In both proposals, option 1 has the same spirit, we slightly prefer option 1, but using which message and what IE are FFS. Option 2 in this proposal is also OK which will reduce positioning latency. |
| Huawei | Both, slightly prefer Option 2 | Option 2 would have lower latency. |

## UE doing UL SRS transmission moves to a new node

In this case, the UE needs to obtain the new SRS configuration in the new node. The two alternative solutions are similar as the one in section 3.3

Option 1: last serving node informs the LMF about the UE mobility and the LMF updates the new SRS configuration.

Option 2: last serving node transfers the SRS configuration to the new node in UE context retrieve.

In principle, the moderator assumes that the solution for this issue shall be aligned with the one in section 3.3, but please provide your views and comments also on above two options here.

| Company | Which option do you prefer? | Comment/Reason |
| --- | --- | --- |
| Samsung | Both are OK | As commented above |
| Huawei | Option1 | The mobility issue can be aligned with that in CONNECTED mode if Option 1 is selected. Editor to clarify that: Option 2 should be that the last serving node transfers the routing ID and Requested SRS transmission characters to the new node in the UE context retrieve. |

## Period configuration for deferred positioning

In R3-21367, it is proposed that:

Proposal 1: LMF can provide period of Deferred positioning to assist the gNB to decide whether to release the UE into RRC_INACTIVE, configure SDT for SRB2, or configure CG resource for SDT.

Please provide your views on above proposal.

| Company | Do you agree on above proposal? | Comment/Reason |
| --- | --- | --- |
| Samsung | Tend to agree | There should be new information to notify gNB that UE will perform positioning in RRC_INACIVE state, but FFS on what kind of IE, we may need more input from SA2. |
| Huawei | Not fully sure. | Configuring SDT, CG is RAN2 issue. The information required for SDT would be discussed in RAN2. LMF can suggest the gNB to release UE into RRCINACTIVE for SRS transmission (to distinguish with R16) if the LMF has the UE capability information of sending SRS in INACTIVE. |

## DL location measurements in inactive

In R3-21367, it is proposed that:

Proposal 2: The UE performs DL location measurements in RRC_INACTIVE based on stored assistance data. If the stored assistance data is not valid, the UE in RRC_INACTIVE can acquire valid assistance data based on existing mechanism.

Based on above proposal, no further enhancement is needed. This can also apply to RAT-independent positioning methods in RRC_INACTIVE.

Please provide your views on above proposal below.

| Company | Do you agree on above proposal? | Comment/Reason |
| --- | --- | --- |
| Samsung | Not sure | Our understanding is DL positioning measurements use LPP messages, so should this be discussed in RAN2 or SA2? |
| Huawei | Not sure | We think that it is a RAN2 topic and no RAN3 impacts. |

## Stage 2 procedure for positioning in inactive

A stage 2 procedure for inactive positioning is proposed in R3-21367, like:

Please provide your views on above message flow.

| Company | Do you agree on the stage 2 procedure above? | Comment/Reason |
| --- | --- | --- |
| Samsung | Not sure | Maybe it’s too early to have this |
| Huawei | No strong view |  |

## On-going positioning session handling

In R3-213853, the handling of on-going positioning session when UE enters RRC_INACTIVE is discussed, e.g., the E-CID positioning measurement. And the following proposals are made:

Proposal 1: In order to allow LMF for a smart decision when the UE goes into RRC_INACTIVE during on-going measurement session, an indication is needed to be reported to the LMF during the failure messages

Proposal 2: Define two new cause values in NRPPa Cause: “UE in RRC_INACTIVE state” and “UE context released”.

Please provide your views and comments on above proposals.

| Company | Do you agree on above proposal 1 and 2? | Comment/Reason |
| --- | --- | --- |
| Samsung | Tend to No | If gNB knows this UE will perform positioning in RRC_INACTIVE state, it should not release the positioning related context, thus the positioning failure will be avoided. |
| Huawei | Partly. | The first one should be OK. For the second one, if there is ongoing positioning session for UEs, the gNB will not send it to idle? |

## Delivery of LPP message to/from inactive UE

In R3-213970, the delivery of LPP message from/to inactive UE are discussed.

The first proposal is to cofirm the scenarios as proposed in proposal 1:

Proposal 1, RAN3 to consider below issues for positioning in RRC inactive state.

- How to delivery UL and DL LPP messages when UE is in RRC_INACTIVE state.

- How to support UL positioning when UE is in RRC_INACTIVE state

Please provide your views and comments on above proposals.

| Company | Do you agree on above proposal 1? | Comment/Reason |
| --- | --- | --- |
| Samsung | Yes | Considering companies’ views are very diverged, we suggest RAN3 firstly decide what kind of issues are necessary and should be addressed mainly in RAN3, in our views, regardless of how RAN2/SA2 work, above two issues should be discussed and addressed in RAN3. |
| Huawei | Partly | UL LPP: NO. The UL LPP message delivery is RAN 2 issue. And there is no LMF selection issue, because the Routing ID is included in the NAS message, with which the AMF can know which LMF to delivery LPP message. DL LPP: YES. The DL LPP message may need to exchange NAS (containing LPP) in UE context exchange and RRC Release message to delivery LPP message to the UE in INACTIVE state. UL positioning: OK to discuss the mobility. |

The second issue is the UL LPP messages delivery.  Two scenarios are listed:

Scenario 1: the serving gNB is unchanged (i.e. last serving gNB)

Scenario 2: the serving gNB is changed (i.e. new serving gNB)

It is concluded that scenario 1 has no additional impact if we don’t consider SDT part. For scenario 2, three solutions are proposed to make sure that he LPP message can be transmitted to the right LMF, below options can be further discussed:

- Option 1: UE provides the LMF information along with LPP message

- Option 2: The new serving gNB requests the last serving gNB for LMF information

- Option 3: The new serving gNB transmits the LPP message as a container to the last serving gNB through Xn interface.

Proposal 2 RAN3 agree to discuss below options to support UL LPP messages successful delivery when the serving gNB is changed.

- -	Option 1: UE provides the LMF information along with LPP message

- -	Option 2: The new serving gNB requests the last serving gNB for LMF information

- -	Option 3: The new serving gNB transmits the LPP message as a container to the last serving gNB through Xn interface.

Please provide your views and comments on above scenarios and proposal.

| Company | Comment |
| --- | --- |
| Samsung | Agree with the proposals. When the serving gNB is changed and UE performs positioning in RRC_INACTIVE state, the new serving gNB should know how to deliver the LLP messages to the right LMF, enhancements are needed, all of the three options can be further discussed. |
| Huawei | There is no LMF selection issue, because the Routing ID is included in the NAS message, with which the AMF can know which LMF to delivery LPP message. |

For DL LPP message related to UL positioning, when the gNB is in split architecture, it states that the gNB-CU should notify the gNB-DU not release the UE positioning context (i.e. SRS configuration).

when the serving gNB is changed, the SRS should be re-configured to UE by the new serving gNB, below options can be considered:

- Option 1, notify the LMF the serving cell/gNB is changed, and the LMF initiates a new UE associated connection with the new serving gNB, the NRPPa messages can be reused for the following procedures.

- Option 2, new serving gNB exchange NRPPa messages with the LMF through the last serving gNB.

Proposal 3 gNB-CU should notify the gNB-DU not release the UE positioning context (i.e. SRS configuration) to support UL positioning in RRC_INACTIVE state.

Proposal 4 RAN3 agree to discuss below options to support UL positioning in RRC_INACTIVE state when the serving gNB is changed:

- Option 1, notify the LMF the serving cell/gNB is changed, and the LMF initiates a new UE associated connection with the new serving gNB, the NRPPa messages can be reused for the following procedures.

- Option 2, new serving gNB exchange NRPPa messages with the LMF through the last serving gNB.

Please provide your views and comments on above scenarios and proposal.

| Company | Comment |
| --- | --- |
| Samsung | Agree with both proposals. For proposal 3, as we commented in section 3.2, if positioning in RRC_INACTIVE state, DU should not release positioning related context, otherwise we cannot say positioning in RRC_INACTIVE is supported, so enhancements are needed. For proposal 4, as we commented in section 3.3, to support UL related positioning in RRC_INACTIVE, when the serving gNB is changed, the LMF should know the new serving cell and initiates the following positioning procedures, e,g. positioning activation or measurement request procedures. |
| Huawei | P3: Seems OK. P4: The discussion for mobility issue can be discussion in issue 3.4 |

## LS RAN2 the progress on this topic

Do you agree to send a LS to RAN2 to inform them the RAN3 progress on this topic at this meeting?

| Company | Do you agree to send the LS? | Comment/Reason |
| --- | --- | --- |
| Samsung | It depends | It depends on whether RAN3 have any progress on this topic. |
| Huawei |  | Let’s see how far we can go at this meeting. |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-213620 | (TP for POS BL CR for TS 38.455): Discussion on RRC inactive positioning (Huawei) | Discussion |
| --- | --- | --- |
| R3-213675 | Positioning for UEs in RRC_INACTIVE state (CATT) | discussion |
| R3-213853 | Discussion on support of RRC-Inactive Positioning (Ericsson) | other |
| R3-213970 | Positioning in RRC inactive state (Samsung) | discussion |