3GPP TSG-RAN WG3 #113	R3-214217

16 - 26 August 2021

Online

Agenda Item:	22.3.2

Source:	Nokia, Nokia Shanghai Bell - Moderator

Title:	Summary of Offline Discussion – MBS Mobility Non-Supporting

Document for:	Approval

# Introduction

This is the SOD document for the following come back:

CB: # MBS7_MobilityNonSupporting

- Further discuss on the open issues and WA, and check SA2/RAN2 progress

- Two cases: handover from non-MBS supporting nodes to MBS supporting node and handdover from MBS supporting nodes to non-MBS supporting node

- How to stop data forwarding from source gNB during handover?

- Stage2/stage3 TPs and check details, split work, if needed

- Capture agreements and open issues

(Nok - moderator)

Summary of offline disc in R3-214217

# For the Chairman’s Notes

Propose the following:

Agree TP … .

# Discussion

## Handover from MBS supporting to Non-supporting Nodes

Trigger to switch from shared delivery to individual delivery

Last RAN3#112 meeting, RAN took a working assumption as follows:

WA: MBS support Indicator is included in Path Switch Request Transfer sent by an MBS supporting node to indicate support

The idea is that the above enables an SMF to detect when the target gNB is a non-MBS supporting node through the absence of this MBS support indicator. SMF then triggers switch from shared delivery to individual delivery.

Q1: Can we change the working assumption into an agreement: MBS support Indicator is included in Path Switch Request Transfer sent by an MBS supporting node to indicate support

| Company | Comment |
| --- | --- |
| Nokia | Yes. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

When to stop Data forwarding

As a legacy node, the target gNB needs to receive end marker packets to stop data forwarding. The question is how and when the source gNB will be able to generate these end marker packets.

There are several options proposed for source gNB to determine to generate these end markers:

- Source gNB stops data forwarding at receiving the Xn Release Context message from target gNB – R3-213240.

- Source can decide to stop forwarding based on internal timer – R3-213988.

- Source gNB receives an end marker packet from the CN (e.g. could be over the N3 shared tunnel or the associated N3 unicast tunnel) – R3-213739

Q2: which trigger do you foresee for source gNB to stop data forwarding from source to target?

| Company | Comment |
| --- | --- |
| Nokia | Timer is the basics but not very good. Continue discussions on end marker to improve if found feasible. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

How and When the source gNB learns that the target gNB does not support MBS

According to previous agreements, data forwarding is supported to minimize data loss and the source gNB needs to know that the target is not supporting at the latest when starting data forwarding in order to know that it needs to switch the MBS QFI into unicast QFI in the forwarded packets for example.

According to current RAN3 assumptions, the source gNB sends the MBS information + legacy associated unicast information to the target gNB and the source gNB will be able to detect that the target is non supporting through the missing MBS information in the Xn Handover Request Acknowledge.

Q3: Can we agree that source gNB knows for sure that target is not supporting at the end of the handover preparation through the content of the handover preparation response message?

| Company | Comment |
| --- | --- |
| Nokia | Yes. For example, if the handover preparation response message does not contain MBS information, the source can infer that he target gNB is non supporting. |

The real question is whether means shall be provided for the source gNB to determine whether the target is non supporting before the handover takes place. According to R3-213739, the source gNB should know before the handover to avoid a “full configuration” and the way to avoid a full configuration is to have the source gNB setting up a kind of “dormant DRB” in advance which gets activated during the handover if an handover takes place.

Q4: Do you think like tdoc R3-213739 that means shall be provided for the source gNB to determine before the handover whether the target gNB is supporting or not and for what reason?

| Company | Comment |
| --- | --- |
| Nokia | Not yet convinced that full reconfiguration is entailed. We could ask RAN2 to check this point by LS. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

## Handover from non-MBS supporting to MBS supporting

Q5: Can we agree that legacy Xn/NG handover takes place and then the target SMF can determine whether to switch to shared delivery based on the MBS support indicator received from target gNB?

| Company | Comment |
| --- | --- |
| Nokia | Yes. In our view is aligned with TS 23.247 [1]. |

Moderator’s summary:

Majority of companies think …

Proposal 1: TP...

# Conclusion

The following is proposed:

Proposal 1: TP...

# References

TS 23.247, Architectural Enhancements for 5G Multicast-Broadcast Services