3GPP TSG-RAN WG3 #113-e							R3-214181

16 August – 26 August 2021

Online

Agenda Item:	14.2

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on MRDC2 - SCG (de)activation

Document for:	Approval

# Introduction

CB: # MRDC2_SCGActivation_Deactivation

- Further discussion on the open issues left in R3-212784 and check RAN2 progress

- Partial rejection or full rejection? New cause value?

- For SCG (de)activation during SN addition, if SN can reject the SCG (de)activation when accepting the SN addition?

- Which node is responsible for the SCG activity detection and if any enhancement to E1/F1/Xn interface is needed?

- Impact on F1 and E1 interfaces?

- Capture agreements as stage2/stage3 CRs and check details, split work, if needed

- List open issues for next meeting in the summary

(ZTE - moderator)

Summary of offline disc in R3-214181

It is proposed to divide the discussion into two phases:

-	Phase 1: Identify the issues to be discussed in RAN3

Deadline: Please provide your views by 11:00am UTC Tuesday August 17th

-	Phase 2: Further discussion to capture agreements and open issues

Deadline: TBD pending on the outcome of Phase 1

# For the Chairman’s Notes

[TBD]

# Phase 1 discussion

Please note that the terms partial rejection and full rejection in the discussion part refer to the following meanings:

Partial rejection: SCG (de)activation request is rejected when accepting the whole procedure.

Full rejection: The whole procedure is rejected due to the rejection of SCG (de)activation request.

## MN initiated SN modification procedure

In the last RAN3 #112 e-meeting, the following WA was made for MN initiated SN modification procedure.

WA: For SCG (de)activation during MN initiated SN modification, SN can reject the SCG (de)activation when accepting SN modification request.

Note that in the RAN3 #111 e-meeting, it was agreed to add a new IE with two codepoints in the SN modification response message, which also indicates that partial rejection shall be supported.

Add a new IE, e.g., “SCG activation result” with two codepoints in the SN modification response message in order to indicate the SCG is activated or de-activated.

Since majority companies propose to support partial rejection according to the contributions, moderator suggests to confirm the above WA as an agreement, which is is also consistent with the agreement made in the RAN3 #111 e-meeting.

Question 1: Do companies agree to confirm the WA on supporting partial rejection for SCG (de)activation during MN initiated SN modification as an agreement?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | It’s not necessary to reject the whole modification procedure if the SCG (de)activation request is rejected by SN. Furthermore, confirming this WA will also keep align with the previous agreement for SN modification procedure. |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |

## MN initiated SN addition procedure

### 3.2.1 Partial rejection or full rejection

In the last RAN3 #112 e-meeting, the following agreement was achieved for MN initiated SN addition procedure.

In the SN addition request message, to set SCG (de)activated, two codepoints are supported (i.e. one for SCG activation, another for SCG deactivation).

Whether to support partial or full rejection for SCG (de)activation during MN initiated SN addition was further discussed into two sub-scenarios in the last meeting [1]:

- Sub-scenario 1: SCG activation during SN addition

- Sub-scenario 2: SCG deactivation during SN addition

Since majority companies propose to support partial rejection for Sub-scenario 2 according to the contributions, and agree that there is no harm for SN to reject the SCG deactivation during SN addition according to the company replies in [1], moderator suggests to agree that SN can reject the SCG deactivation when accepting SN addition (i.e. partial rejection).

Question 3: Do companies agree that SN can reject the SCG deactivation when accepting SN addition (i.e. partial rejection)?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | In case of inter-MN handover without SN change, the SN knows the data status for SN terminated bearer during SN addition. Thus SN can reject SCG activation or deactivation while accepting SN addition in this case. |
| Lenovo, Motorola Mobility | Yes | It does not seem harmful. |
| CATT | Yes |  |

According to the contributions and company replies in [1], half companies think that partial rejection shall be supported for rejecting SCG activation during SN addition, and the other half companies think full rejection shall be supported. As stated in [2][14], if RAN3 agrees to support partial rejection for SCG deactivation during SN addition, it would be better to have a unified solution for the SCG (de)activation during SN addition, i.e., RAN3 agrees to support partial rejection for SCG activation during SN addition. After all, MN can trigger SN release or SN change.

Moderator’s view: If receiving the SN addition request acknowledge message including “de-activate”, it is the MN to make the further decision (other than the SN refuses the SN addition procedure"), i.e., the MN can further initiates SN release procedure to this SN and initiates another SN addition procedure with another SN.

Question 4: Do companies agree that SN can reject the SCG activation when accepting SN addition (i.e. partial rejection)?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | In case of inter-MN handover without SN change, the SN knows the data status for SN terminated bearer during SN addition. Thus SN can reject SCG activation or deactivation while accepting SN addition in this case. It seems too complicated if full rejection is supported for SCG activation while partial rejection is supported for SCG deactivation during SN addition, and a unified solution may be more straightforward and simple. |
| Lenovo, Motorola Mobility | Yes | Although it seems rejecting SCG activation while accepting the SN addition will make the SN addition wasted, smart NW implementation can use full rejection whenever SN wants. To have a unified solution considering Question 3 and not making the design too fragmented, we are fine to support partial rejection for SCG activation during SN addition. |
| CATT | Yes | Support using the unified solution |

### 3.2.1 SCG (de)activation indicator design

In moderator’s view, as long as RAN3 agrees to support partial rejection for Sub-scenario 1 of MN initiated SN addition, a new IE with two codepoints needs to be added in SN modification request acknowledge message to indicate the SCG is activated or deactivated.

Question 4: Do companies agree to add a new IE with two codepoints in SN modification request acknowledge message to indicate the SCG is activated or deactivated?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | If partial rejection is supported, a new IE with two codepoints is required. |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |

## SN initiated SN modification procedure

### 3.3.1 Activity Notification

In the last RAN3 #112 e-meeting, the following WA and agreement were achieved for SN initiated SCG (de)activation.

WA: RAN3 does not enhance Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation. RAN3 supports SCG (de)activation during SN initiated SN modification.

Considering that there seems no objection to confirm the above WA into an agreement in the contributions, the moderator suggests to confirm it as an agreement.

Question 5: Do companies agree to confirm the WA on not enhancing Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation as an agreement?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |

### 3.3.2 Partial rejection or full rejection

Another remaining issue for SN initiated SCG (de)activation during SN modification procedure is whether to support partial or full rejection. Slight majority companies believe that full rejection shall be supported, and a critical issue was acknowledged to support partial rejection for SN initiated SN modification procedure in the last meeting as stated in [1][2][14]. There is a principle that MN does not interpret SN RRC message from SN, but include it into MN RRC message as a container to UE directly. If partial rejection is supported for SN initiated SCG (de)activation, SN RRC message shall be modified otherwise UE behavior is not aligned with SCG state. Therefore, only full rejection should be allowed for SN initiated SCG (de)activation in order to keep the above principle in Rel-15.

Question 5: Do companies agree not to support partial rejection for SN initiated SCG (de)activation during SN modification procedure? If no, how to solve the above mentioned issue?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | The SN initiated modification case is different from the MN initiated modification case, the principle is still kept if we support partial rejection in MN initiated modification. We shall not just simply reuse the rejection principle of MN initiated modification for SN initiated modification. |
| Lenovo, Motorola Mobility | Yes | Full rejection is always supported if MN wants to reject the whole SN modification required procedure. So we suppose the question is asking not to support partial rejection. As explained by moderator, when the RRC container is sent together with the SCG (de)activation indicator in the same Xn message, we should avoid sending RRC container to UE if rejecting the SCG (de)activation. If RAN3 is not sure about whether the SCG (de)activation indicator in Xn message can be sent without SN RRC container, RAN3 is suggested to send a LS to RAN2. |
| CATT | Yes | Agree with ZTE comments as the reason. |

## New cause value

In the last RAN3 #112 e-meeting, the following agreement was achieved to introducing a new cause value. However, Some issues regarding the new cause value need to be further discussed.

A new cause value will be introduced to indicate the reason to reject SCG (de)activation. FFS what exactly value.

The first issue is when to use the new cause value. [2][9] believe that the new cause value shall only be used in the case that the whole procedure is rejected due to SCG (de)activation request failure, i.e. full rejection. However, [6][11][15] believe that if the request of SCG (de)activation is rejected during partial rejection, the rejection cause shall be provided to indicate the reason of rejecting.

Question 6: Companies are kindly asked which option below is preferred for the new cause value?

- It shall be used in the case that the whole procedure is rejected due to SCG (de)activation request failure

- It shall be used to indicate the rejecting reason of partial rejection for SCG (de)activation

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | If partial rejection is supported, the rejection of SCG (de)activation can be indicated via the response message. There is no need to use the new cause value for partial rejection. The new cause value shall only be used when the whole procedure is rejected due to the rejection of SCG (de)activation. |
| Lenovo, Motorola Mobility | 1) 2) | No strong view, it seems helpful to indicate the exact reason of SCG (de)activation during full or partial rejection. |
| CATT | 1) |  |

The next issue is the cause value design of the new cause value. According to the contributions, two options are provided.

-  Option 1: General cause value to indicate that the request is rejected due to the rejection of SCG (de)activation

-  Option 2: Specific reason to indicate the detailed reason for the rejection of SCG (de)activation

Question 7: Companies are kindly asked which option below is preferred.

- General cause value

- Specific cause value

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | SCG (de)activation is a simple function and it’s not necessary to include the specific rejection reason. This may cause unnecessary signalling and slow down the whole procedure. |
| Lenovo, Motorola Mobility | 2) | If the cause value is only “SCG (de)activation failure”, then it seems cannot be used for any other purpose. We consider it better to introduce cause value that can be used in other scenarios too, to be more future proof. |
| CATT | 1) | We prefer to use the option 1. If the detail cause value is introduced, many kinds value should be listed. |

## F1 interface related issues

In the last RAN3 #112 e-meeting, the following agreement was achieved for F1 interface.

F1 interface enhancement to support SCG (de)activation reuses the principle in Xn interface regarding: Codepoint design for SCG (de)activation for UE context setup Whether/how DU can reject the SCG (de)activation during UE context setup procedure Whether/how DU can reject the SCG (de)activation during UE context modification procedure

All companies agree to reuse the principle in Xn/X2 interface for F1 interface according to the contributions. Thus, moderator will propose mirror agreements for F1 interface after achieving agreements for Xn interface.

It is noted that the codepoint design for SCG (de)activation during UE context modification is not mentioned in the above agreement. Therefore, moderator suggests to add the agreement that the codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface.

Question 8: Do companies agree to add the agreement that the codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |

It is also noted that gNB-DU initiated UE context modification required procedure is also enhanced for SCG (de)activation in the agreed SCG BL CR to TS 38.473[19]. Therefore, moderator suggests to add the agreement that whether/how CU can reject the SCG (de)activation during UE context modification required procedure also reuses the principle in Xn interface.

Question 9: Do companies agree to add the agreement that whether/how CU can reject the SCG (de)activation during UE context modification required procedure also reuses the principle in Xn interface?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Lenovo, Motorola Mobility | No | In our understanding, it’s CU-CP that decides/triggers SCG (de)activation based on information collected from DU, CU-UP. For example, DU can inform CU-CP about the UE inactivity using UE INACTIVITY NOTIFICATION. We don’t see strong motivation to let DU requires the SCG (de)activation explicitly. |
| CATT |  | Need further study whether the DU can initial the deactivation |

## E1 interface related issues

In the last RAN3 #112 e-meeting, the following WA was made for enhancing E1 interface.

WA:E1 interface enhancement to support SCG (de)activation is needed to let CU-UP be aware of the SCG state.

Since majority companies propose to enhance E1 interface according to the contributions, moderator suggests to confirm the above WA as an agreement.

Question 10: Do companies agree to confirm the WA on enhancing E1 interface to support SCG (de)activation to let CU-UP be aware of the SCG state as an agreement?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | Since it is beneficial to let CU-UP be aware of the SCG state, we agree to confirm the WA as an agreement. |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |

Some companies believe that the principle for Xn interface cannot be reused for E1 interface according to the contributions and the company replies in [1]. Thus, the enhancements for E1 interface shall be discussed in details.

For the same reason as Xn interface, the moderator provides the similar question for E1 interface about the SCG (de)activation indicator design in the request messages and how to reject SCG (de)activation. Whether to add a SCG (de)activation indicator in the response message shall be discussed after reaching an agreement on how to reject the SCG (de)activation.

### 3.6.1 Bearer context setup procedure

Question 11: Do companies agree to add new IE with two codepoints in the Bearer Context Setup Request message to indicate the SCG is requested to activate or de-activate?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | CU-CP shall be able to initiate both SCG activation and deactivation requests since it controls SCG. |
| Lenovo, Motorola Mobility | Yes | Following Xn interface principle. |
| CATT | Yes |  |

Question 12: Companies are kindly asked which option below is preferred.

- Not allowed to reject SCG (de)activation

- Partial rejection shall be supported

- Full rejection shall be supported

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | CU-CP controls SCG and the CU-UP resources, thus there seems no need to allow CU-UP to reject SCG (de)activation request from CU-CP. CU-CP just needs to inform CU-CP about the SCG state. |
| Lenovo, Motorola Mobility | 2) | Following Xn interface principle, depending on Q3 and Q4, it could be partial rejection. Full rejection is by default supported in our understanding. |
| CATT | 2) |  |

### 3.6.2 gNB-CU-CP initiated bearer context modification procedure

Question 13: Do companies agree to add new IE with two codepoints in the Bearer Context Modification Request message to indicate the SCG is requested to activate or de-activate?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | CU-CP shall be able to initiate both SCG activation and deactivation requests since it controls SCG. |
| Lenovo, Motorola Mobility | Yes | Following Xn interface principle. |
| CATT | Yes |  |

Question 14: Companies are kindly asked which option below is preferred.

- Not allowed to reject SCG (de)activation

- Partial rejection shall be supported

- Full rejection shall be supported

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | CU-CP controls SCG and the CU-UP resources, thus there seems no need to allow CU-UP to reject SCG (de)activation request from CU-CP. CU-CP just needs to inform CU-CP about the SCG state. |
| Lenovo, Motorola Mobility | 2) if it’s MN initiated | As one example, if CU-CP requests SCG deactivation but there is DL data arrival at CU-UP, it seems straight forward for CU-UP to reject the SCG activation. In case of whether it’s partial rejection, following Xn interface if it’s MN initiated modification, then partial rejection can be used. It’s FFS how to distinguish MN initiated or SN initiated SCG (de)activation. Full rejection is by default supported in our understanding. |
| CATT | 2) |  |

## SCG activity detection

In the last RAN3 #112 e-meeting, one open issue was noted for SCG activity detection.

Open issue: Which node is exactly responsible for the SCG activity detection and if any enhancement to E1/F1/Xn interface is needed.

Companies have diverging views on this issue. [12] has analyzed this issue in detail and also proposes a possible solution to solve the inter-operability issue among multiple entities. In moderator’s view, it would be better to first clarify which node is exactly responsible for the SCG activity detection, and then discuss the possible enhancement.

Question 15: Companies are kindly asked which node is exactly responsible for the SCG activity detection.

| Company | Comment |
| --- | --- |
| ZTE | We agree with the analysis in [14] for this question. As long as the CU-CP makes the final decision of SCG (de)activation, the source of SCG activity information does not seem to be critical. |
| Lenovo, Motorola Mobility | In our understanding, it should be CU-CP makes the SCG (de)activation decision based on the information collected from DU or CU-UP. CU-UP and DU will of course detect any data traffic and inform CU-CP as in legacy, e.g., via UE INACTIVITY NOTIFICATION, or BEARER CONTEXT INACTIVITY NOTIFICATION. |
| CATT | Agree with Lenovo |

Question 16: Companies are kindly asked if any enhancement to E1/F1/Xn interface is needed .

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | No | No need to enhance E1/F1/Xn interface. |
| Lenovo, Motorola Mobility | No | We don’t foresee necessary enhancement to E1/F1/Xn interface for SCG (de)activation apart from what has been discussed. |
| CATT | No |  |

# Phase 2 discussion

# Conclusion, Recommendations [if needed]

If needed

# References

R3-212784 was R3-212644 SOD on SCG activation and deactivation_Phase 2_v4

R3-213215	TP for SCG BL CR to TS37.340 (ZTE)	other

R3-213216	TP for SCG BL CR to TS38.423 36.423 38.473 38.463 (ZTE)	other

R3-213282	(TP for SCG BL CR to TS36.423) Acceptance / Rejection of SCG Activation / Deactivation (NEC)	other

R3-213283	SCG Activation / deactivation discussion on E1 (NEC)	discussion

R3-213368	Aspects of SCG deactivation/activation (Qualcomm Incorporated)	discussion

R3-213381	(TP to SCG BL CR to 38.423, LTE_NR_DC_enh2-Core) Completion of the solution for the SCG activation state change (Nokia, Nokia Shanghai Bell)	other

R3-213382	(TP to SCG BL CR to 36.423, LTE_NR_DC_enh2-Core) Completion of the solution for the SCG activation state change (Nokia, Nokia Shanghai Bell)	other

R3-213563	(TP to 38.401 SCG BL CR) SCG activation and deactivation (Huawei)	other

R3-213564	(TP to 38.463 SCG BL CR) SCG activation and deactivation (Huawei)	other

R3-213661	Open Issues on Activation/Deactivation for One SCG and SCells (LG Electronics)	discussion

R3-213701	(TP to SCG BL CR TS38.473) Discussion on SCG activation and deactivation (Samsung)	discussion

R3-213716	Support of SCG Activation and Deactivation (Lenovo, Motorola Mobility)	CR0623r, TS 38.463 v16.6.0, Rel-17, Cat. B

R3-213717	Remaining issues on SCG activation and deactivation (Lenovo, Motorola Mobility)	discussion

R3-213868	(TP for SCG BL CR to TS 36.423) Feedback for SCG (de)activation (Ericsson)	other

R3-213869	(TP for SCG BL CR to TS 38.423) Feedback for SCG (de)activation (Ericsson)	other

R3-213940	Discussion on efficient Activation/Deactivation for SCG (CATT)	discussion

R3-213941	(TP for [LTE_NR_DC_enh2-Core] SCG BLCR for TS 38423) efficient Activation/Deactivation for SCG (CATT)	CR0660r, TS 38.423 v16.6.0, Rel-17, Cat. B

R3-212993	SCG BL CR to TS 38.473(Samsung) CR0777r0, TS 38.473 v16.5.0, Rel-17, Cat. B