3GPP TSG-RAN WG3 #113-e							R3-214298

16 August – 26 August 2021

Online

Agenda Item:	14.2

Source:	ZTE (moderator)

Title:	Summary of Offline Discussion on MRDC2 - SCG (de)activation

Document for:	Approval

# Introduction

CB: # MRDC2_SCGActivation_Deactivation

- Further discussion on the open issues left in R3-212784 and check RAN2 progress

- Partial rejection or full rejection? New cause value?

- For SCG (de)activation during SN addition, if SN can reject the SCG (de)activation when accepting the SN addition?

- Which node is responsible for the SCG activity detection and if any enhancement to E1/F1/Xn interface is needed?

- Impact on F1 and E1 interfaces?

- Capture agreements as stage2/stage3 CRs and check details, split work, if needed

- List open issues for next meeting in the summary

(ZTE - moderator)

Summary of offline disc in R3-214181

It is proposed to divide the discussion into two phases:

-	Phase 1: Identify the issues to be discussed in RAN3

Deadline: Please provide your views by 11:00 am UTC Tuesday August 17th

-	Phase 2: Further discussion to capture agreements and open issues

Deadline for comments: 3:00 pm UTC Monday August 23rd

Deadline for first version TP: 3:00 pm UTC Tuesday August 24th

(We will start assigning and preparing for TPs after achieving more agreements in phase 2 discussion)

# For the Chairman’s Notes (Phase 2)

# Phase 2 discussion

## SCG (de)activation during SN addition and MN initiated SN modification

Moderator suggests to first confirm the scenarios which may need partial rejection to finally decide whether to support partial rejection for each case. Companies are also welcome to add any other possible scenarios.

### 3.1.1 SCG activation during MN initiated SN modification

Scenario 1: A package of configurations may be sent together with SCG activation request, but inside the package of configuration, there could be part of it not related to SCG activation, e.g. the MN wants SN to release some QoS flow, rejecting the whole package of configurations might lead to some ping-pong effect too.

Scenario 2: If the MN wants SN to support a new QoS flow and requests SCG activation, due to lack of SCG resources or due to power saving strategy, SN may reject the SCG activation and configure a SN terminated MCG bearer for the new QoS flow.

Scenario 3: If only MN terminated split bearers are configured with SCG deactivated, then MN initiates SCG activation, due to lack of SCG resources or due to power saving strategy, SN may reject the SCG activation which does not seem a disaster.

Scenario 4: For MN asking to activate, the deactivated SN may face resource loaded then can reject, but still keep the SCG deactivated.

Question 1: Do companies agree that partial rejection shall be supported in at least one of the above scenarios? If no, please list the reason.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Samsung | Yes |  |
| Nokia | Rather no | Perhaps scenario 2 could be considered, but only if the PDCP is also moved to the SN and the MN indicates enough resources to handle the whole traffic… |

### 3.1.2 SCG deactivation during MN initiated SN modification

Scenario 1: When the Modification is used to add or modify a bearer (so that PDCP is transferred to the SN). This corresponds to the Addition case. Then, the SN could accept the modification but with SCG activated (only when the MN indicates SCG may be deactivated).

Scenario 2: For MN asking to deactivate, the active SN may still have traffic to go for SN terminated bearer, then it can reject the deactivation request, and keep the SCG activated.

Question 2: Do companies agree that partial rejection shall be supported in at least one of the above scenarios? If no, please list the reason.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Samsung | Yes |  |
| Nokia | Yes |  |

### 3.1.3 SCG activation during SN addition

Scenario 1: The load of SN changes in real time, it can reject the SCG activation request temporarily due to overload, and request SCG activation when SCG resource is available again. If partial rejection is not supported, SN needs to reject the whole addition procedure due to temporary resource shortage, then MN needs to select another available SN which might provide worse signal quality compared with the old SN. Once the old SN has available resources, MN may initiate the SN change procedure to add the old SN, which introduces unnecessary SN change PingPong and signalling overhead.

Question 3: Do companies agree that partial rejection shall be supported in at least one of the above scenarios? If no, please list the reason.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Samsung | Yes |  |
| Nokia | No | In case of load issues, the SN shall reject the whole request, so that the MN may request it in another SN. It perhaps may be considered if the PDCP is transferred to the SN and the MN offers enough resources on the MCG to handle the whole call, but that’s a very conditional scenario… |

### 3.1.4 SCG deactivation during SN addition

Scenario 1: From MN point of view, it indicates to SN to deactivate SCG from its current understanding of the bearer situation, i.e., the SCG bearers may not require a lot of the resources from the time being and offloading now is from the future estimation or mobility point of view. However, from the SN point of view, if it has a lot of resources that can be used now, it may reject the SCG deactivation when accepting the SN addition procedure, which can be implementation of SN.

Question 4: Do companies agree that partial rejection shall be supported in at least one of the above scenarios? If no, please list the reason.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | SCG is controlled by SN and thus the flexibility shall be allowed. |
| Samsung | Yes | Another case is that when the SN receives the addition request, the SN decides to configure SRB3 for SCG. |
| Nokia | Yes |  |

Question 5: Please list if there are other possible scenarios that may need partial rejection for SCG (de)activation during SN addition/MN initiated SN modification procedure.

| Company | Comment |
| --- | --- |
| ZTE | The design of addition and modification shall be consistent to provide sufficient flexibility and meet the needs of possible scenario expansion. |
| Samsung | It is better to have a unified procedure. |
| Nokia | The signalling shall be designed so that only the scenarios that were accepted in RAN3 can be handled. Also, we will not have partial rejection on SN-initiated modification, so the only “unified solution” is the one without partial rejection in any procedure. If we are fine to have different solutions for MN- and SN-initiated procedures, the good “unification” is to agree that the SN may have SCG activated, if the MN indicates it may be deactivated, but not vice-versa. |

## Remaining proposed agreements of phase 1 discussion

To facilitate the progress, moderator provides the remaining proposed agreements which seem to be easy to converge based on the company replies of phase 1 discussion.

### 3.2.1 SN initiated SN modification procedure

1) Convert the following WA to Agreement:

WA: RAN3 does not enhance Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation.

- Partial rejection is not supported for SN initiated SCG (de)activation during SN modification procedure.

Question 6: If companies do not agree with the above agreements, please indicate which one cannot be agreed and list the reason or any possible compromise way. This question can be skipped if companies agree with the above agreements.

| Company | Comment |
| --- | --- |
| ZTE | We agree with the above agreements. Samsung has pointed out that SN RRC message can be modified in “SN Modification Required” triggered SN Modification procedure (step 2-3 of figure 10.3.1-2, TS37.340). However, we have another concern to use the above procedure to modify RRC message. The MN may send modification request to SN to try to modify the SN RRC messages if partial rejection is supported according to figure 10.3.1-2 in TS37.340. However, SN may reject the SCG (de)activation in the modification request acknowledge message, which may cause necessary Ping Pong and the UE behaviour is still not aligned with SCG state. Thus, we think partial rejection shall not be supported for SN initiated SCG (de)activation during SN modification procedure. |
| Samsung | We have concerns on changing WA to agreement since we are unclear the SCG activity detection procedure. If Activity Notification message is not enhanced, we are wondering if this message is used to indicate the SCG activity or not. If not, how does CU-CP differentiate the intention of sending Activity Notification, i.e., send the UE into Inactivity status, or (de)activate SCG. So, we prefer to keep such WA open until we have clear view on the SCG activity detection. |

### 3.2.2 New cause value

1) The use of the new Cause is not limited to particular scenarios, and it will be up to implementation.

2) Use a general cause value, e.g., Failure due to SCG (de)activation, to indicate that the request is rejected due to the rejection of SCG (de)activation.

Question 7: If companies do not agree with the above agreements, please indicate which one cannot be agreed and list the reason or any possible compromise way. This question can be skipped if companies agree with the above agreements.

| Company | Comment |
| --- | --- |
| Samsung | In our understanding, such general cause can be used for the partial rejection. However, this general cause cannot provide additional information. So, we failed to know the intention of the new cause value. If new cause value is needed, some specific causes should be given. |

## E1 and F1 related issues

According to company replies of phase 1 discussion, the following agreements of E1 and F1 interfaces can be achieved.

The codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface.

CU/CU-CP makes the final decision of SCG (de)activation.

Convert the following WA to Agreement:

WA:E1 interface enhancement to support SCG (de)activation is needed to let CU-UP be aware of the SCG state.

However, companies still have diverging views on gNB-DU initiated SCG (de)activation and some E1 interface related issues. Thus, moderator suggests to firstly reach some basic consensus, and then discuss the details of F1 and E1 related issues.

Question 8: All in all, it's the CU/CU-CP that makes the final decision on SCG activation or deactivation. Does CU-CP needs the assisting information collected from DU or CU-UP to make final decisions of SCG (de)activation? If yes, how to obtain the assisting information?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | CU-UP can use DL data notification procedure and Bearer context inactivity notification procedure to inform CU-CP about the DL data activity. It can also use bearer context modification required message with a new SCG status indicator IE to inform CU-CP. DU can use UE inactivity notification procedure to inform CU about the UL data activity. It can also use UE context modification required message with a new SCG status indicator IE to inform CU. |
| Samsung | Yes | We have no problem for the above three agreements. For assistant information, we think it should be discussed by differentiating SCG activation from SCG deactivation. For SCG activation: E1: DL Data Notification For SCG deactivation: F1: UE Inactivity Notification E1: Bearer Context Inactivity Notification However, for SCG deactivation, whether the existing information contained in those procedure can be considered as the assistant information needs further discussion since the legacy information is originally used to help CU-CP make decision on sending the UE to the RRC INACTIVE status. As a follow-up issue, the SCG deactivation decision should be made based on inputs of multiple entities. How to deal with the inter-operability should be discussed as well. |
| Nokia | Yes, it is already present | The SCG activation hall follow the data traffic – SCG can be deactivated when there is no data. Therefore, the existing activity notification from the CU-UP to the CU-CP is all the CU needs to control the SCG (and the Xn signalling, if SCG is in the other node). |

## Prepare TP to be agreed

[TBD]

(We will start assigning and preparing for TPs after achieving more agreements in phase 2 discussion)

# For the Chairman’s Notes (Phase 1)

Agreements:

MN initiated SN modification procedure

Convert the following WA to Agreement:

WA: For SCG (de)activation during MN initiated SN modification, SN can reject the SCG (de)activation when accepting SN modification request.

SN addition procedure

For SCG deactivation during SN addition, SN can reject the SCG deactivation when accepting SN addition request.

For SCG activation during SN addition, SN can reject the SCG activation when accepting SN addition request.

In the SN modification request acknowledge message, to indicate SCG (de)activated, two codepoints are supported (i.e. one for SCG activation, another for SCG deactivation).

(The detail code of this IE can be discussed in phase 2.)

SN initiated SN modification procedure

Convert the following WA to Agreement:

WA: RAN3 does not enhance Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation.

Partial rejection is not supported for SN initiated SCG (de)activation during SN modification procedure.

New cause value

The use of the new Cause is not limited to particular scenarios, and it will be up to implementation.

Use a general cause value, e.g., Failure due to SCG (de)activation, to indicate that the request is rejected due to the rejection of SCG (de)activation.

F1 interface related issues

The codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface.

E1 interface related issues

Convert the following WA to Agreement:

WA:E1 interface enhancement to support SCG (de)activation is needed to let CU-UP be aware of the SCG state.

SCG activity detection

CU-CP makes the final decision of SCG (de)activation.

(We shall firstly reach some basic consensus, and then discuss the details for F1 and E1 related issues. )

Open issues:

- Does CU-CP needs the assisting information collected from DU or CU-UP to make SCG (de)activation decisions?

- How can CU-CP get the assisting information? Reuse existing messages, introducing new indicators or introducing new mechanisms?

# Phase 1 discussion

Please note that the terms partial rejection and full rejection in the discussion part refer to the following meanings:

Partial rejection: SCG (de)activation request is rejected when accepting the whole procedure.

Full rejection: The whole procedure is rejected due to the rejection of SCG (de)activation request.

## MN initiated SN modification procedure

In the last RAN3 #112 e-meeting, the following WA was made for MN initiated SN modification procedure.

WA: For SCG (de)activation during MN initiated SN modification, SN can reject the SCG (de)activation when accepting SN modification request.

Note that in the RAN3 #111 e-meeting, it was agreed to add a new IE with two codepoints in the SN modification response message, which also indicates that partial rejection shall be supported.

Add a new IE, e.g., “SCG activation result” with two codepoints in the SN modification response message in order to indicate the SCG is activated or de-activated.

Since majority companies propose to support partial rejection according to the contributions, moderator suggests to confirm the above WA as an agreement, which is is also consistent with the agreement made in the RAN3 #111 e-meeting.

Question 1: Do companies agree to confirm the WA on supporting partial rejection for SCG (de)activation during MN initiated SN modification as an agreement?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | It’s not necessary to reject the whole modification procedure if the SCG (de)activation request is rejected by SN. Furthermore, confirming this WA will also keep align with the previous agreement for SN modification procedure. |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |
| LGE | Yes |  |
| Nokia | No | As discussed at RAN3 #112, a scenario for rejecting part of the modification is unclear. In this context, RAN3 shall enable partial rejection of other changes that can be signalled in the modification. So, it would have to be shown what special scenario requires that the sender must combine changes and then the receiver must accept/reject the procedure parcially. When reading others’ papers, we realise there may be only one such scenario: when the Modification is used to add or modify a bearer (so that PDCP is transferred to the SN). This corresponds to the Addition case. Then, the SN could accept the modification but with SCG activated (only when the MN indicates SCG may be deactivated). We can’t see any other scenarios. |
| E/// | Yes | Partial rejection is allowed as usual handling. As already mentioned in last meeting, SCG activation status may not be accepted by SN, though other configuration update is accepted. |
| NEC | Yes | The SN can send back the SN Modification Acknowledge with an indication to show the Request of activation or deactivation has been reject. The SCG status in SN will be kept. |
| Huawei | No or Neutral | The information contained in a single request is a package, some information are related to some other information. For example, during SN initiated SN modification, in case SCG activation is requested by the SN, besides the SCG activation indication in the SN Modification Required, the corresponding secondaryCellGroup information will probably be provided within the NR RRC Reconfiguration message, the MN should not reject SCG activation and accept the other modifications. In case of partial rejection, the MN may need to trigger SN modification procedure again to revise some of the parameters. |
| Samsung | Yes |  |
| Qualcomm | Yes |  |

Moderator summary: (8/10) companies agree to confirm this WA as an agreement, (1/10) company says no, and (1/10) company says no or neutral.

Proposal 1: Confirm the WA on supporting partial rejection for SCG (de)activation during MN initiated SN modification as an agreement.

## MN initiated SN addition procedure

### 5.2.1 Partial rejection or full rejection

In the last RAN3 #112 e-meeting, the following agreement was achieved for MN initiated SN addition procedure.

In the SN addition request message, to set SCG (de)activated, two codepoints are supported (i.e. one for SCG activation, another for SCG deactivation).

Whether to support partial or full rejection for SCG (de)activation during MN initiated SN addition was further discussed into two sub-scenarios in the last meeting [1]:

- Sub-scenario 1: SCG activation during SN addition

- Sub-scenario 2: SCG deactivation during SN addition

Since majority companies propose to support partial rejection for Sub-scenario 2 according to the contributions, and agree that there is no harm for SN to reject the SCG deactivation during SN addition according to the company replies in [1], moderator suggests to agree that SN can reject the SCG deactivation when accepting SN addition (i.e. partial rejection).

Question 2: Do companies agree that SN can reject the SCG deactivation when accepting SN addition (i.e. partial rejection)?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | In case of inter-MN handover without SN change, the SN knows the data status for SN terminated bearer during SN addition. Thus SN can reject SCG activation or deactivation while accepting SN addition in this case. |
| Lenovo, Motorola Mobility | Yes | It does not seem harmful. |
| CATT | Yes |  |
| LGE | Yes | From SN point of view, if it has a lot of resources that can be used during the addition, it may reject the SCG deactivation when accepting the SN Addition procedure, which depends on the implementation of SN. |
| Nokia | Yes | I understand, by “rejecting de-activation” we mean a case where the MN proposes SCG to be deactivated, but the SN decides to have it activated? If yes, then this option is beneficial. |
| E/// | Yes | In principle MN should be able to know if need to add an activated SCG but not a de-activated SCG. Anyway SN is in charge of its own resource, such flexibility should be allowed. |
| NEC | No | (What is the “MN Initiated” SN addition?) In any case, the SN Addition with SCG activation is by default supported from Rel-15. The SN reject the SN addition of SCG activation or deactivation is only for the reason that it is too loaded that cannot reserve resource even for the SCG deactivation. If the SN have enough resource, then it simply just accept and send back addition acknowledge message. |
| Huawei | No or Neutral | Similar comment to Q1. No clear reason for SN to reject SCG deactivation during SN addition. For the inter-MN HO without SN change, the target MN is aware of the SCG status, therefore the target MN should not indicate SCG deactivation if it should not be deactivated. |
| Samsung | Yes | A unified scheme would be preferred |
| Qualcomm | Yes | SCG can decide based on incoming traffic and resource status. |

Moderator summary: (8/10) companies agree to support partial rejection for SCG deactivation during SN addition, (1/10) company says no, and (1/10) company says no or neutral.

Form moderator’s point of view, although the scenario for SN to reject SCG deactivation during SN addition is not quite clear, the SCG is controlled by SN and thus the flexibility shall be allowed.

Proposal 2:  For SCG deactivation during SN addition, SN can reject the SCG deactivation when accepting SN addition request.

According to the contributions and company replies in [1], half companies think that partial rejection shall be supported for rejecting SCG activation during SN addition, and the other half companies think full rejection shall be supported. As stated in [2][14], if RAN3 agrees to support partial rejection for SCG deactivation during SN addition, it would be better to have a unified solution for the SCG (de)activation during SN addition, i.e., RAN3 agrees to support partial rejection for SCG activation during SN addition. After all, MN can trigger SN release or SN change.

Moderator’s view: If receiving the SN addition request acknowledge message including “de-activate”, it is the MN to make the further decision (other than the SN refuses the SN addition procedure"), i.e., the MN can further initiates SN release procedure to this SN and initiates another SN addition procedure with another SN.

Question 3: Do companies agree that SN can reject the SCG activation when accepting SN addition (i.e. partial rejection)?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | In case of inter-MN handover without SN change, the SN knows the data status for SN terminated bearer during SN addition. Thus SN can reject SCG activation or deactivation while accepting SN addition in this case. It seems too complicated if full rejection is supported for SCG activation while partial rejection is supported for SCG deactivation during SN addition, and a unified solution may be more straightforward and simple. |
| Lenovo, Motorola Mobility | Yes | Although it seems rejecting SCG activation while accepting the SN addition will make the SN addition wasted, smart NW implementation can use full rejection whenever SN wants. To have a unified solution considering Question 3 and not making the design too fragmented, we are fine to support partial rejection for SCG activation during SN addition. |
| CATT | Yes | Support using the unified solution |
| LGE | No | Partially rejection is not good in this case since the intention of MN’s offloading to this SN cannot be really realized. MN may have other SN candidate to offload the bearers successfully, i.e., partially rejection in this case may let MN lose other opportunity. |
| Nokia | No | If the MN indicates SCG is needed, accepting the request without SCG is pointless – the MN will have to release it immediately. Therefore, if the MN needs SCG, the SN hall provide it (as per legacy), or reject DC addition right away, to save unnecessary signalling. Also, please note, before the addition, the SN has no solid information about the traffic, so it can’t make a decision of its own concerning the need of SCG. |
| E/// | Neutral | As said above, MN understands better about the incoming data to be offloaded to SN. So when MN triggers the addition of activated SCG, there is no strong point for the SN to reject. However, to align with modification procedure from IE design point of view, partial rejection might be supported as well. |
| NEC | No | In the SN addition procedure, the SN can either accept or reject the procedure, no partial rejection is allowed. |
| Huawei | No or Neutral | Similar comment to Q1. |
| Samsung | Yes | We prefer to a unified solution. |
| Qualcomm | No | If MN wants to offline traffic to SN and SN partially accepts, what shall MN do, release the SN and select another SN? To make the feature simple and efficient, we’d better avoid this kind of partial rejection. |

Moderator summary: (4/10) companies agree to support partial rejection for SCG activation during SN addition, (4/10) company says no, (1/10) company says no or neutral, (1/10) company says neutral.

Form moderator’s point of view, a unified solution could be better to allow enough flexibility to adapt to multiple scenarios. Furthermore, the traffic load of SN changes in real time, it can reject the SCG activation request temporarily, and request SCG activation when SCG resource is available. If partial rejection is not supported, then MN needs to select another available SN which might be worse than the the old SN. Once the old SN has available resources, MN may initiate the SN change procedure to add the old SN, which may cause unnecessary handover. Thus, moderator suggests to support partial rejection for SCG activation during SN addition.

Proposal 3:  For SCG activation during SN addition, SN can reject the SCG activation when accepting SN addition request.

### 5.2.2 SCG (de)activation indicator design

In moderator’s view, as long as RAN3 agrees to support partial rejection for Sub-scenario 1 of MN initiated SN addition, a new IE with two codepoints needs to be added in SN modification request acknowledge message to indicate the SCG is activated or deactivated.

Question 4: Do companies agree to add a new IE with two codepoints in SN modification request acknowledge message to indicate the SCG is activated or deactivated?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | If partial rejection is supported, a new IE with two codepoints is required. |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |
| LGE | Yes |  |
| Nokia | No | As discussed above, it is unclear at what scenario it would be needed. If it concerns transfer of PDCP, such IE may be added, but its use has to be carefully defined so that it is not used in undefined scenarios. |
| E/// | Yes | Either add a new IE with (accept, reject) or reuse the existing SCG Activation Status IE will do. |
| NEC | No | No need for partial rejection in SN Addition procedure, therefore nothing indicator is needed. |
| Huawei | Yes | If partial rejection is supported, the SN may indicate SCG is activated or deactived, therefore two code points are needed. If partial rejection is not supported, in case the SN accept the request, the SN needs to reply the indicator with same value as received from the MN, otherwise the MN may not able to know whether the SN is a legacy SN or a new SN which supports this feature. |
| Samsung | Yes |  |
| Qualcomm | Yes |  |

Moderator summary: (8/10) companies agree to use a two-codepoint IE in the SN modification request acknowledge message to indicate the SCG is activated or deactivated, (2/10) company says no. The detail code of this IE can be discussed in phase 2.

Proposal 4: In the SN modification request acknowledge message, to indicate SCG (de)activated, two codepoints are supported (i.e. one for SCG activation, another for SCG deactivation).

## SN initiated SN modification procedure

### 5.3.1 Activity Notification

In the last RAN3 #112 e-meeting, the following WA and agreement were achieved for SN initiated SCG (de)activation.

WA: RAN3 does not enhance Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation. RAN3 supports SCG (de)activation during SN initiated SN modification.

Considering that there seems no objection to confirm the above WA into an agreement in the contributions, the moderator suggests to confirm it as an agreement.

Question 5: Do companies agree to confirm the WA on not enhancing Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation as an agreement?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |
| LGE | Yes |  |
| Nokia | Yes | Does not seem needed at this moment. Can be reconsidered, if a new scenario is proposed and accepted. |
| E/// | Yes | This is already clear in the group, unless further enhancement is required. |
| NEC | Yes | Probably no need to enhance the Activity Notification, however by implementation the MN can still take this into account when try to initiate SCG activation or SCG deactivation. |
| Huawei | Yes |  |
| Samsung | Depends | Till now, how to use Activity Notification procedure for SCG (de)activation is unclear to us. One possible understanding is that the SN sends the Activity Notification to MN, and then MN makes decision on SCG (de)activation; another possible understanding is that the Activity Notification procedure is not involved in the whole procedure of SCG (de)activation. Thus, to determine whether enhancement to Activity Notification procedure is needed or not, we need confirm the understanding on the question: Can Activity Notification procedure be used for SCG (de)activation decision-make? |
| Qualcomm | Yes |  |

Moderator summary: (9/10) companies agree to confirm the WA on not enhancing Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation as an agreement, (1/10) company says it depends on whether the Activity Notification procedure can be used for SCG (de)activation decision-making.

Proposal 5: Confirm the WA on not enhancing Activity Notification for the sake of supporting SCG (de)activation for the SN initiated SCG (de)activation as an agreement.

### 5.3.2 Partial rejection or full rejection

Another remaining issue for SN initiated SCG (de)activation during SN modification procedure is whether to support partial or full rejection. Slight majority companies believe that full rejection shall be supported, and a critical issue was acknowledged to support partial rejection for SN initiated SN modification procedure in the last meeting as stated in [1][2][14]. There is a principle that MN does not interpret SN RRC message from SN, but include it into MN RRC message as a container to UE directly. If partial rejection is supported for SN initiated SCG (de)activation, SN RRC message shall be modified otherwise UE behavior is not aligned with SCG state. Therefore, only full rejection should be allowed for SN initiated SCG (de)activation in order to keep the above principle in Rel-15.

Question 6: Do companies agree not to support partial rejection for SN initiated SCG (de)activation during SN modification procedure? If no, how to solve the above mentioned issue?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | The SN initiated modification case is different from the MN initiated modification case, the principle is still kept if we support partial rejection in MN initiated modification. We shall not just simply reuse the rejection principle of MN initiated modification for SN initiated modification. |
| Lenovo, Motorola Mobility | Yes | Full rejection is always supported if MN wants to reject the whole SN modification required procedure. So we suppose the question is asking not to support partial rejection. As explained by moderator, when the RRC container is sent together with the SCG (de)activation indicator in the same Xn message, we should avoid sending RRC container to UE if rejecting the SCG (de)activation. If RAN3 is not sure about whether the SCG (de)activation indicator in Xn message can be sent without SN RRC container, RAN3 is suggested to send a LS to RAN2. |
| CATT | Yes | Agree with ZTE comments as the reason. |
| LGE | Yes |  |
| Nokia | Yes | In addition to the above arguments (which are indeed relevant!), we may consider the case where the MN hosts PDCP (thus has better information about resource needs). However, we believe that for existing bearers, the SN will have good enough knowledge to be allowed to control SCG, too. |
| E/// | Open | We won’t say such way of handling RRC container is a critical issue, but a concern to be solved, as Lenovo said, LS to RAN2 for example. |
| NEC | Yes | Full rejection is by default supported from Rel-15. Considering especially for EN-DC case that the LTE side MeNB does not encode the NR RRC message, it would be reasonable not to support partial rejection in SN Initiated SCG activation or SCG deactivation. |
| Huawei | Yes | We support to use full rejection for SN addition, MN initiated SN modification and SN initiated SN modification for unified solution for the SCG (de)activation. |
| Samsung | Yes |  |
| Qualcomm | No | SN RRC message can be modified in “SN Modification Required” triggered SN Modification procedure (step 2-3 of figure 10.3.1-2, TS37.340). For MN terminated bearer, MN knows the need of offloading traffic to SN. So, we should allow MN to reject the deactivation/activation request of SN. |

Moderator summary: (8/10) companies agree not to support partial rejection for SN initiated SCG (de)activation during SN modification procedure, (1/10) company says no, (1/10) company says open.

Form moderator’s point of view, the MN may send modification request to SN to try to modify the SN RRC messages if partial rejection is supported according to figure 10.3.1-2 in TS37.340. However, SN may reject the SCG (de)activation in the modification request acknowledge message, which may cause necessary Ping Pong and the UE behaviour is still not aligned with SCG state. Thus, moderator suggests not to support partial rejection for SN initiated SCG (de)activation during SN modification procedure.

Proposal 6: Partial rejection is not supported for SN initiated SCG (de)activation during SN modification procedure.

## New cause value

In the last RAN3 #112 e-meeting, the following agreement was achieved to introducing a new cause value. However, Some issues regarding the new cause value need to be further discussed.

A new cause value will be introduced to indicate the reason to reject SCG (de)activation. FFS what exactly value.

The first issue is when to use the new cause value. [2][9] believe that the new cause value shall only be used in the case that the whole procedure is rejected due to SCG (de)activation request failure, i.e. full rejection. However, [6][11][15] believe that if the request of SCG (de)activation is rejected during partial rejection, the rejection cause shall be provided to indicate the reason of rejecting.

Question 7: Companies are kindly asked which option below is preferred for the new cause value?

- It shall be used in the case that the whole procedure is rejected due to SCG (de)activation request failure

- It shall be used to indicate the rejecting reason of partial rejection for SCG (de)activation

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | If partial rejection is supported, the rejection of SCG (de)activation can be indicated via the response message. There is no need to use the new cause value for partial rejection. The new cause value shall only be used when the whole procedure is rejected due to the rejection of SCG (de)activation. |
| Lenovo, Motorola Mobility | 1) 2) | No strong view, it seems helpful to indicate the exact reason of SCG (de)activation during full or partial rejection. |
| CATT | 1) |  |
| LGE | 1) 2) | Better to define a new cause value to cover the rejection is because of SCG (de)activation, no matter it is full or partial rejection |
| Nokia | 1 & 2 | Normally, use of Cause values is not restricted to particular scenarios (it is rather bad habbit to introduce such limits, because usage of the Causes is not specified anyway). So we are fine to have the new Cause, but we think it shall be defined generally and then it will be up to implementation to use it (as it is always with Causes). |
| E/// | 1) 2) | For full rejection, add a generic reason. For partial rejection, the network node needs to know what it happens for in order to be clear about next step. |
| NEC | 1) | A cause value for the whole rejection. (Presuming the indicator for showing “activation” or “deactivation” can be used for partial rejection, the cause value is not used or partial rejection. ) |
| Huawei | 1) | The cause value is only used for full rejection cases to indicate the receiving node reject the whole request. |
| Samsung | 2) | As agreed, this cause value is used to indicate the reason to reject SCG (de)activation, So, as long as the procedure includes the rejection of SCG (de)activation, it should include such new cause value, regardless of partial/full rejection. |
| Qualcomm | 1), 2) | Better to support both for flexibility. |

Moderator summary: (6/10) companies agree to use the new cause value as long as the SCG (de)activation request is rejected, i.e. for both partial rejection and full rejection. (4/10) companies believe that the new cause can only be used for full rejection.

From moderator’s point of view, the use of the new Cause is not limited to particular scenarios, and it will be up to implementation.

Proposal 7: The use of the new Cause is not limited to particular scenarios, and it will be up to implementation.

The next issue is the cause value design of the new cause value. According to the contributions, two options are provided.

-  Option 1: General cause value to indicate that the request is rejected due to the rejection of SCG (de)activation

-  Option 2: Specific reason to indicate the detailed reason for the rejection of SCG (de)activation

Question 8: Companies are kindly asked which option below is preferred.

- General cause value

- Specific cause value

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | SCG (de)activation is a simple function and it’s not necessary to include the specific rejection reason. This may cause unnecessary signalling and slow down the whole procedure. |
| Lenovo, Motorola Mobility | 2) | If the cause value is only “SCG (de)activation failure”, then it seems cannot be used for any other purpose. We consider it better to introduce cause value that can be used in other scenarios too, to be more future proof. |
| CATT | 1) | We prefer to use the option 1. If the detail cause value is introduced, many kinds value should be listed. |
| LGE | 2) | Better to give clear reason on the rejection |
| Nokia | 1 | There may be many implementation-specific reasons. |
| E/// | 1) 2) | Same as above. |
| NEC | 2) | The receiver needs to know the specific reason, otherwise it cannot know why the procedure is rejected. |
| Huawei | 1) | Agree with ZTE |
| Samsung | 2) | A general cause value does not help the receiver. |
| Qualcomm | 2) |  |

Moderator summary: (4/10) companies support to use a general cause value. (5/10) companies support to use specific cause values. (1/10) company support to use a general cause value for full rejection, and use specific cause values for partial rejection.

Form moderator’s point of view, there may be too many specific reasons to include all the scenarios. Thus the moderator suggests to use a general cause value.

Proposal 8:Use a general cause value, e.g., Failure due to SCG (de)activation,  to indicate that the request is rejected due to the rejection of SCG (de)activation.

## F1 interface related issues

In the last RAN3 #112 e-meeting, the following agreement was achieved for F1 interface.

F1 interface enhancement to support SCG (de)activation reuses the principle in Xn interface regarding: Codepoint design for SCG (de)activation for UE context setup Whether/how DU can reject the SCG (de)activation during UE context setup procedure Whether/how DU can reject the SCG (de)activation during UE context modification procedure

All companies agree to reuse the principle in Xn/X2 interface for F1 interface according to the contributions. Thus, moderator will propose mirror agreements for F1 interface after achieving agreements for Xn interface.

It is noted that the codepoint design for SCG (de)activation during UE context modification is not mentioned in the above agreement. Therefore, moderator suggests to add the agreement that the codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface.

Question 9: Do companies agree to add the agreement that the codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |
| LGE | Yes |  |
| Nokia | Yes | However, please note, in our understanding that means that partial rejection of a modification is not supported. |
| E/// | Yes |  |
| NEC | Yes |  |
| Huawei | Yes |  |
| Samsung | Yes |  |
| Qualcomm | Yes |  |

Moderator summary: All companies agree to add the agreement that the codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface.

Proposal 9: Add the agreement that the codepoint design for SCG (de)activation during UE context modification also reuses the principle in Xn interface.

It is also noted that gNB-DU initiated UE context modification required procedure is also enhanced for SCG (de)activation in the agreed SCG BL CR to TS 38.473[19]. Therefore, moderator suggests to add the agreement that whether/how CU can reject the SCG (de)activation during UE context modification required procedure also reuses the principle in Xn interface.

Question 10: Do companies agree to add the agreement that whether/how CU can reject the SCG (de)activation during UE context modification required procedure also reuses the principle in Xn interface?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Lenovo, Motorola Mobility | No | In our understanding, it’s CU-CP that decides/triggers SCG (de)activation based on information collected from DU, CU-UP. For example, DU can inform CU-CP about the UE inactivity using UE INACTIVITY NOTIFICATION. We don’t see strong motivation to let DU requires the SCG (de)activation explicitly. |
| CATT |  | Need further study whether the DU can initial the deactivation |
| LGE | No | Agree with Lenovo |
| Nokia | ? | This is unclear – which “principle in Xn”? The one related to MN-initiated modification, or the one for SN-initiated modification? In our view, it does not seem needed that the SN rejects only SCG state, while accepting the rest of the modification. If SCG state can’t be changed, the whole DU-initiated modification shall be rejected. |
| E/// |  | The changes in BL CR is only considered as placeholder. Prefer to wait for discussion over Xn to be stable first. |
| NEC | Yes |  |
| Huawei | Yes |  |
| Samsung |  | This depends on how SCG (de)activation decision is made: If the decision is completely made by CU-CP, DU only needs provide the SCG activity information to the CU-CP. If the decision can be made by DU, DU can directly trigger the SCG (de)activation request since SN-DU has the well knowledge on the SCG activity. |
| Qualcomm | Yes |  |

Moderator summary: Companies have diverging views on this issue, the moderator suggests to postpone the discussion.

## E1 interface related issues

In the last RAN3 #112 e-meeting, the following WA was made for enhancing E1 interface.

WA:E1 interface enhancement to support SCG (de)activation is needed to let CU-UP be aware of the SCG state.

Since majority companies propose to enhance E1 interface according to the contributions, moderator suggests to confirm the above WA as an agreement.

Question 11: Do companies agree to confirm the WA on enhancing E1 interface to support SCG (de)activation to let CU-UP be aware of the SCG state as an agreement?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | Since it is beneficial to let CU-UP be aware of the SCG state, we agree to confirm the WA as an agreement. |
| Lenovo, Motorola Mobility | Yes |  |
| CATT | Yes |  |
| LGE | Yes |  |
| Nokia | No | As explained in our paper, we do not understand why this would be needed? SCG deactivation shall follow the data activity, so if there is some data for the bearer, the SCG shall be activated. The UP can inform about it using the Activity Notification. Then, we also have the flow control which will prevent data flow from the UP to the DU for the short while when the SCG is not yet activated (probably the control of the buffer sizes is enough, but if needed, there is also the “outage” status available). |
| E/// | Neutral | It is natural to follow principles from XnAP, however we are open to discuss if any other mechanism would help. |
| NEC | Yes |  |
| Huawei | Yes |  |
| Samsung | Yes |  |
| Qualcomm | Yes |  |

Moderator summary: (8/10) companies agree to confirm this WA as an agreement, (1/10) company says no, and (1/10) company says neutral.

Proposal 10: Confirm the WA on enhancing E1 interface to support SCG (de)activation to let CU-UP be aware of the SCG state as an agreement.

Some companies believe that the principle for Xn interface cannot be reused for E1 interface according to the contributions and the company replies in [1]. Thus, the enhancements for E1 interface shall be discussed in details.

For the same reason as Xn interface, the moderator provides the similar question for E1 interface about the SCG (de)activation indicator design in the request messages and how to reject SCG (de)activation. Whether to add a SCG (de)activation indicator in the response message shall be discussed after reaching an agreement on how to reject the SCG (de)activation.

### 5.6.1 Bearer context setup procedure

Question 12: Do companies agree to add new IE with two codepoints in the Bearer Context Setup Request message to indicate the SCG is requested to activate or de-activate?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | CU-CP shall be able to initiate both SCG activation and deactivation requests since it controls SCG. |
| Lenovo, Motorola Mobility | Yes | Following Xn interface principle. |
| CATT | Yes |  |
| LGE | Yes |  |
| Nokia | No | E1 changes are not needed at this moment, the SCG status follows data flow, not vice versa. |
| NEC |  | For the Bearer Context Setup procedure, CP only need to indicate “deactivation” since the “activation” is always by default needed for the CU-UP to work i.e. to receive data whenever after bearer context and tunnels are established. The “deactivation” indication from the CU-CP is for the CU-UP to inform the CU-CP when any data is received during inactivated status. |
| Huawei | Yes |  |
| Samsung |  | CU-UP is in the position of sending/receiving packets via SCG. If CU-UP knows the SCG status, it can determine whether to use SCG or not for data transmission. However, CU-UP does not control SCG resource. So, we are not clear the intention of using bearer context setup/modification procedure to perform SCG (de)activation. If we introduce such procedure, it means that to (de)activate the SCG, the CU-CP should send request to each CU-UP and DU, and derive the response from each entity. We are not sure if those procedures can really satisfy our intention for fast SCG (de)activation. So, at this moment, we prefer to not introduce SCG (de)activation request/response over bearer context setup/modification procedure. |
| Qualcomm | Yes |  |

Moderator summary: Majority companies agree to add a new IE with two codepoints in the Bearer Context Setup Request message to indicate the SCG is requested to activate or de-activate.

Question 13: Companies are kindly asked which option below is preferred.

- Not allowed to reject SCG (de)activation

- Partial rejection shall be supported

- Full rejection shall be supported

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | CU-CP controls SCG and the CU-UP resources, thus there seems no need to allow CU-UP to reject SCG (de)activation request from CU-CP. CU-CP just needs to inform CU-CP about the SCG state. |
| Lenovo, Motorola Mobility | 2) | Following Xn interface principle, depending on Q3 and Q4, it could be partial rejection. Full rejection is by default supported in our understanding. |
| CATT | 2) |  |
| LGE | 1) |  |
| NEC | 3) | Full rejection is by default supported from Rel-15. We think no need for partial rejection as for the CU-UP, the reason for not accepting “deactivation” request is only for the case when the function is not supported. If no resource is available, then same as today, just reject the whole procedure. |
| Huawei | 3) | Full rejection of deactivation shall be supported. On the other hand, the CU-UP shall not be able to reject SCG activation request, the CU-UP is just be informed about SCG activation. |
| Samsung |  | See our comment to Question 12. |

Moderator summary: Companies have diverging views on this issue, the moderator suggests to postpone the discussion.

### 5.6.2 gNB-CU-CP initiated bearer context modification procedure

Question 13: Do companies agree to add new IE with two codepoints in the Bearer Context Modification Request message to indicate the SCG is requested to activate or de-activate?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | CU-CP shall be able to initiate both SCG activation and deactivation requests since it controls SCG. |
| Lenovo, Motorola Mobility | Yes | Following Xn interface principle. |
| CATT | Yes |  |
| LGE | Yes |  |
| NEC | Yes | CU-CP to tell CU-UP if the “deactivated” is changed to “activated” or the “deactivate” is requested. |
| Huawei | 3) | Full rejection of deactivation shall be supported. On the other hand, the CU-UP shall not be able to reject SCG activation request, the CU-UP is just be informed about SCG activation. |
| Samsung |  | See our comment to Question 12. |

Moderator summary: Majority companies agree to add a new IE with two codepoints in the Bearer Context Modification Request message to indicate the SCG is requested to activate or de-activate.

Question 15: Companies are kindly asked which option below is preferred.

- Not allowed to reject SCG (de)activation

- Partial rejection shall be supported

- Full rejection shall be supported

| Company | Option | Comment |
| --- | --- | --- |
| ZTE | 1) | CU-CP controls SCG and the CU-UP resources, thus there seems no need to allow CU-UP to reject SCG (de)activation request from CU-CP. CU-CP just needs to inform CU-UP about the SCG state. |
| Lenovo, Motorola Mobility | 2) if it’s MN initiated | As one example, if CU-CP requests SCG deactivation but there is DL data arrival at CU-UP, it seems straight forward for CU-UP to reject the SCG activation. In case of whether it’s partial rejection, following Xn interface if it’s MN initiated modification, then partial rejection can be used. It’s FFS how to distinguish MN initiated or SN initiated SCG (de)activation. Full rejection is by default supported in our understanding. |
| CATT | 2) |  |
| LGE | 1) |  |
| NEC | 3) | Full rejection is by default supported from Rel-15. We think no need for partial rejection as for the CU-UP, the reason for not accepting “deactivation” request is only for the case when the function is not supported. |
| Huawei | 3) | Full rejection of deactivation shall be supported On the other hand, the CU-UP shall not be able to reject SCG activation request, the CU-UP is just be informed about SCG activation. |
| Samsung |  | See our comment to Question 12. |
| Qualcomm | 3) |  |

Moderator summary: Companies have diverging views on this issue, the moderator suggests to postpone the discussion.

## SCG activity detection

In the last RAN3 #112 e-meeting, one open issue was noted for SCG activity detection.

Open issue: Which node is exactly responsible for the SCG activity detection and if any enhancement to E1/F1/Xn interface is needed.

Companies have diverging views on this issue. [12] has analyzed this issue in detail and also proposes a possible solution to solve the inter-operability issue among multiple entities. In moderator’s view, it would be better to first clarify which node is exactly responsible for the SCG activity detection, and then discuss the possible enhancement.

Question 16: Companies are kindly asked which node is exactly responsible for the SCG activity detection.

| Company | Comment |
| --- | --- |
| ZTE | We agree with the analysis in [14] for this question. As long as the CU-CP makes the final decision of SCG (de)activation, the source of SCG activity information does not seem to be critical. |
| Lenovo, Motorola Mobility | In our understanding, it should be CU-CP makes the SCG (de)activation decision based on the information collected from DU or CU-UP. CU-UP and DU will of course detect any data traffic and inform CU-CP as in legacy, e.g., via UE INACTIVITY NOTIFICATION, or BEARER CONTEXT INACTIVITY NOTIFICATION. |
| CATT | Agree with Lenovo |
| LGE | CU-CP is responsible for the SCG activity detection and decision |
| Nokia | The SCG status shall follow the data needs – if there is data to transfer, SCG shall be activated. However, bearers are controlled in the CU-CP. So, the split of responsibility is that the CU-UP indicates if there is data activity for given bearer and the CU-CP (hosting PDCP) decides if SCG is needed for this bearer and requests activation/deactivation as needed. Additionally, the SN’s CP and the DU hosting SCG may have a say (e.g. SCG can’t be deactivated due to hardware reasons), so it must be allowed to reject a modification that can’t be executed. |
| E/// | This question is a bit confusing. Thought it is not only for E1, but also Xn and F1? SCG activity is usually detected by the incoming data. What’s the difference between legacy? |
| NEC | For CP-UP split, during the deactivated state, when the CU-UP receive DL data, it needs to inform the CU-CP by using the current DL Data Notification procedure. Regardless of CP-UP split or not, during the deactivated state, when any UL is received, the gNB-DU trigger any action to the gNB-CU. Therefore it should be the CU-CP to make the decision. |
| Huawei | CU is responsible for SCG activation detection. For DL data arrival, CU-UP is aware of that. For UL data arrival, it is FFS in RAN2 how to indicate to the network. |
| Samsung | CU-CP is in the position of making decision on SCG (de)activation. To help decision make, CU-CP should collect information from other entities. The collected information can be either SCG activity detection results or the SCG (de)activation request. Thus, the SCG activity detection should be distributed among the entities, e.g., MN-CU-UP, SN-CU-UP, SN-DU. We can agree that: CU-CP makes the decision of SCG (de)activation, and then trigger SCG (de)activation request procedure MN-CU-UP/SN-CU-UP/DU performs the SCG activity detection To activate SCG, any entity detecting data for SCG can trigger the SCG activation. However, to deactivate SCG, all entities serving the traffic over SCG should detect the inactivity of SCG. We think this issue is not clearly discussed. If each entity has its own criteria of determining the SCG is inactivity, this may cause an inter-operability issue. Thus, based on the above two points we can agree, we would like to derive the clarification on how to solve the inter-operability issue when CU-UP(s)/DU detect that the SCG is in inactivity status. |
| Qualcomm | CU-UP detects the activity, i.e. incoming data. CU-CP makes the activation/deactivation decision. |

Moderator summary: Majority companies agree that CU-CP makes the final decision of SCG (de)activation. However, companies have diverging views on gNB-DU initiated SCG (de)activation  and E1 interface related issues.

From moderator’s point view, we shall firstly reach some basic consensus, and then discuss the details. Since Majority companies agree that CU-CP makes the final decision of SCG (de)activation, moderator suggests agree on the following proposal.

Proposal 11: CU-CP makes the final decision of SCG (de)activation.

However, there are still some related issues that need further discussion. Thus moderator suggests to further discuss the following issues.

- Does CU-CP needs the assisting information collected from DU or CU-UP to make SCG (de)activation decisions?

- How can CU-CP get the assisting information? Reuse existing messages, introducing new indicators or introducing new mechanisms?

Question 17: Companies are kindly asked if any enhancement to E1/F1/Xn interface is needed .

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | No | No need to enhance E1/F1/Xn interface. |
| Lenovo, Motorola Mobility | No | We don’t foresee necessary enhancement to E1/F1/Xn interface for SCG (de)activation apart from what has been discussed. |
| CATT | No |  |
| LGE | No |  |
| Nokia | ? | Well, some enhancements may be needed on Xn for the bearer addition scenario discussed above, or for the rejection (the new cause). But nothing extra seems needed now. |
| E/// | No |  |
| NEC |  | Not sure about the question. But apart what have been discussed above, not sure what to enhance, |
| Huawei | No | Same view as Lenovo. |
| Samsung |  | We can decide the potential impact after our concern on inter-operability issue is resolved. |
| Qualcomm | No |  |

Moderator summary: Majority companies agree not to enhance E1/F1/Xn interface SCG activity detection.

# Conclusion, Recommendations [if needed]

If needed

# References

R3-212784 was R3-212644 SOD on SCG activation and deactivation_Phase 2_v4

R3-213215	TP for SCG BL CR to TS37.340 (ZTE)	other

R3-213216	TP for SCG BL CR to TS38.423 36.423 38.473 38.463 (ZTE)	other

R3-213282	(TP for SCG BL CR to TS36.423) Acceptance / Rejection of SCG Activation / Deactivation (NEC)	other

R3-213283	SCG Activation / deactivation discussion on E1 (NEC)	discussion

R3-213368	Aspects of SCG deactivation/activation (Qualcomm Incorporated)	discussion

R3-213381	(TP to SCG BL CR to 38.423, LTE_NR_DC_enh2-Core) Completion of the solution for the SCG activation state change (Nokia, Nokia Shanghai Bell)	other

R3-213382	(TP to SCG BL CR to 36.423, LTE_NR_DC_enh2-Core) Completion of the solution for the SCG activation state change (Nokia, Nokia Shanghai Bell)	other

R3-213563	(TP to 38.401 SCG BL CR) SCG activation and deactivation (Huawei)	other

R3-213564	(TP to 38.463 SCG BL CR) SCG activation and deactivation (Huawei)	other

R3-213661	Open Issues on Activation/Deactivation for One SCG and SCells (LG Electronics)	discussion

R3-213701	(TP to SCG BL CR TS38.473) Discussion on SCG activation and deactivation (Samsung)	discussion

R3-213716	Support of SCG Activation and Deactivation (Lenovo, Motorola Mobility)	CR0623r, TS 38.463 v16.6.0, Rel-17, Cat. B

R3-213717	Remaining issues on SCG activation and deactivation (Lenovo, Motorola Mobility)	discussion

R3-213868	(TP for SCG BL CR to TS 36.423) Feedback for SCG (de)activation (Ericsson)	other

R3-213869	(TP for SCG BL CR to TS 38.423) Feedback for SCG (de)activation (Ericsson)	other

R3-213940	Discussion on efficient Activation/Deactivation for SCG (CATT)	discussion

R3-213941	(TP for [LTE_NR_DC_enh2-Core] SCG BLCR for TS 38423) efficient Activation/Deactivation for SCG (CATT)	CR0660r, TS 38.423 v16.6.0, Rel-17, Cat. B

R3-212993	SCG BL CR to TS 38.473(Samsung) CR0777r0, TS 38.473 v16.5.0, Rel-17, Cat. B

# Comments

I understand, it is meant that the MN requests SCG to be activated, right? My comment is based on this assumption.

And here the MN asks SCG to be deactivated, right?

MN asks to have SCG activated, right?

This is from Qualcomm.