3GPP TSG-RAN WG3 #113-e	R3-214187

16 – 26 Aug 2021

Agenda Item:	21.3

Source:	Huawei (moderator)

Title:	Summary of Offline Discussion on New QoS Related Parameters

Document for:	Approval

# Introduction

CB: # NRIIOT3_NewQoS

- The maximum value of survival time? For the Survival Time IE, the granularity should be 1 us (i.e. same as the Periodicity IE)? Turn WA to agreement as supporting the Survival Time for both downlink and uplink?

- The maximum value of periodicity should be extended to 60000000 us or not needed?

- E1 impact?

- TPs if agreeable

(HW - moderator)

Summary of offline disc in R3-214187

# For the Chairman’s Notes

Propose the following:

R3-20xxxa, R3-20xxxc merged

R3-20xxxc rev [in xxxg] – agreed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion – First round

On the new QoS parameters, especially the survival time, last RAN3-112-e meeting made many agreements, and left open issues as follows.

The survival time is not applicable to aperiodic deterministic traffic in Rel.17.

The Survival Time is expressed as unit of time.

The minimum value for the Survival Time is 0.

WA: Supporting the Survival Time for both downlink and uplink pending to RAN2 progress

Open issues:

- The maximum value for the Survival Time is FFS.

Possible topics below are contribution driven:

- The extension of the Periodicity

- TSN services in acknowledgement mode

TBC...

In the following, we take each related question in a separate section.

## The survival time for uplink

There is a working assumption on the survival time applicable for uplink from last RAN3-112-e meeting.

WA: Supporting the Survival Time for both downlink and uplink pending to RAN2 progress

R3-213647 proposes to agree the working assumption:

- the working assumptions can be agreed, i.e. supporting the Survival Time for both downlink and uplink.

Question: Do you agree to turn the working assumption into the agreement?

Please provide any view / comments on this topic and the question in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree And this is already supported by TS 23. 501. |
| Nokia | Agree |
| Samsung | Agree |
| Ericsson | Agree |
| ZTE | Agree |

## The granularity of the survival time

R3-213447, R3-213952 and R3-213647 propose that the granularity should be 1 us (i.e. same as the Periodicity IE).

Moderator proposal: The granularity of the survival time should be 1 us (i.e. same as the Periodicity IE)

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree. |
| Nokia | Agree |
| Samsung | Agree |
| Ericsson | Agree |
| ZTE | Agree |

## The related maximum values

### The maximum value of the periodicity

The following papers propose no need to extend the maximum value of periodicity.

- In R3-213447, the current maximum value of the Periodicity IE is 640ms, which was agreed by RAN3 based on the maximum periodicity of SPS/CG in TS 38.331. No communication service in table 5.2-1 of TS 22.104 having both long periodicity (e.g. greater than 640ms) and short PDB (e.g. few ms).

- In R3-213647, based on the above agreement made in RAN2, only the top three rows in TS 22.104 will be considered.

- In R3-213910, the Periodicity value is used for NG-RAN to decide the SPC/CG configuration and other usage of the Periodicity value has not been clarified.

While R3-213242 and R3-213952 propose to extend to 60s after checking the table 5.2-1 in 22.104.

The moderator intends to have the following proposal.

Moderator proposal: No need to increase the maximum value of the periodicity.

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree. |
| Nokia | Agree. There is no benefit for gNB to know about periodicities greater than 640ms. |
| Samsung | Agree. We don’t see the benefit yet as Nokia mentions. |
| Ericsson | Agree. |
| ZTE | Slight prefer to support all possible values of the periodicity.. Although at most 640ms periodicity can be supported in CG/SPS, the larger periodicity can be used by eNB to dynamically allocate radio resource, especially in uplink(e.g. can avoid SR and/or BSR transmission, and can reduce the packet delay). |

### The maximum value of survival time

The following values are proposed as seen from the contributions to this meeting.

- R3-213242, R3-213910 and R3-213952 propose to be 180s.

- R3-213447 proposes that it should support at least 1.92s (i.e. 3 times the maximum value of the Periodicity IE).

- R3-213647 proposes to be 6.4s or so, (i.e. 10 times of the maximum value of the Periodicity IE).

Moderator proposal: The maximum value of the survival time should be at least 3 times the maximum value of the Periodicity IE. Company can provide preference among e.g. 1.92s or 6.4s, or other values.

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree. Either 1.92s or 6.4s are ok to us. But 180s is not needed. |
| Nokia | Agree. The maximum value should be at least 1.92s (3x transfer interval), but larger value could be supported for future-proofness, e.g. on the order of seconds (but not tens of seconds which seems too much). |
| Samsung | Agree. But we also think the larger value than 1.92s would be required for future proof. We don’t have strong position on hundreds of seconds as the maximum value. |
| Ericsson | At least 3 times. Our thinking is to define it as 10 times for any future change. |
| ZTE | Agree. Based on the relationship that the ST value is three times the periodicity, we think it can be decided based on the maximal periodicity value. |

## The survival time format

In R3-213447, it proposes that the encoding of survival time can be made more futureproof (e.g. if survival time can in the future be greater than 3 times the transfer interval) if we encode as follows:

| IE/Group Name | Presence | Range | IE type and reference | Semantics description |
| --- | --- | --- | --- | --- |
| Survival Time | M |  | INTEGER (0..1, …) | Expressed in units of 1 second. |
| Fractional Part of Survival Time | O |  | INTEGER (1..999999) | Expressed in units of 1 us. If present, survival time is obtained by adding the value of this IE to the Survival Time IE. |

Question: Do you agree the above encoding of the survival time?

Please provide any view / comments on this topic below:

| Company | Comment |
| --- | --- |
| Huawei | Seems not necessary. We acknowledge the effort of the company. But if the ST is not 1s (which is the typical case), it requires two integer type IEs to be signaled. Thus one integer type IE would be sufficient. |
| Nokia (proponent) | Either encoding works, but from a specification readability perspective we prefer the above encoding particularly if RAN3 decides to support max ST >3x transfer interval (i.e. ST on the order of several seconds). |
| Samsung | Either encoding works, but we want to keep the current encoding in the BL CRs if there is no explicit benefit. |
| Ericsson | BL CR encoding is preferred. |
| ZTE | Agree with Huawei. |

## The survival time during handover

In R3-213448, it has the following proposal.

- introduce Available Survival Time within the TSC Assistance Information IE transferred over Xn and F1,

The main motivation there is that it is essential for the target gNB to know the AST, so it can determine the level of reliability that is needed when transmitting the first packet following handover.

Question: Do you think the Available Survival Time is beneficial during the handover?

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Yes. We support the principle of this proposal, and think it is necessary to ensure TSC services with ST during handover. And we think the details can be considered further e.g. applicable for downlink or uplink etc. |
| Nokia | Yes, without something like “Available Survival Time” (i.e. the remaining survival time of the total ST) passed during handover, the target gNB must always assume that it must transmit the next packet with very high reliability since it does not know if previous transmission(s) failed. |
| Samsung | Yes. Some information about the remaining survival time would be required. |
| Ericsson | No. The serving gNB can choose not to trigger the handover if it knows packet (re-)transmission is still ongoing in the cell where transmission was first initiated. |
| ZTE | Yes. For the Available ST information, we think it is necessary to distinguish between uplink service and downlink service. In the uplink, in order to avoid that UE reports complicated information to network, the UE or the source gNB may only need to notify the target gNB whether they are currently in the ST state. In the downlink, the source gNB may be able to notify the target gNB of the detailed relevant information about the current ST monitoring so that the target gNB can continue to carry out ST monitoring. In addition, we think that the details of Available ST information should wait for the relevant conclusions of RAN2. |

## TSN service in acknowledgment mode

R3-213242 proposes that there is no need for RAN3 to discuss the application of survival time under the TSN service of acknowledgment mode and provide the input to SA2.

R3-213647 has the observation that the NG-RAN node may fulfil the survival time requirements either the uplink or downlink, but cannot meet the TSN services in acknowledge mode. It provides more background information without proposal.

Moderator proposal: No RAN3 further actions are needed for the TSN service in acknowledge mode, unless further action is required by other groups.

Please provide any view / comments on this topic and the proposal in bold below:

| Company | Comment |
| --- | --- |
| Huawei | Agree |
| Nokia | Agree |
| Samsung | Agree |
| Ericsson | Agree, no further action is needed. |
| ZTE | Agree |

## Further aspects

Please add any further aspects that are in scope and were not included in the above:

| Company | Comment |
| --- | --- |

# Conclusion, Recommendations [if needed]

If needed

# References

| R3-213242 | (TP for Introduction of Enhanced IIoT support) Analysis of New QoS Related parameters (ZTE) | other |
| --- | --- | --- |
| R3-213243 | (TP for Introduction of the enhanced IIoT over E1) New QoS related parameters (ZTE) | other |
| R3-213447 | (TP for NR_IIOT_URLLC_enh BL CR for TS 38.413) Resolution of TSCAI open issues (Nokia, Nokia Shanghai Bell) | other |
| R3-213448 | (TP for NR_IIOT_URLLC_enh BL CR for TS 38.423) Impact of handover on Survival Time (Nokia, Nokia Shanghai Bell) | other |
| R3-213647 | (TP for eIIoT BLCR for 38.473) Survival time remaining issues (Huawei) | other |
| R3-213910 | (TP for NR_IIOT_URLLC_enh BL CR for TS 38.413) Discussion on the remaining issues for the Survival Time (Samsung) | discussion |
| R3-213913 | (TP for NR_IIOT_URLLC_enh BL CR for TS 38.423) The maximum value for the Survival Time (Samsung) | other |
| R3-213952 | Discussion on new QoS related parameters (CATT) | discussion |
| R3-213953 | (TP for [NR_IIOT_URLLC_enh-Core] BLCR for TS 38413) new QoS related parameters (CATT) | CR0653r, TS 38.413 v16.6.0, Rel-17, Cat. B |