3GPP TSG-RAN3 #112-e								R3-214177

Online, 17th – 27th May 2021

Agenda Item:	10.5

Source:	Ericsson (moderator)

Title:	SoD SON/MDT for NR-U

Document for:	Approval

# Introduction

CB: # SONMDT13_NRU_LB

- Topics to discuss

- Load Information from NR-U to licensed NR

- Potential load metrics

- Reporting granularity

- Failure event for NR-U, e.g. RLF report for LBT failure

- Any other topic based on contributions submitted

- Start with summary of offline

[NWM] (E/// - moderator)

# For the Chairman’s Notes

Propose the following:

R3-21xxxa, R3-21xxxc merged

R3-21xxxc rev [in xxxg] – agreed

R3-21xxxd rev [in xxxh] – agreed

R3-21xxxe rev [in xxxi] – agreed

R3-21xxxf rev [in xxxj] – endorsed

Propose to capture the following:

Agreement text…

Agreement text…

WA: carefully crafted text…

Issue 1: no consensus

Issue 2: issue is acknowledged; need to further check the impact on xxx. May be possible to address with a pure st2 change. To be continued…

# Discussion

During RAN3-113e the following agreements were taken with respect to SON/MDT for NR-U:

Following problems seem the most relevant for the SON for NR-U: load information from NR-U towards licensed NR and new failure events related to e.g. LBT or channel occupancy in the failure report.

Resource coordination between licensed NR and NR-U and optimized resource utilization in NR-U is FFS (contribution driven).

At RAN3-113e a number of topics were brought forward, some of them not in the list of topics agreed as to be considered at RAN3-112e. Here is a list of proposals.

## MLB for NR-U

In [2] and [5] proposals are made to enhance MLB for the purpose of supporting NR-U scenarios.

Both [2] and [5] propose the following:

- To report, as part of load information for cells supporting NR-U, information about the time when the cell resources of the NR-U cell were accessible, i.e. when access to such resources by means of LBT was successful

- To report existing load metrics for the amount of time when resources of the NR-U cell were accessible

- To report such load metrics on a per cell and per NR-U channel (20MHz) granularity

Companies are invited to provide their view on the addition of such load metrics to the Resource Status Reporting procedure

| Company | Comment |
| --- | --- |
| Ericsson | Reporting, with a granularity per cell and per NR-U channel, of the time the NR-U resources are accessible and of the load metrics recorded within such time is an essential step to enabling MLB to support NR-U |

Additionally, [2] also proposes to report the “Channel Occupancy measurement” as part of the load information for the cell supporting NR-U. the Channel Occupancy measurement consists of a measure of the time the resources were un-available. Namely, LBT failed when the RAN attempted access to the NR-U resources during the time indicated by the Channel Occupancy measurement.

Companies are invited to provide their view on the addition of the Channel Occupancy measurement

| Company | Comment |
| --- | --- |
| Ericsson | This is an interesting idea. We would like to understand better the usage of this information. In [2] it is said that the following 3 types of channel status times exist: The channel is free i.e. the measured RSSI by the Cell is below the threshold The channel is used by the Node or one of the served UE: during this time, the Cell or a served UE is transmitting. This can be UL or DL. The channel is used by neighbour UE or Node, ie the measured RSSI is above the threshold. However, wouldn’t it be the case that LBT is run when resources need to be used? Namely, is there a time when LBT is carried out but the RAN node does not use the NR-U resources in case of successful LBT? If such a case does not exists, then 1) and 3) above would always coincide and there would not be a need to signal the Channel Occupancy measurement. |

In addition to the above, [5] proposes to exchange between RAN nodes parameters that indicate the LBT configuration of an NR-U cell. The parameters proposed are the LBT Mode and the ED Threshold. With these parameters, the receiving node is able to understand the criteria according to which the reporting node has judged NR-U resources to be available or not available. For example, a very high ED Threshold is an indication that the reporting node is accessing NR-U resources potentially affected by high interference. Such information may influence load balancing, e.g. mobility load balancing could be done towards NR-U cells where resources are less interference polluted.

Companies are invited to provide their view on the addition of the LBT configuration parameters as part of the Resource Status Reporting

| Company | Comment |
| --- | --- |
| Ericsson | We support this proposal as it allows the receiving RAN node to have a full understanding of how the load information for the NR-U cell were generated and because it provides information of the potential quality of resources in a target NR-U cell |

## MRO for NR-U

[1], [3] and [4] focused on a new use case, namely MRO enhancements for NR-U.

Companies are invited to provide their view on whether RAN3 should work on MRO enhancements for NR-U

| Company | Comment |
| --- | --- |
| Ericsson | We support this use case. However, we see the need to involve RAN2 in order to better study what are the shortfalls of the MRO solution, if any. |

The use case discussed is the one where an HOF occurs due to persistent LBT failure. In this case it is claimed that MRO is not able to distinguish whether the HO failed due to reasons of badly configured mobility parameters or whether the HO failed because of persistent NR-U channel occupancy (LBT failure). In HOF cases, the RLF Report form the UE does not report any information about the nature of the failure, i.e. LBT.

On the contrary, the case of RLF due to LBT failure seems to be already taken into account in the current specifications, as a UE can report the lbtFailure-r16 cause as part of the RLF Report, in case of RLF.

Proposal: it is proposed to prioritise the use case of enhancements to HOF carer for MRO, to allow the RAN to identify LBT failures as the root cause of failure

Companies are invited to provide their view on the proposal above

| Company | Comment |
| --- | --- |
| Ericsson | We agree with such prioritization. However, we see the need to involve RAN2 in order to better study what are the shortfalls of the MRO solution, if any. |

# Conclusion, Recommendations [if needed]

If needed

# References

[1] R3-213224, SON for NR-U (Huawei)

[2] R3-213395, Load information enhancements for NR-U (Nokia, Nokia Shanghai Bell)

[3] R3-213505, Discussion on MRO for NR-U (CATT)

[4] R3-213722, SON enhancements for NR-U (Lenovo, Motorola Mobility)

[5] R3-213829, Further details on proposals on MLB for NR-U (Ericsson)

[6] R3-214093, Discussion on Load Balancing Optimization for NR-U (ZTE)