3GPP TSG-RAN WG3 #113-e	R3-214167

Online, 16 – 26 Aug, 2021

Agenda Item:	10.2.1.4

Source:	ZTE(moderator)

Title:	Summary of Offline Discussion on CB: # SONMDT3_UEHistoryInfor

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # SONMDT3_UEHistoryInfor - Check whether WAs from last meeting can be confirmed as agreements - Topics to discuss: - Whether only SN UHI or correlated MN and SN UHI should be sent - How to retrieve SN UHI - Which node collects SN UHI - What information is contained in SN UHI - Whether the SCG UE History Information is to be encoded directly, or as a container to be passed as an OCTET STRING - Whether to introduce one flag in SN Addition Response message to indicate whether MN should inform SN of the latest Pcell for every intra-MN PCell change - Any other topics based on contributions submitted - Start with summary of offline, proceed to TPs if there are agreements to capture (ZTE - moderator) Summary of offline disc in R3-214167

Please Note:

Two rounds of discussion.

The first round email discussion plan to be end 2 hours before 1st SON-MDT on-line session.(Friday 11:00 UTC, 2021-8-20)

Based on progress of on-line session to trigger 2nd round discussion.

# For the Chairman’s Notes

# Discussion

### Trade off between HO efficiency and signalling overhead during Node change

## At last meeting, one controversy issue discussed heavily without achieve convergence. Take procedure Inter-Master Node handover with/without Secondary Node change as example, the source MN may trigger Handover request towards target MN node without contact with SN pertain to source MN.

## Based on the inputs , 5 options on the table.

Option 1: MN initiates SN modification procedures to retrieve SN UHI before handover.

Option 2: In order to avoid handover delays, the master node is always aware of the latest PSCell UE history information.

Option 3: Use other messages to transfer UHI.

Option 4: MN saves SN UHI after SN addition procedure complete.MN not necessary to provide latest SN UHI to target gNB/MN when PScell change result is not available in MN.

Option 5: Hybrid option 1&2: For the case that the SRB3 is not allowed, RAN3 shall enable including the SCG UHI in the SN Modification Required message, so that it can be updated in the MN.

It is obviously hard to achieve agreement with so may solutions above. Therefore, Moderator would like to clarify several questions before optional decision.

One WA achieved at last meeting.

WA: RAN3 should consider solutions which would not delay HO more than it would have been delayed without UHI

Q1: Please provide your view on this WA.

Proposal 1: Confirm RAN3 should consider solutions which would not delay HO more than it would have been delayed without UHI.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | The selected solution should not delay handover. |
| Nokia | Yes | However, if SRB3 is used, the MN practically must fetch SCG config prior to a HO. Usage of SRB3 does not depend on the MN, MN has no control over it. Therefore, an MN-initiated modification prior to a HO does not delay a HO – since Rel.15 it is acceptable part of the HO procedure. |

WA: The usage of SN UHI for target NG-RAN node during handover includes:

-  SN node Ping pong issue

- assisting MN in selecting the appropriate SN (for example, in the Inter-Master Node handover with/without flow),

-  assisting MN in determining whether DC needs to be supported.

Q2: Please provide your view on this WA.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Nokia | ? | The WID does not help much in hinting the purpose of the enhancements in the scope, but to our understanding, the SCG UHI is for the SCG mobility. Other usage in the target MN is of course possible, but up to the implementation. |

Does the master node is always need to aware of the latest PSCell UE history information?

The benefits includes:

-  assistant MN for MN initialed SN change

Q3: Please provide your view on this question

Does the master node is always need to aware of the latest PSCell UE history information?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | No | 1: For inter-SN handover decision, MN can make the HO decision without specific PSCell information in the SN. 2: For intra-SN handover decision, SN can also make the decision. 3: In addition, always aware latest PSCell UHI introduce unnecessary signalling via X2/Xn interface. |
| Nokia | Not in general | The principle of MR-DC is that the MN is not aware of the PSCell. There are features imposed from outside, where the information of the PSCell changes is needed in the MN and the necessary signalling has been defined. However, it is optional and up to the feature support. |

Q4: Please provide your view on options

| Company | Option 1-5 | Comment |
| --- | --- | --- |
| ZTE | Option 4 | 1: Option 1 may delay Inter Node HO. 2: Option 2 may introduce unnecessary signalling 3: Option 3 may introduce extra impact on specification (e.g. new message) 4: Option 5 may introduce RAN2 impact (e.g enhance SRB3) which make it not apply to pre-R17 UE. |
| Nokia | Option 1 or 5 | As discussed above, option 1 does not delay a HO – using the MN-initiated modification to fetch the SCG config is a de facto part of the HO. |

### Issue 2: MCG UHI for SN

In [3] the company thinks there was no claim that MCG UHI is of any use for the SN.

Proposal In order to avoid burden related to extracting the SCG UHI from the combined UHI and impacting existing UE History Information, RAN3 shall implement signalling of SCG UHI as a separate IE in the HO procedure

While in [9] the company thinks MCG UHI is benefit for SN.

It is proposed to send the MN and SN correlated UHI from MN to SN. Besides, MN should inform SN of the PCell in case of occurrence of PCell change.

Q5: Please provide your view on this.

| Company | Do you support provide MN UHI to SN? | Comment |
| --- | --- | --- |
| ZTE | No | Don’t see the benefit of MCG UHI in SN node. |
| Nokia | No | No scenario where the SN could benefit from the MCG UHI has been acknowledged. |

### Issue 3: Cell Type of SN UHI

In [6] the company think it is necessary.

It was considered very important in the legacy information exchange. For example, the MN or SN may use the SN UHI to estimate the mobility speed. The cell type of SN may be small in FR2, be medium or large in FR1. We think the cell type is very important in this case. Also the cell is already configured with this information and to include this in SN history has a very low effort.

While in [17] the company think cell type is not apply for SN UHI.

In LTE and NR, the parameter is designed for RAN node to optimize handover decision move between micro and macro cells. While for Dual connectivity scenario, it is not necessary.

Q6: Please provide your view on this?

| Company | Do we need Cell type for SN UHI? | Comment |
| --- | --- | --- |
| ZTE | No |  |
| Nokia | No | Historically, configuring cell types was considered huge effort. No need to repeat the mistake. |

# Potential Second round Discussion

Based on result of first round discussion and on-line discussion, open issues in 2nd discussion may be discussed as following:

-Which node (MN or SN) collects UE history information of S-NG-RAN node.

-Whether SN UHI correlated with MN UHI

-Hoe does SN UHI correlated with MN UHI

-Messages for transfer of UE History Information

-SN UHI information: Time spent without SCG/Time stamps

-Stage 2/3 update

# Conclusion, Recommendations [if needed]

If needed

# References

R3-213281 Further discussion on UE History Information (UHI) in MR-DC (NEC)

R3-213307 Discussion on UE history information (China Telecommunication)

R3-213385 Discussion on 2-dimentional structure for the SCG UHI (Nokia, Nokia Shanghai Bell)

R3-213386 (TP to SON BL CR to 38.423, NR_ENDC_SON_MDT_enh-Core) Enabling SCG UHI (Nokia, Nokia Shanghai Bell)

R3-213387 (TP to SON BL CR to 36.423, NR_ENDC_SON_MDT_enh-Core) Enabling SCG UHI (Nokia, Nokia Shanghai Bell)

R3-213404 (TP for SON BLCR for 38.423) UE History Information in MR-DC (Huawei)

R3-213405 (TP for SON BLCR for 38.413) UE History Information in MR-DC (Huawei)

R3-213406 (TP for SON BLCR for 36.413 and 36.423) UE History Information in EN-DC (Huawei)

R3-213502 Enhancement of UE history information in MR-DC scenario (CATT,CMCC)

R3-213503 (TP on UE history information for 36.413) Addition of UE history information for SN (CATT,CMCC)

R3-213504 (TP on UE history information for 36.423) Addition of UE history information for SN (CATT,CMCC)

R3-213658 UE History Information in MR-DC (Qualcomm Incorporated)

R3-213812 (TP for SON BL CR for TS 38.423) UE History Information for Secondary Node (Ericsson)

R3-214010 UE History Information in MR-DC (Samsung)

R3-214011 TP for SON BLCR for 36.423: UE History Information in EN-DC (Samsung)

R3-214012 TP for SON BLCR for 38.423: UE History Information in MR-DC (Samsung)

R3-214061 UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214062 (TP for SON BL CR for TS 37.340) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214063 (TP for SON BL CR for TS 36.423) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214064 (TP for SON BL CR for TS 38.413) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214065 (TP for SON BL CR for TS 38.423) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214122 (TP to SON BLCR TS 38.413)UE history information in MR-DC (CMCC, CATT)

R3-214123 (TP to SON BLCR TS 38.423)UE history information in MR-DC (CMCC, CATT)