3GPP TSG-RAN WG3 #113-e	R3-214167

Online, 16 – 26 Aug, 2021

Agenda Item:	10.2.1.4

Source:	ZTE(moderator)

Title:	Summary of Offline Discussion on CB: # SONMDT3_UEHistoryInfor

Document for:	Approval

# Introduction

This contribution is to kick off the following discussion.

CB: # SONMDT3_UEHistoryInfor - Check whether WAs from last meeting can be confirmed as agreements - Topics to discuss: - Whether only SN UHI or correlated MN and SN UHI should be sent - How to retrieve SN UHI - Which node collects SN UHI - What information is contained in SN UHI - Whether the SCG UE History Information is to be encoded directly, or as a container to be passed as an OCTET STRING - Whether to introduce one flag in SN Addition Response message to indicate whether MN should inform SN of the latest Pcell for every intra-MN PCell change - Any other topics based on contributions submitted - Start with summary of offline, proceed to TPs if there are agreements to capture (ZTE - moderator) Summary of offline disc in R3-214167

Please Note:

Two rounds of discussion.

The first round email discussion plan to be end 2 hours before 1st SON-MDT on-line session.(Friday 11:00 UTC, 2021-8-20)

Based on progress of on-line session to trigger 2nd round discussion.

# For the Chairman’s Notes

# Discussion

### Trade off between HO efficiency and signalling overhead during Node change

## At last meeting, one controversy issue discussed heavily without achieve convergence. Take procedure Inter-Master Node handover with/without Secondary Node change as example, the source MN may trigger Handover request towards target MN node without contact with SN pertain to source MN.

## Based on the inputs , 5 options on the table.

Option 1: MN initiates SN modification procedures to retrieve SN UHI before handover.

Option 2: In order to avoid handover delays, the master node is always aware of the latest PSCell UE history information.

Option 3: Use other messages to transfer UHI.

Option 4: MN saves SN UHI after SN addition procedure complete.MN not necessary to provide latest SN UHI to target gNB/MN when PScell change result is not available in MN.

Option 5: Hybrid option 1&2: For the case that the SRB3 is not allowed, RAN3 shall enable including the SCG UHI in the SN Modification Required message, so that it can be updated in the MN.

It is obviously hard to achieve agreement with so may solutions above. Therefore, Moderator would like to clarify several questions before optional decision.

One WA achieved at last meeting.

WA: RAN3 should consider solutions which would not delay HO more than it would have been delayed without UHI

Q1: Please provide your view on this WA.

Proposal 1: Confirm RAN3 should consider solutions which would not delay HO more than it would have been delayed without UHI.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes | The selected solution should not delay handover. |
| Nokia | Yes | However, if SRB3 is used, the MN practically must fetch SCG config prior to a HO. Usage of SRB3 does not depend on the MN, MN has no control over it. Therefore, an MN-initiated modification prior to a HO does not delay a HO – since Rel.15 it is acceptable part of the HO procedure. |
| Qualcomm | Yes | In general, agree with the Proposal 1. So, either we design a solution to make sure MN always has the latest SN UHI (e.g., Option 2) or leave it up to MN as best-effort or implementation-specific (e.g., Option 1 or Option 4). Maybe it is better to check with companies if a best-effort or implementation-specific solution is OK or we need a complete standard based solution? |
| Ericsson | Yes | Fetching through SN modification procedure would delay handover in case this is not used to fetch SCG config. MN can be in charge of all SCG-related configuration in the SN (e.g. band combination, …) and in that case does not need to fetch the SCG config from the SN all the time. Full configuration can also be applied and then there is no need to fetch SCG config before HO. |
| Huawei | Yes | We believe option1 is enough because it is existing in the legacy MR-DC procedure. Also option 1 will not bring any additional delay. If further enhancement is needed, option 3 is preferred |
| Lenovo and Motorola Mobility | Yes | It is common understanding. |
| China Telecom | Yes | We agree with the proposal1 and slightly prefer to adopt option1 as the potential solution. |

WA: The usage of SN UHI for target NG-RAN node during handover includes:

-  SN node Ping pong issue

- assisting MN in selecting the appropriate SN (for example, in the Inter-Master Node handover with/without flow),

-  assisting MN in determining whether DC needs to be supported.

Q2: Please provide your view on this WA.

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | Yes |  |
| Nokia | ? | The WID does not help much in hinting the purpose of the enhancements in the scope, but to our understanding, the SCG UHI is for the SCG mobility. Other usage in the target MN is of course possible, but up to the implementation. |
| Qualcomm |  | All of the above use cases seem valid (although “flow” is not clear in 2nd bullet). Is the intention to capture this in stage-2 specs? |
| Ericsson | Yes | Can also be forwarded to the target SN to select PSCell. |
| Huawei | Yes | But we think we should not limit the usage of SN UHI. For example, the target NG-RAN also can use it to estimate the UE speed. |
| China Telecom | Yes | Agree with HW, there may be other usage of SN UHI, we should not limit it usage to the two bullet listed. |

Does the master node is always need to aware of the latest PSCell UE history information?

The benefits includes:

-  assistant MN for MN initialed SN change

Q3: Please provide your view on this question

Does the master node is always need to aware of the latest PSCell UE history information?

| Company | Yes/No | Comment |
| --- | --- | --- |
| ZTE | No | 1: For inter-SN handover decision, MN can make the HO decision without specific PSCell information in the SN. 2: For intra-SN handover decision, SN can also make the decision. 3: In addition, always aware latest PSCell UHI introduce unnecessary signalling via X2/Xn interface. |
| Nokia | Not in general | The principle of MR-DC is that the MN is not aware of the PSCell. There are features imposed from outside, where the information of the PSCell changes is needed in the MN and the necessary signalling has been defined. However, it is optional and up to the feature support. |
| Qualcomm | Not always, an optional support could be provided if deemed necessary | Depends on Q1. Not needed if a best-effort or implementation-based solution is deemed sufficient in Q1. Else, other options like MN to “subscribe” to intra-SN PSCell changes need to be considered |
| Ericsson | Yes | The latest PSCell history is needed in MN to aid selection of SN and PSCell. Also, in the case of handover or MN initiated SN change the information should be forwarded to the target nodes (MN and SN) so the up-to-date SN UHI can be used in the target SN to perform a proper selection of the PSCell. |
| HW | No | MN can always ask if he wants to have it |
| Lenovo and Motorola Mobility | No | Latest PSCell UE history information is not mandatory for making PSCell change decision. |
| China Telecom | No | SN is responsible for selecting the PScell, so it is not needed for MN always knows the latest SN UHI, however if MN need to know, it can retrieve the SN UHI through proper X2/Xn signaling. |

Q4: Please provide your view on options

| Company | Option 1-5 | Comment |
| --- | --- | --- |
| ZTE | Option 4 | 1: Option 1 may delay Inter Node HO. 2: Option 2 may introduce unnecessary signalling 3: Option 3 may introduce extra impact on specification (e.g. new message) 4: Option 5 may introduce RAN2 impact (e.g enhance SRB3) which make it not apply to pre-R17 UE. |
| Nokia | Option 1 or 5 | As discussed above, option 1 does not delay a HO – using the MN-initiated modification to fetch the SCG config is a de facto part of the HO. |
| Qualcomm | Option 1 as baseline Option 4 should be checked first. If Option 4 is not to be considered, then down selection b/w Option 2 or Option 3. | Option 1 (as Nokia pointed out) won’t cause additional delay if also used for retrieving SCG config. So, Option 1 can be supported as baseline. Option 2 would mean MN is always informed of intra-SN PSCell changes e.g., via a “subscribe/notify” mechanism, which some companies showed concern in previous meetings. Option 3 uses a new message to update SN UHI in target MN post-handover. Option 4 basically means latest SN UHI might not always be available in source MN (e.g., MN is not aware of intra-SN PSCell changes without MN involvement) in case SN modification or location information reporting procedure is not used before inter-MN handover. Needs to be checked if best-effort propagation of SN UHI is sufficient. Option 5 is not clear. Why is this related to SRB3 and UE impacts (also RAN2 almost have agreed to not enhance SRB3)? Is this option proposing to use “SN Modification Required” to update MN with latest SN UHI before inter-MN handover (isn’t this then similar as Option 1)? |
| Ericsson | Option 2 (maybe 5 depending on stage-3 details) | Option 1: May delay handover – it is not required from the specification to perform SN modification procedure before HO request, especially if full config is used. Option 2: Could be solved by allowing MN to optionally subscribe to information on PSCell changes. Option 3: Most proposals we seen so far uses other messages to retrieve the information after HO request or SN change request, meaning that the information will not be available in the target node when needed. Option 4: As option 3, the needed information will not be available in the target node in time, and the SN UHI will be outdated. Option 5: If we implement the subscription mechanism, there is no benefit to link it to SRB3 availability. It should be up to implementation to decide to trigger the subscription or not |
| Huawei | Option 1 | Option 1: It will not bring any additional delay because the MN need to initiate SN modification procedures to retrieve SN RRC context. Option 2: It need more signaling interaction Option 3: It may introduce new message Option 4: The above usages in Q2 cannot be used by the target RAN. Option 5: In R15&R16, the MN also need to send the MN initiated modification procedure to fetch the SCG configuration even if the SRB3 is not allowed (because the source SN may initiate more than one intra-SN PSCell change before the SN change. Even the source SN sends the SCG configuration to the MN during the intra-SN PSCell change, the MN will not to merge or keep the previous SCG configuration). Therefore we think the MN also can use the MN initiated modification procedure to fetch the SN UHI even if the SRB3 is not allowed. |
| Lenovo and Motorola Mobility | Option 1 | Option 1 has less spec impacts, and it would not cause handover delay. |
| China Telecom | Option 1 | We prefer to adopt option1, MN may not always store the SCG configuration, so it needs to trigger the MN-initiated SN Modification procedure (to the source SN) to retrieve the current SCG configuration, in this situation, no additional delay is introduced. |

### Issue 2: MCG UHI for SN

In [3] the company thinks there was no claim that MCG UHI is of any use for the SN.

Proposal In order to avoid burden related to extracting the SCG UHI from the combined UHI and impacting existing UE History Information, RAN3 shall implement signalling of SCG UHI as a separate IE in the HO procedure

While in [9] the company thinks MCG UHI is benefit for SN.

It is proposed to send the MN and SN correlated UHI from MN to SN. Besides, MN should inform SN of the PCell in case of occurrence of PCell change.

Q5: Please provide your view on this.

| Company | Do you support provide MN UHI to SN? | Comment |
| --- | --- | --- |
| ZTE | No | Don’t see the benefit of MCG UHI in SN node. |
| Nokia | No | No scenario where the SN could benefit from the MCG UHI has been acknowledged. |
| Qualcomm | No (to make progress) | Although we earlier preferred to have a two-dimensional and correlated list of MN and SN UHI to have easy maintenance across MN and SN, we are also OK to have an independent list for the sake of progress. We can then look to define appropriate timers e.g., “Time without PSCell” to help achieve correlation via implementation. This also means only SN UHI is propagated between MN and SN in both directions. |
| Ericsson | Yes, partly | This is two separate proposals in one. We agree to sending the MN and SN correlated UHI from MN to SN in the SN addition message. Because the target MN receives the correlated UHI from the source MN, the extraction of SN UHI has to be performed anyhow. The MN will not know what SN information that is of relevance for the SN, and therefore it is better that the SN itself extracts that information. We do not think it is needed that the MN inform the SN of the PCell in case of PCell change. |
| Huawei | Yes | As pointed in the [1], the SN can use the correlation between MN UHI and SN UHI to choose the suitable PSCell. As we know, MN change may trigger the PSCell change and also SN can trigger the PSCell change. We think the SN can use the MN UHI and SN UHI to know whether the pingpong is caused by the SN. For example, For example, the history of PCell and PSCell is changed as PCell 1+PScell 1-> PCell 2+ PSCell 2 -> PCell 1+PSCell 1. The pingpong of PSCell is caused by the PCell change, not cause by the SN. Therefore the SN knows it can still trigger the PSCell change. |
| Lenovo and Motorola Mobility | No | Agree wit ZTE. |
| China Telecom | Yes | We agree to send the correlated MN and SN UHI from MN to SN, it can optimize the PScell Change configuration (i.e. source SN to decide when/whether to trigger the SN-initiated PScell change) or the PScell selection (i.e. target SN to select the PScell when MN/SN-initiated PScell change is occurred). |

### Issue 3: Cell Type of SN UHI

In [6] the company think it is necessary.

It was considered very important in the legacy information exchange. For example, the MN or SN may use the SN UHI to estimate the mobility speed. The cell type of SN may be small in FR2, be medium or large in FR1. We think the cell type is very important in this case. Also the cell is already configured with this information and to include this in SN history has a very low effort.

While in [17] the company think cell type is not apply for SN UHI.

In LTE and NR, the parameter is designed for RAN node to optimize handover decision move between micro and macro cells. While for Dual connectivity scenario, it is not necessary.

Q6: Please provide your view on this?

| Company | Do we need Cell type for SN UHI? | Comment |
| --- | --- | --- |
| ZTE | No |  |
| Nokia | No | Historically, configuring cell types was considered huge effort. No need to repeat the mistake. |
| Qualcomm | No strong opinion |  |
| Ericsson | No strong opinion | Cell type could be useful, but we do not see this as a high priority information. |
| Huawei | Optional | This can be optional. We have used it in legacy and a cell is typically already configured with it. It would be helpful for another node to interpret the history. |
| China Telecom | No | We do not see much benefit on it. |

# Potential Second round Discussion

Based on result of first round discussion and on-line discussion, open issues in 2nd discussion may be discussed as following:

-Which node (MN or SN) collects UE history information of S-NG-RAN node.

-Whether SN UHI correlated with MN UHI

-Hoe does SN UHI correlated with MN UHI

-Messages for transfer of UE History Information

-SN UHI information: Time spent without SCG/Time stamps

-Stage 2/3 update

# Conclusion, Recommendations [if needed]

If needed

# References

R3-213281 Further discussion on UE History Information (UHI) in MR-DC (NEC)

R3-213307 Discussion on UE history information (China Telecommunication)

R3-213385 Discussion on 2-dimentional structure for the SCG UHI (Nokia, Nokia Shanghai Bell)

R3-213386 (TP to SON BL CR to 38.423, NR_ENDC_SON_MDT_enh-Core) Enabling SCG UHI (Nokia, Nokia Shanghai Bell)

R3-213387 (TP to SON BL CR to 36.423, NR_ENDC_SON_MDT_enh-Core) Enabling SCG UHI (Nokia, Nokia Shanghai Bell)

R3-213404 (TP for SON BLCR for 38.423) UE History Information in MR-DC (Huawei)

R3-213405 (TP for SON BLCR for 38.413) UE History Information in MR-DC (Huawei)

R3-213406 (TP for SON BLCR for 36.413 and 36.423) UE History Information in EN-DC (Huawei)

R3-213502 Enhancement of UE history information in MR-DC scenario (CATT,CMCC)

R3-213503 (TP on UE history information for 36.413) Addition of UE history information for SN (CATT,CMCC)

R3-213504 (TP on UE history information for 36.423) Addition of UE history information for SN (CATT,CMCC)

R3-213658 UE History Information in MR-DC (Qualcomm Incorporated)

R3-213812 (TP for SON BL CR for TS 38.423) UE History Information for Secondary Node (Ericsson)

R3-214010 UE History Information in MR-DC (Samsung)

R3-214011 TP for SON BLCR for 36.423: UE History Information in EN-DC (Samsung)

R3-214012 TP for SON BLCR for 38.423: UE History Information in MR-DC (Samsung)

R3-214061 UE History Information in MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214062 (TP for SON BL CR for TS 37.340) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214063 (TP for SON BL CR for TS 36.423) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214064 (TP for SON BL CR for TS 38.413) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214065 (TP for SON BL CR for TS 38.423) Introduce UHI of MR-DC (ZTE, Lenovo, Motorola Mobility, China Unicom)

R3-214122 (TP to SON BLCR TS 38.413)UE history information in MR-DC (CMCC, CATT)

R3-214123 (TP to SON BLCR TS 38.423)UE history information in MR-DC (CMCC, CATT)